## Slide 1
Introduction to Statics and the Concept of Force
Notes: This section introduces the units found in Statics and describes one of the very basic quantities in Statics, namely forces, and some of the important properties of forces.

## Slide 2
Learning Objectives
Quantities and Their Units
Forces
vector addition
use of Cartesian and oblique coordinates
unit vectors
solving force problems in MATLAB
Notes: We will briefly outline the various quantities that are present in a Statics course and the units that define them. The concept of force is introduced and the various ways in which we can describe forces and their behavior. The usefulness of MATLAB will be demonstrated.

## Slide 3
STATICS
Statics is concerned with the conditions under which structures are at rest (in equilibrium). The basic quantities we will deal with in Statics are
Scalar Quantities
lengths , angles (geometry)
Vector Quantities
forces, moments, position (geometry)
Matrix Quantities
Mass moments of inertia, area moments, equilibrium matrices, stiffness matrices, flexibility matrices, compatibility matrices
Notes: Statics deals with describing systems that are at rest and the effects, in that state of rest, of having external actions being impressed on those systems. The basic quantities we will deal with in Statics are geometrical quantities, forces, and moments. These quantities, as we will see, are described by the concepts of scalars and vectors so it is important to know how these concepts are defined and how they behave. Many matrix quantities are also present in Statics although traditionally Statics courses have not discussed them in that context. In this course we will use matrices extensively.

## Slide 4
Units of the Quantities considered in Statics
Length
U.S. Customary: feet (ft), inches (in.)
Metric (SI): meter (m) , centimeter (cm), millimeter (mm)
1 in. = 25.4 mm 1 m = 39.37 in. = 3.281 ft
Angle
radians, degrees
1 radian = 360/2p degrees = 57.3 degrees
Force
U.S. Customary: Pound (lb)
Metric (SI): Newton (N)
1 lb = 4.448 N , 1 N = 0.2248 lb
Moment
U.S. Customary: foot-pounds (ft-lb) or inch-pounds( in-lb)
Metric (SI): Newton-meters (N-m)
Notes: The basic quantities we deal with in Statics are lengths and angles and forces and moments. We will measure those quantities either in the U.S . Customary system or the metric (SI) system. Here are some relations between the two systems.

## Slide 5
In the SI system, the fundamental unit of mass is the kilogram. The weight (W) of a body is a force and in the SI system it is measured in Newtons.
Force = mass x acceleration
1 Newton = (1 kg)(1 m/s2)
W = mg
On the surface of the earth g =9.80665 m/s2 (usually used in engineering calculations as 9.81)
Suppose I have 454 grams of sugar. What is its weight in Newtons? In pounds?
W = (0.454 kg)(9.81) =4.454 Newtons (approximately)
= (4.454 Newtons )(.2248 lb/Newton) = 1.00 pound
Note that it is common to say that one pound of sugar “weighs” 454 grams but grams is a measure of mass and pounds is a force so we are really mixing two different units.
!
Example 1.1
Notes: In the SI system the unit of force (Newton) is a derived unit that is obtained from a measurement of mass, which is measured in kilograms. This is different from the U.S. Customary units where the unit of force (lb) is a fundamental unit, so it leads to some confusion as shown above.

## Slide 6
In the U.S. Customary system the fundamental unit of force is the pound (lb). The mass in this system is called the slug
Force = mass x acceleration
1 lb = (1 slug) (1 ft/sec2)
W = mg
On the surface of the earth g = 32. 1740 (usually used as 32.2 in engineering calculations)
Suppose I have a 100 lb sack of flour. What is its mass in slugs? In kg?
( 100 lb) = (m slugs)(32.2 ft/sec2)
m = 100/32.2 = 3.11 slugs
(100 lb) (4.448 N/lb) =4 44.8 N m = 444.8/9.807 = 45.4 kg
Example 1.2
Notes: In the U.S. customary system of units the fundamental unit of force is the pound (lb). The mass is measured in slugs where 1 slug given an acceleration of 1 ft/sec2 is equal to one pound of force. On the surface of the earth if we have the weight of a body given in pounds, we can compute its mass in slugs by dividing by the acceleration of gravity, which is 32.2 ft/sec2.

## Slide 7
Forces, Vectors
A force is a measure of the "push" or "pulling action exerted on a structure. It is a vector quantity having both a magnitude and direction.
In two-dimensions we can characterize a vector by directed arrow, having a length and two angles with respect to a set of rectangular axes
10 lb
In three-dimensions, we can also characterize a vector by a directed arrow, having a length and three angles with respect to a set of rectangular axes
x
y
z
10 lb
x
y
these are called direction cosines
Notes: Intuitively, we think of forces as a push or pull of some size acting in a given direction. Quantities such as forces having both a magnitude and direction are called vectors. Thus, we can describe a force graphically as a directed arrow where the size of the arrow indicates the magnitude of the force, and the direction of the arrow is measured by the angles it makes with respect to a set of axes. In both 2-D and 3-D cases, however, the angles with respect to the axes are not independent since the cosines of the angles (called the direction cosines) must satisfy the relations shown.

## Slide 8
Forces
Forces obey the parallelogram law of addition. The sum of two (or more) forces is called the resultant force
F1
F2
R = F1 + F2
Because the resultant and its constituent forces form an oblique triangle, we can use the law of sines and cosines to effectively solve 2-D force addition problems
a
b
c
C
A
B
Notes: Vector forces add according to the parallelogram law of addition , where in the plane containing the two forces, we form up a parallelogram with the forces as the sides. The sum of two or more forces is called the resultant force. In forming resultants in terms of its components we see an oblique triangle construct, so the law of sines and law of cosines are used frequently in force addition problems.

## Slide 9
650 N
780 N
48o
59o
x
y
For the two forces applied to a block find the resultant force and its angle from the x-axis
650 N
780 N
R
48o
59o
q
a
b
Example 1.3
Notes: Here is a problem of finding the resultant of two known forces. If we form up the oblique triangle that defines the relationship of these forces, we see we can determine the magnitude of he resultant from the law of cosines and its angle from the negative x-axis from the law of sines.

## Slide 10
There may be more than one solution
to a resultant problem
q
Find the tension T and the angle q so that we obtain a net force of 100 lb acting vertically
30o
T
55 lb
30o
q
b
55
100
T
but since
is also a solution
100
55
T=109.5
100
55
T=63.7
30o
84.6o
30o
35.4o
lb
lb
Example 1.4
solution 1
solution 2
Notes: We should realize that in a force addition problem there may be more than one possible solution as this problem shows. If we use the law of sines to calculate the angle theta, we see there are two possible solutions, either of which can be used, together with the law of cosines, to find the magnitude of the tension. These two solutions are shown graphically. The second solution is likely better since we need a smaller tension to produce the 100 lb force.

## Slide 11
When there are multiple solutions to resultant problems, we may have to reject one of the possible solutions
100 lb
F
700
q
Find the magnitude of the force F and the angle q so that the sum of the two forces shown has a magnitude of 20 lb and is directed to the left
20
100
F
70o
q
calculator solution. It is WRONG!
b
interior angles would add to > 180o
but if b = 11.41o then q must = 98.59o
Example 1.5
Notes: Even though we may have multiple solutions to a force addition problem, we may not be able to accept every solution. Here, we can find the force magnitude with the law of cosines but when we try to determine the angle theta with the law of sines, we get two solutions for the angle theta. However, if we use both solutions in the law of sines to calculate the other unknown angle, beta, we find that only one is acceptable in order to have the sum of the interior angles to be 180 degrees. Note that if you calculate the angle theta from the law of sines on your calculator (or in any computer software such as MATLAB), you will get the wrong answer since the calculator always determines a solution of an inverse sine function as the value between -90 and 90 degrees and here we must choose a value outside that range.

## Slide 12
Unit Vectors and Cartesian (Rectangular) Components
A unit vector is a vector of magnitude one
Given any vector A whose magnitude is A, a unit vector eA in the direction of A is
Unit vectors ( i , j , k ) along the Cartesian (x,y,z) axes
x
y
z
i
j
k
A
A
1
A/A
Other notations for unit vectors:
Notes: If we divide any vector by its magnitude, we get a vector of magnitude one, which is called a unit vector. Thus, any vector can be represented by its magnitude times a unit vector. Note that in writing a vector we will often write it as a bold symbol, such as A, to distinguish it from its magnitude, A, which is just a scalar (i.e., a number) . The unit vectors i, j, k along a set of Cartesian axes will, as we see, be a fundamental set of unit vectors to use in problems. Statics texts will sometimes write these unit vectors symbolically in other forms, as shown, where the ^caret over a bold symbol is used to designate it as a unit vector.

## Slide 13
Arbitrary vector in terms of its Cartesian components
x
y
z
O
P
R
S
Cartesian (rectangular) scalar components of F
Cartesian (rectangular) vector components of F
i
j
k
Notes: Any vector in three dimensions can be written as the sum of its Cartesian components. For forces, those components represent the forces acting along the three sides of the box shown. The vectors along those sides are in terms of the unit vectors i , j, k and are called the vector components and the lengths of the sides are the scalar components. In two dimensions, there are only two vector and scalar components.

## Slide 14
x
y
O
P
R
S
i
j
k
magnitude
unit vector along F
(direction of F)
Notes: We see the magnitude of a vector is just the square root of the sum of the squares of the Cartesian scalar components. The direction of a vector can be described by a unit vector along that vector and we see that unit vector also can be written in terms of the scalar components and the unit vectors i , j , k .

## Slide 15
Generally, when adding forces, it is convenient to add the Cartesian components directly rather than use the parallelogram law of addition.
Example: for 2-D vectors
F1
F2
R
F1x
F1y
F2x
F2y
Rx
Ry
Notes: Writing vectors in terms of their Cartesian components is very useful since to add vectors we can simply add their scalar components rather than having to use the parallelogram law and associated geometry relations and trigonometry.

## Slide 16
Find the resultant of these two known forces and the angle that the resultant force makes with respect to the positive x-axis
170 N
210 N
x
y
5
12
13
5
2
F1
F2
resultant:
q
Rx
Ry
R
151.7 N
30.5o
Solve this problem with
the parallelogram law
Example 1.6
(2)
(3)
(1)
Notes: Here is an example of using Cartesian components in vector addition. The steps are: (1) determine the Cartesian components of the two forces, (2) simply add them up to get the Cartesian components of the resultant, and (3) compute the magnitude and angle of the resultant from its Cartesian components. Compare this approach with using the parallelogram law. The Cartesian approach generally preferred since it can be easily applied in 3-D problems as well as 2-D problems.

## Slide 17
e1 = [ (12/13) -(5/13)]; % define unit vectors in the direction of the forces
e2 = [ -2/sqrt(29) 5/sqrt(29) ];
F1 = 210*e1; % form up forces from their unit vectors and magnitudes
F2 = 170*e2;
R = F1 + F2; % compute the resultant force
magR = norm(R) % and its magnitude, in Newtons
magR =
151.7402 % magnitude in Newtons
angR = atand(R(2)/R(1)) % determine the angle the resultant makes with % the x-axis in degrees
angR =
30.5253 % angle theta in degrees
The problem can also be done effectively in MATLAB
q = 30.5o
Rx
Ry
R = 151.7 N
Notes: Here is the MATLAB solution, which uses unit vectors.

## Slide 18
Determining the oblique components of a vector often leads to rather complex expressions. MATLAB can help to solve such problems effortlessly.
R
a
a
b
b
A
B
R
x
y
Rx
Ry
Cartesian components of R
Oblique components of R
Oblique Components
Notes: Just as we can decompose a vector into its Cartesian components, we can examine oblique components, i.e., those acting in non-orthogonal (oblique) directions, as shown. Again, we use the parallelogram law to find oblique components, but the relations often get more complex so that such problems are ideally set up to use tools such as MATLAB. On the next slide we will give an example.

## Slide 19
Example 1.7
A 250 N force is to be resolved into two oblique components A and B, acting along lines a-a and b-b, respectively . If A is 160N, determine the angle b and the component B along b-b.
70o
250 N
a
a
b
b
A
B
250 N
70o
110o
160 N
B
from the oblique triangle and the law of sines
Notes: Here, we want to resolve a force R into its oblique components along lines a-a and b-b. We know the magnitude of the force ( R = 250 N) and one of its components (A =160 N), and want to find the angle β and the unknown component B. Using the oblique triangle and the law of sines we can find the angle β . Once β is known we can again use the law of sines and find the force B. However, this is not the only solution.

## Slide 20
Now, use Cartesian components
and solve in MATLAB symbolically
250
70o
110o
A = Ax = 160
B
b
(a)
By
Bx
x
y
250
160
145
(b)
33o
160
250
254.5
73o
37o
(c)
From (a)
syms B b % b = angle beta
Eq(1) = 250*sind(b) - B*sind(70) == 0; % the two equations
Eq(2) = 160 + B*cosd(70) - 250*cosd(b) == 0;
S = solve (Eq); % solve equations symbolically, place in MATLAB structure S
double([S.B S.b]) % Convert to double precision numerical values
ans = 145.0132 33.0295
-254.4596 -73.0295
We have the two solutions
shown in (b) and (c) above
Notes: If we use Cartesian components and equate the x- and y-components, we have two equations in two unknowns. If we solve these in MATLAB we obtain the solution found before but also a second solution.