## Slide 1
Pressure Forces
Notes: Here we will examine the resultant force due to a pressure distribution acting on a surface.

## Slide 2
Learning Objectives
Center of Pressure
Archimedes Principle
Notes: These slides will demonstrate examples of calculating forces due to pressure and show how examining pressure distributions leads to Archimedes principle of buoyancy.

## Slide 3
resultants of pressure (force/unit area) distributed loads
Example: pressure in a fluid
z
p= g z
g … weight/vol of the fluid
d
p=gd
p=gd
p=gd
pressure is the same in all directions at a given depth
Notes: In a fluid the pressure increase linearly with depth. At the surface, the pressure is atmospheric pressure but this pressure, which adds a uniform term to the pressure distribution in the fluid, does not generate any net force on a submerged or partially submerged so it will be neglected. The pressure that we will use without the atmospheric terms is called the gage pressure.

## Slide 4
Archimedes Principle of Buoyancy
A floating object displaces a volume of water whose weight is equal to the weight of the floating object
Wboat
Vboat
volume of water displaced by boat
d
acting over a rectangular area A
Wboat
Notes: A floating object such as a boat has a pressure distributed over its bottom which is generally a complex shaped surface. Rather than try to do an integral of the pressure over such a complex surface, we can choose a free body diagram of a simpler-shaped portion of water and the boat where the pressure is on either straight sides or the bottom, so that we can calculate the water (pressure) forces easily. If we take a free body diagram of the boat and the water of this volume and sum forces vertically, we find that the weight of the boat is equal to the volume of water displaced by the boat (i.e., the volume of the bottom of the boat that is under water) times the weight/volume, or in other words:
the weight of the boat is equal to the weight of water displaced by the boat (Archimedes Principle of Buoyancy)

## Slide 5
Example 12.1
The width of the cylindrical gate is 4 ft. Determine the magnitude and direction of the resultant force exerted by the water pressure on the gate ( g =62.4 lb/ft3).
pressure at top of gate
pressure at bottom of gate
W = weight of water in cylindrical volume Vf
4 ft
4 ft
10 ft
4 ft
O
volume of a cylinder of height w and
radius a:
Notes: Here is a problem where a submerged gate has a curved shape. We can use the same idea as employed in Archimedes principle and choose a free body diagram of the gate and a volume of water where the calculation of the forces from the pressure distributions is much easier.

## Slide 6
2 ft
2 ft
8/3 ft
F1
W=3137 lb
F2
F3
O
a
R
+
so the line of action of R must go thru O
O
17.77 kips
47.6o
centroid of Vf = 4a/3π =
(from tables)
Notes: If we use the idea of a composite pressure distribution to break the horizontal pressure into parts, we can easily obtain the resultant force and resultant moment about point O. Since the moment is zero, the resultant must act along a line through O.

## Slide 7
Example 12.2
The width of the rectangular hinged gate
is 4 m. Determine the magnitude of the resultant force exerted on the gate by the water pressure and the center of pressure with respect to the hinge at A.
r = 1000 kgm/m3 for water.
3.5 m
60o
5 m
A
A
R
d
a
Notes: This problem asks to find the resultant force and its location on a submerged gate. If we draw the triangular pressure distribution on the gate, we can find the resultant and its location in the same fashion as done with linearly distributed loads on beams.