## Slide 1
Principle of Virtual Work for A Rigid Body
Notes: In Statics, the principle of virtual work can be used to solve equilibrium problems as we will show in these slides.

## Slide 2
Learning Objectives
Virtual Work as Equilibrium Replacement
Examples
Notes: We will see that the principle of virtual work is, in fact, a replacement for satisfying equilibrium so it can be used to solve many of the same Statics problems we have already considered. We will demonstrate this replacement with several examples.

## Slide 3
Rigid Body Displacements (in 2-D)
a general displacement of any point in a rigid body consists of a translation plus a rotation. If a 2-D translation and rotation (about the z-axis) are both small in 2-D problems then the displacement at any point in a rigid body can be written as
q
D
x
y
small
translation
small
rotation
Notes: We will limit our discussion of virtual work to 2-D problems to keep the problems relatively simple. The small displacement of a rigid body in 2-D consists of a translation and rotation. We can write this displacement in vector form with the use of a vector cross product to describe the rotation.

## Slide 4
we can also write
in matrix-vector form as
In three dimensions if we have small rotations (dqx , dqy, dqz ) of a rigid body about the x-, y-, and z-axes then have in matrix-vector form
but we will only consider 2-D problems here
or, equivalently
where
Notes: We also can write the displacement in a matrix-vector form. This matrix-vector form generalizes directly to more complex 3-D problems, as does the purely vector form with the cross product. We deal with small translations and rotations since in 3-D displacements with finite rotations the order in which we apply rotations is important so the relationships during a displacement become more complex.

## Slide 5
translation:
small rotation dq about a point P:
dD
dD
dD
dr =dD = constant for all points in the body
dr has a magnitude
of rdq
direction of dr
is perpendicular to r
dr =dqk x r
where k is a unit vector along the z-axis
x
y
r
dq
dr
dq
P
Notes: These diagrams illustrate a small translation and rotation of a rigid body in two dimensions. We can use the definition of a rigid body as a body where the change in distance between any two points in the body must remain fixed in any displacement to prove that the displacement can in fact at most be the sum of a translation and rotation, as we have assumed.

## Slide 6
if we have a series of forces, Fi , and couples , Ci ,acting on a rigid body then the virtual work, dW, done by these forces and couples, if we imagine giving a small virtual rigid body displacement to the body, is
where
is the virtual displacement of each point where the forces act,
consisting of a translation δD at P and a rigid body rotation δθ about P
F1
F2
Fi
C1
δq
δri
ri
P
δq
Cj
δD
δq
Notes: If we have forces and couples acting on a rigid body, then a small displacement will cause those forces and couples to do work. The work of the forces depends on the displacements at the points where they act while the work of the couples depends just on the rotation, which is the same for all points. We treat these displacements as virtual displacements, i.e., ones that we imagine giving to a rigid body so that its configuration is changed by a small amount from its equilibrium configuration. The corresponding work done is then also called the virtual work.

## Slide 7
Thus
but
since
so the virtual work done is
Notes: We can express the virtual work directly in terms of the work done by the forces and couples and use a vector identity to rewrite the virtual work expression as shown.

## Slide 8
If equilibrium of the rigid body is satisfied then we have
and, hence dW =0
Thus, if a rigid body is in equilibrium the virtual work done by
all the forces and moments acting on the body is zero, or in other words
equilibrium
dW = 0
Notes: In this form we see that when equilibrium is satisfied for the rigid body the virtual work done in any small virtual displacement from that equilibrium position must be zero.

## Slide 9
However, we can also turn this relationship around say that
If the virtual work done by all the forces and couples on a body is zero, for all possible virtual rigid body displacements, then the body must be in equilibrium, i.e.
equilibrium
dW =0
Principle of Virtual Work for a Rigid Body
Notes: However, if instead we satisfy the virtual work being zero for any small virtual displacements, we also will satisfy equilibrium. This means that the virtual work being zero is equivalent to equilibrium as they imply each other.

## Slide 10
To prove that dW =0 for all virtual displacements implies that equilibrium is satisfied:
If we let dDx = dD and all other components of the translation = 0 and set the rotation dq = 0 , then for zero virtual work we must have
so that we also find
in a similar fashion we can show that
If, instead we give the body a pure virtual rotation, we find
which is just the moment equilibrium equation for 2-D problems:
Notes: This slide shows that satisfying the virtual work being zero for all virtual displacements is equivalent to satisfying equilibrium, where an arbitrary virtual displacement is shown to be equivalent to satisfying force equilibrium and an arbitrary virtual rotation is equivalent to satisfying moment equilibrium.

## Slide 11
Example 13.1
Find the equilibrium angle for a platform of weight 200 lb supported by two identical weightless links. All connections are smooth pins.
equilibrium approach:
q
q
50 lb
200 lb
T1
T2
T1 =T2 =T
tanq =4
q = 76o
200 lb
50 lb
3 ft
3 ft
5 ft
q
P
A
B
Notes: To see the principle of virtual work in action, consider this platform which is supported by two weightless links (two force members) and is held in an angular position by an applied force. We want to find the angle at equilibrium. We can easily solve this problem from our three equilibrium equations which gives us the angle as well as the forces in the links (which were not asked for).

## Slide 12
virtual work approach:
note: tensions do no work in this assumed virtual
rotation
50 lb
q
du=5dq
200 lb
q
du=5dq
q
q
assume rotation of the links
5 ft
50 lb
200 lb
dq
dq
q
T1
T2
dq
A
B
50 lb
200 lb
du
du
du
in this case the platform
simply translates:
Notes: Now let’s consider a virtual work approach. If we let the links have a small angular rotation about the equilibrium position as shown, both the applied 50 lb force and the weight of the platform does work and if we compute the component of the displacements at these forces in their directions and multiply by the forces, we get the virtual work of these forces. Note that in this assumed virtual rotation of the links the platform simply translates by an amount δu, as shown. Summing up these virtual works and setting the total equal to zero gives us the angle found by equilibrium. We never had to consider the tensions in the links, as we did when using equilibrium, since they do no virtual work in the assumed rotation.

## Slide 13
we can find the tensions if we want to by looking at additional virtual
rotations or translations :
T1
T2
dq
dq
3 ft
3 ft
50 lb
200 lb
q
du=3dq
du = 3δq
q
50 lb
200 lb
T1
T2
q
q
du
du
du
same result as our previous moment equation
same result as first previous force equation
rotation
x-translation
Notes: If we did want to find the tensions in the links, we can also do that by considering other virtual displacements. For example, giving the platform a virtual rotation about its center gives us that the two tensions are equal, which is what we found with equilibrium and the moment equation. Both the known loads do not enter here as they do no virtual work in this assumed displacement. If instead we give the platform a virtual displacement to the left (an x-translation), we obtain the same equation as when we looked at equilibrium in the horizontal x-direction.

## Slide 14
same result as second previous force equation
y-translation
50 lb
200 lb
T1
T2
q
q
du
du
du
Notes: Finally, considering a virtual displacement of the platform in a vertical direction gives us the same relationship found from equilibrium of forces in the y-direction. However, note that with our first virtual work expression we obtained the angle directly without having to consider these other equilibrium equations. This is because our first choice was equivalent to equilibrium of forces in a direction normal to the tension in the links so that they did not appear.

## Slide 15
A 10-lb weight is supported by two cables AB and AC. Using virtual work, determine the tensions in the cables.
10 lb
TAB
TAC
45o
30o
10 lb
A
B
C
45o
30o
x
y
For a virtual translation in the x-direction, dx
for a virtual translation in the y-direction, dy
Notes: Here is another example where we choose virtual displacements in the x- and y-directions which gives us two equations to solve for the tensions.

## Slide 16
Example 13.2
q
k=100 lb/ft
100 lb
4 ft
4 ft
A
B
The uniform rod AB weighs 10-lb and has a 100-lb weight attached to its end. The linear spring rides in a smooth slot so it always remains vertical and is unstretched when q = 60 degrees. Determine the angle q for equilibrium using virtual work.
Note: if we have a force F acting on a body and we give the body a small virtual rotation, dq, about an origin O then the work done (2-D) is just the moment of the force about O taken through the rotation dq , i.e.
O
r = OP
F
P
Notes: Here is a rod supported by a spring and again we want to find the angle at equilibrium. We show that when we compute the work of a force during a virtual rotation that work is equal to the moment of that force about a point O times the small virtual rotation of the body about O, a fact we will use in solving problems.

## Slide 17
q
k=100 lb/ft
100 lb
4 ft
4 ft
A
B
Note: This whole system is not a system of rigid bodies because the spring is not rigid so dW =0 is not true for the whole system. We will see later how to handle deformable systems. But if we remove the spring and just look at the rigid rod then dW = 0 is valid for the rigid rod.
4 ft
D = elongation
q
60o
q
4 ft
4 ft
Ax
B
10 lb
100 lb
Fs
Ay
If we give the rod a small virtual rotation dq then the virtual work done is
moment
moment
moment
so
Notes: The whole system is not a system of rigid bodies because of the spring so the virtual work done for the whole system is not zero but if we remove the spring and consider just the rod, we do have a rigid body. If we give the rod a small rotation about A and compute the virtual work because the spring force is proportional to the elongation which is a function of the angle θ the principle of virtual work gives us an equation involving θ only.

## Slide 18
This equation has two solutions. One is cosq =0 so q = 900
100 lb
A
10 lb
The other solution is
so
This is just the configuration shown. This is not a stable equilibrium configuration.
Notes: One solution is θ = 90 degrees which is the configuration shown where the spring and rod are aligned. It can be shown that this is not a stable solution. The other solution gives the spring force as 210 lb which then means that the angle θ must be 19.9 degrees.

## Slide 19
For the beam loaded as shown, determine the reaction force at B.
Give the beam a virtual rotation about A
300 lb/ft
1000 lb
300 lb/ft
6 ft
6 ft
3 ft
3 ft
A
B
1000 lb
1800 lb
900 lb
B
Ax
Ay
3 ft
6 ft
5 ft
4 ft
Notes: Now, consider a beam supporting the loads shown and with simple supports of a pin and roller at A and B respectively. We want to find the reaction forces at B. If we give the beam a virtual rotation about A and replace the distributed forces by their statically equivalent resultants them the principle of virtual work gives us the reaction at B directly. This is equivalent to assuming moment equilibrium about A.

## Slide 20
The principle of virtual work applies also to a system of interconnected rigid bodies. One of the nice things about the use of virtual work is that normally we do not have to break the system apart and consider equal and opposite internal reaction forces as we often must do when applying equilibrium conditions directly. This is because the internal reaction forces do no work on the whole system if there are no internal deformations of the system.
Example 13.3
If all surfaces are smooth and the inextensible cable connecting A and B passes over a smooth pulley, determine the angle q needed for equilibrium of the two carts.
q
500 lb
1000 lb
A
B
15o
Notes: The principle of virtual work allows us to also deal with systems of interconnected rigid bodies like the two carts shown here which are connected by an inextensible string.

## Slide 21
Consider the virtual displacements shown
Since the cable is inextensible
q
500 lb
1000 lb
A
B
15o
Notes: Giving the system the virtual displacements shown, since the cable is rigid (inextensible) we find the equilibrium angle directly.

## Slide 22
If we had done this problem directly via the equilibrium equations, we would have broken the system into two parts and applied equilibrium:
+
+
adding these equations gives the same equation obtained by virtual work but there the tension, T, never appeared since it does no work on the system as a whole (see displacements above).
q
500 lb
1000 lb
A
B
15o
T
T
x
x
Notes: If we had done this problem with equilibrium, we would have broken the system up into two parts and then combined the results, giving us the same solution. But with the principle of virtual work, we can consider the entire system.

## Slide 23
Note, however, if we chose virtual displacements that violated the inextensibility of the cable then the tension T will do work and we could use the principle of virtual work to find that tension.
Suppose we had found q as before. Then if we choose
q
500 lb
1000 lb
A
B
15o
T
T
x
x
the virtual work would be
giving
Notes: If we had wanted to also find the tension in the cable, we could also do that with virtual work but then we would have to break the system up and choose virtual displacements that violated the inextensibility of the cable so the tension, T, does work.

## Slide 24
In general, by breaking a system of rigid bodies up such that an internal force does virtual work in a rigid body displacement, as in the previous example, we can solve for that internal force.
Example 13.4
A system of beams is loaded and supported as shown. Determine the reaction force at B acting on BC.
Choose the virtual displacements as shown. Note that by giving BC a displacement ds there is also a displacement up at D, ds/2, and a clockwise rotation of BC about C, dq=ds/3 so the virtual work is
giving
1500 N
750 N-m
1.5 m
1.5 m
1.5 m
A
B
C
1.5 m
A
750 N-m
1.5 m
1.5 m
By
C
By
D
D
Notes: We can use the same idea for finding the tension of the cable in the carts problem to find the internal forces in other systems of connected rigid bodies by assuming virtual displacements or rotations that violate those connection constraints so that the internal constraint forces or moments do work. Here we see we can find the internal force at B acting on beam BC by allowing beam AB to have zero displacement at B while beam BC does a rotation about C, which obviously violates the constraint of the roller at B which requires that the beams have the same displacement at B. However, with this virtual displacement we can find the force at B from virtual work.

## Slide 25
Example 13.5
A uniform 100 lb bar is held by a spring in the position shown. The unstretched length of the spring is 5 ft. Determine the spring constant k.
Fs = kd = k(1)
stretch = 1 ft
A
B
6 ft
8 ft
100 lb
A
B
100 lb
Fs
xs
yW
q
5 ft
5 ft
Notes: Here is a bar held by a spring against the wall. If we again remove the spring, we have a rigid body, so the virtual work done on that rigid body at equilibrium is zero. We can write the displacements at all the forces including the spring in terms of the angle θ so when we apply the principle of virtual work, we can solve for the spring constant.

## Slide 26
Virtual Work for Rigid Bodies
Airplanes
Spacecraft
Buildings
Autos
Roads
Bridges
Power Plants
Ships
Virtual Work for
Deformable Bodies
(using Finite Elements)
Notes: The principle of virtual work for rigid bodies gives us an alternate way to satisfy equilibrium. But this principle has a much more significant role when extended to the statics of deformable bodies. The structures considered can be complex when the principle of virtual work for deformable bodies is combined with the method of finite elements, which currently is the method of choice for doing engineering statics analyses. The finite element method also has a very wide range of applications in areas other than statics. Thus, there are many applications “hidden beneath the surface” that we do not consider in a statics class.