## Slide 1
Principle of Virtual Work for a Deformable Body
Notes: We have applied virtual work ideas to rigid bodies. Now we want to apply them to deformable bodies.

## Slide 2
Learning Objectives
Virtual Work as a Replacement for Equilibrium
Examples
Notes: Again we will see that the principle of virtual work for deformable bodies can be used as a replacement for equilibrium.

## Slide 3
For a rigid body, that body can only translate and rotate. For a deformable body, however, the shape and dimensions of the body can change. If we choose virtual displacements that are not just rigid body displacements, then the virtual work done will not be zero.
Example:
Consider a spring of unstretched length L:
L
F
If we apply a small elongation, dx, to the spring, the force F will do work
dx
dW = Fdx
This work is not zero since by stretching the spring we increase its internal energy, V, (also called the strain energy or the potential energy of the spring).
For a linear spring, we have F= kx, where k is the spring constant and x is the total stretch of the spring
Notes: Deformable bodies such as spring can do work when we give them real or virtual displacements.

## Slide 4
Thus, the total work , W, in going from the unstretched length to a final length xf is
The quantity on the right side of this equation is just the total strain energy or potential, V, of the spring, so we have
W = V
(total work done by the force on the spring is equal to the strain energy of the spring)
By differentiating this relationship, we also have
dW = dV
( Fdx = kx dx)
Notes: The work done by external force on the spring is not zero because it is equal to the potential energy V stored in the spring.

## Slide 5
If we choose small virtual displacements that allow deformations of the body to
occur, then the virtual work done by the forces and couples acting on the body will not be zero but will be equal to the virtual change in the strain energy of the body, i.e.
dW = dV
As in the case of rigid bodies, for deformable bodies we can show that if we satisfy the above relationship for "all" possible small virtual displacements, then equilibrium of the deformable body will be satisfied, or in other words:
dW = dV equilibrium
Principle of Virtual Work for Deformable Bodies
The reason this is important is that we can use this principle to solve both statically determinate and indeterminate problems. Note that if equilibrium is satisfied, we also have the principle of virtual work satisfied here, as found for rigid bodies:
equilibrium
dW = dV
Notes: For deformable bodies, the virtual work done is equal to the small virtual change of the potential energy of the system. This principle can again be used to replace equilibrium, but it is even more powerful since it also can be used to solve statically indeterminate systems that cannot be solved by equilibrium alone.

## Slide 6
q
k=100 lb/ft
100 lb
4 ft
4 ft
A
B
Consider now this problem by including the spring in the system directly. Then dW = dV is valid for the entire system. (compare to the rigid body solution)
q
4 ft
4 ft
Ax
B
10 lb
100 lb
Fs
Ay
4 ft
D = elongation
q
60
Example 14.2
The uniform rod AB weighs 10-lb and has a 100-lb weight attached to its end. The linear spring rides in a smooth slot so it always remains vertical and is unstretched when q = 60 degrees. Determine the angle q for equilibrium using virtual work.
elongation of spring
C
C
Notes: Let's consider the rod and spring problem we examined previously using the principle of virtual work for a rigid body. Now examine the entire system, where we include the spring. We know the potential energy of the spring in terms of its elongation so we can write it in terms of the angle θ and compute its virtual change with a small change of that angle.

## Slide 7
4Fs
but here we assumed the Fs in the free body diagram does no work. Why?
Putting all the terms on the left, we have the same result as before, where we have
identified the Fs term from before
If we give the rod a small virtual rotation dq then
moment
moment
Now, consider this expression
(1)
As before, the solution of (1) is either q = 90o, which is an unstable solution or q = 19.9o
Notes: We can then set the virtual work done by all the forces on the free body diagram to be equal to this change in potential energy. We end up with the same equation as before for the angle θ where if we compare it to our previous equation, we can identify the term that was the spring force. However, here the spring does no work on the entire system since the only place the spring force appears acting on that system is at the upper support C which can only move horizontally.

## Slide 8
Example 14.3
A uniform 100 lb bar is held by a spring in the position shown. The unstretched length of the spring is 5 ft. Find the spring constant k.
A
B
100 lb
Fs
xs
yW
q
5 ft
The spring force at the wall does not move so the reaction there, Fs ,does no work. But now there is an increase in V of the spring for the entire system so either a rigid body or a deformable body approach gives the same answer
A
B
6 ft
8 ft
100 lb
same as before
consider the entire system (compare with the rigid body solution)
5 ft
Notes: Here is the problem of a bar held by a spring which we also treated previously with the principle of virtual work for a rigid body. In this case we look at a free body diagram of the entire system and use the principle of virtual work for the deformable system to obtain the spring constant k.