## Slide 1
Moments about a Line
Notes: In addition to calculating moments of a force about a point we can compute moments of a force about a line.

## Slide 2
Learning Objectives
Moment of a Force About a Line
Notes: We will define the moment about a line and give some of its properties and uses.

## Slide 3
Moment of a Force About a Line
F
r
e
P
plane containing r, F
moment of the force
about point P
A
B
Suppose we have a force F and a line AB and we take the moment of the force about a point P that lies on that line
Then the moment of F about the line AB, MAB , is defined to be the rectangular component of the moment about point P along that line AB, i.e.
P
A
B
eAB
unit vector along AB
scalar component
vector component
Notes: If we take moments of a force about a point on a given line and then compute the Cartesian component of that moment in the direction of the line, we get the moment about the line. As shown, we can define either a scalar component or a vector component. Physically, the moment about a line gives us that part of the total moment that causes a turning about that line.

## Slide 4
One efficient way to calculate the scalar moment about a line is to write it as a 3x3 determinant.
Let
Then
unit vector along AB
position vector from a point on AB to the force F
Notes: To compute the moment about a line we can do this as a vector cross product followed by a dot product. This gives many terms so one easy way to get the scalar moment is to define it as a 3x3 determinant and then just expand that determinant.

## Slide 5
A force F = 4 k lbs acts at a point Q. Determine the moment of this force about line OP. All distances are in ft.
x
y
z
O
F = 4k
P = (3,3,3)
Q=
(2,3,0)
since O is on the line can take moments about O
r = 2i + 3j + 0k
Need the unit vector along OP:
Example 2.5
Notes: Here is a problem about computing moments about lines in three dimensions. First, we use the determinant expression and a unit vector along the line to get the vector moment about line OP.

## Slide 6
r = [2 3 0];
F = [ 0 0 4];
OP = [ 3 3 3];
e = OP/norm(OP);
MOP = cross(r, F)*e'
MOP =
2.3094
divide vector by its magnitude to get
a unit vector along the line
note the use of the transpose of e !!
(we could also use the dot function)
in MATLAB
MV = MOP*e
MV =
1.3333 1.3333 1.3333
scalar component
vector component
Notes: Here is the same problem in MATLAB.

## Slide 7
Another Way to Define the Moment of a Force about a Line
A
B
Plane perpendicular to AB and containing r, Fpl
F
FAB
Fpl
r
P
component of F along AB
component of F in the plane
eAB
dpl
distance from P to Fpl along a direction
perpendicular to Fpl in the plane
unit vector perpendicular to both r, Fpl, direction determined by right hand rule
but in either case
so
we can let
Notes: As shown on this slide, another way to define the moment about a line is to take the component of the force in a plane perpendicular to the line times the perpendicular distance from the line to the force component in that same plane. We get the direction by the right-hand rule.

## Slide 8
Relationship Between Moments about a Point and Moments about a Line
so we have
or in other words the moment of a force about a point P is just the sum of the moments of the force about three orthogonal lines (i.e., the x, y, and z-axes) taken through P
moment about a point
moment about the x-axis
moment about the y-axis
moment about the z-axis
Notes: There is an explicit relationship between moments about points and lines. As shown here the moment of a force about a point can be thought to be the sum of the moments about three orthogonal lines (in the x-, y-, and z-directions) taken through that point.

## Slide 9
x
z
y
We can use this relationship and the expression of the moment of a force about a line in the form
to easily calculate the moment of a force about a point in terms of its
rectangular components
Fx
Fy
Fz
P
rx
ry
rz
r
moment about x-axis
moment about y-axis
moment about z-axis
Notes: We can use the relationship between moments about points and lines and the expression for a moment about a line in terms of a component in a plane perpendicular to a line and the perpendicular distance in that plane to derive the expression obtained earlier for the moment about a point components. For example, the moment about point P in the x-direction is the sum of the moments of the forces Fy and Fz in the y-z plane times their perpendicular distances rz and ry from the x-axis, respectively, using the right-hand rule to get the correct signs.

## Slide 10
Determine the moment of the 510 lb force (the direction of the force is along line AD) with respect to: (a) line CB, (b) point B. All distances are in inches.
5 in
9 in
12 in
8 in
510 lb
A
B
C
D
x
y
z
Example 2.6
First, get the force vector
Notes: Here is a problem where we ask for both moments about points and lines. First, we get the vector expression for the force.

## Slide 11
270 lb
240 lb
360 lb
B
C
14 in
(a)
x
y
z
(b)
only the 360 lb component gives
a moment about CB. Why?
moments about the x-, y-, z- axes
through point B are moments about
those lines. They are also the x-, y-,
and z-components of the moment
about point B
Notes: (a) We can get the moment about line CB by using its definition in terms of the force in a plane perpendicular to a line and the perpendicular distance in that plane to the force. (b) We can consider the moment about point B to be the sum of the moments about the x-, y- , and z- axes through that point.

## Slide 12
Here are all the same steps in MATLAB
AD = [ -12 8 9]; % vector AD
eAD = AD/norm(AD); % unit vector along AD
F = 510*eAD % the force vector
F = -360 240 270
rBA = [ 0 0 14]; % position vector from B to the force at A
eBC = [ 0 1 0]; % unit vector along BC
MBC = cross(rBA, F)*eBC.' % scalar moment of the force about line BC
MBC = -5040
MVBC = MBC*eBC % vector moment of the force about line BC
MVBC = 0 -5040 0
MB = cross(rBA, F) % moment about point B
MB = -3360 -5040 0
Notes: Here are the equivalent calculations in MATLAB