## Slide 1
Equivalent Systems (2-D)
Notes: These slides will examine equivalent force-couple systems for coplanar (2-D) systems

## Slide 2
Learning Objectives
Equivalent Systems and Resultants
2-D Examples
Notes: We will define equivalent systems and resultants and demonstrate how to obtain resultants in 2-D systems.

## Slide 3
Equivalent Force-Couple Systems and Resultants
Definition: Two sets of forces and couples are said to be statically equivalent if they produce the same total force and moment with respect to any point.
The resultant of a set of forces and couples is said to be the simplest system that is statically equivalent to the original set.
Given any set of forces and couples, we can always reduce the system to an equivalent single force, R, and single couple, M, if we set
F1
F2
FN
r1
r2
rN
C1
CM
=
R
M
O
O
Notes: A pair of systems of forces and couples are said to be equivalent if they produce the same net force and moment. Obviously, any system can always be reduced to a single force R and a single couple M at any point.

## Slide 4
R
M
For general force and couple systems a single force and couple in the form of a wrench (which we will discuss later) is the simplest equivalent system. However, in some special cases we can reduce the system to a single resultant force.
We can do this if we can place R at some location, r, where
R
O
r
=
O
Notes: Here, we want to examine when we can further replace the force R and couple M by a single resultant force R, acting at some location.

## Slide 5
The equation
has a solution only if R and M are
perpendicular to each other since
so that if the equation is satisfied, we must have
also
One important force-couple systems where R and M are perpendicular are:
Planar (2-D) force-couple systems
x
y
=
R
M
=
R
resultant
line of action
Notes: We can find such a single force resultant only if R and M are perpendicular to each other. In coplanar (2-D) force-couple systems, this is always the case. Note that the resultant single force can be located anywhere along its line of action.

## Slide 6
Determine the resultant of this coplanar force system and locate it with respect to point O. The
400 lb force is tangent to the circle.
Vector method
To locate R we must solve:
if we choose y = 0, x = -3.48 ft
O
7
24
25
212 lb
600 lb
400 lb
x
y
=
x
y
R
r
4 ft
3.48 ft
O
7
24
7
24
O
4 ft
or, equivalently
+
Example 3.1
Notes: Here is a planar force system for which we want to determine the resultant. In a vector approach we form the resultant force and moment and solve r x R = M by choosing a location along the x-axis.

## Slide 7
scalar method
+
to locate R:
1.5
1
389 lb
O
1.93 ft
O
7
24
25
212 lb
600 lb
400 lb
x
4 ft
Notes: In a scalar approach we compute the magnitude of the resultant and the moment and use those values to determine the perpendicular distance to the line of action of the resultant force.

## Slide 8
MATLAB method
F1 = [ 212 0 0];
F2 = [ 0 -600 0];
F3 = [ 400*7/25 400*24/25 0];
R = F1 + F2 + F3
R = 324 -216 0
r1 = [ 0 4 0];
r3 = [ 4*24/25 -4*7/25 0];
M = cross(r1, F1) + cross(r3,F3)
M = 0 0 752
define vector forces and
sum to get resultant
define position vectors ( r2 = 0)
compute the net moment
As seen in the vector solution determining the location of the resultant by hand is not difficult but since we are doing this in MATLAB it would be also nice to solve rxR = M directly
Notes: Now, lets examine this problem in MATLAB. We define all the forces and their position vectors and then simply sum up the forces and moments.

## Slide 9
We can obtain a symbolic solution by using the MATLAB solve function to find a location of the resultant either along the x-axis or y-axis:
same result as before for distance along the x-axis
we can also find the location along the y-axis
syms x y
r1 =[x 0 0]; % let position vector be along x-axis
xn = double(solve(cross(r1,R) - M))
xn = -3.4815
r2 = [ 0 y 0]; % let position vector be along the y-axis
yn = double(solve(cross(r2,R) - M))
yn = -2.3210
Notes: We then use the MATLAB function solve to locate the resultant either along the x- or y-axis

## Slide 10
Replace the coplanar force system with a single resultant force and locate the force with respect to point A. All distances are in mm.
scalar method
480 cos30 = 415.69 N
480 sin30 = 240 N
800 cos45 = 565.69 N
800 sin45 = 565.69 N
320 mm
320 mm
120 mm
240 mm
A
R =
1034 N
18.36o
resultant force
800 N
480 N
320 mm
320 mm
120 mm
120 mm
45o
30o
A
x
y
Notes: Here is another coplanar force system where we want to find the resultant. First, we will use a scalar approach where we only deal with the components.

## Slide 11
415.69 N
240 N
565.69 N
565.69 N
320 mm
320 mm
120 mm
240 mm
A
+
A
R = 1034 N
d
18.36o
resultant moment
perpendicular distance
Notes: We calculate the net moment also from the components of the forces and their perpendicular distances from A and then calculate the perpendicular distance, d

## Slide 12
vector solution
A
r
(x, y)
x
y
if x = 0 then y = 142.89 mm
A
R = 1034 N
18.360
142.89 mm
d
18.360
d = (142.89)cos18.36 = 135.6 mm
Notes: Here is a vector solution using the cross product. We see it agrees with the scalar solution.

## Slide 13
480 cos30=415.69
480 sin30 =240
800 cos45=565.69
800 sin45=565.69
320
320
120
240
A
Here is the MATLAB solution
same solution as before along the y-axis
here is the resultant location on the x-axis
F1 = [ 800*sind(45) 800*cosd(45) 0];
F2 = [ 480*cosd(30) -480*sind(30) 0];
R = F1 + F2;
r1 = [320 120 0];
r2 = [640 240, 0];
M = cross(r1, F1) + cross(r2,F2);
syms x y
rx = [x 0 0];
xn = double(solve(cross(rx,R)-M))
xn = -430.5659
ry= [ 0 y 0];
yn = double(solve(cross(ry,R) - M))
yn = 142.8900
Notes: The MATLAB solution is also straightforward.