## Slide 1
Introduction to the Finite Element Method
Notes: Here is a brief introduction to the finite element method

## Slide 2
Learning Objectives
Stiffness-Based Finite Elements
The Stiffness Matrix
Applying Boundary Conditions
Solution
Post-Processing
Force-Based Finite Elements
Notes: The finite element formulation in common use today is the stiffness-based finite element method. We will examine all the elements of this method for simple problems. We will define what we mean by a stiffness matrix and how it is used to solve statically indeterminate deformable body problems. We will show how we apply either force or displacement boundary conditions and solve for the displacements of the deformable body with the stiffness matrix. After that solution we will see how to obtain the internal forces in the deformable body as part of the post-processing phase. We will also discuss an alternative approach where we solve for the internal forces directly from an equilibrium matrix used in conjunction with a compatibility matrix that involves the deformations. This is called a force-based finite element method. After those forces are found we will see how to obtain the displacements of the deformable body in the post processing phase..

## Slide 3
V
N
M
100 lb
25 lb
15 lb/ft
A
A
A
A
We have examined structures such as the frame shown here where we break the structure apart at the pins and solve for the unknown forces, as shown in red below (assuming, of course, we also knew all the appropriate dimensions).
However, we also have internal
forces/moments acting throughout
all the parts
100 lb
25 lb
15 lb/ft
This is a statically determinate structure so we can solve for any of these forces or moments throughout the structure
Notes: In Statics we solve problems like this frame where we break the system into parts and solve for all the forces at the connections. Once we have all these internal and external forces at the connections, we can solve for the internal forces and moments (as shown in green) anywhere in the frame.

## Slide 4
25 lb
100 lb
15 lb/ft
However, what if we assume this structure is deformable and break this structure up into very small elements and use information on both equilibrium and the deformations of these elements? In that case we can solve for all of the internal forces and reactions (and the deformations).
This is the basic approach of the finite element method.
There is no reason, however, that the structures we consider need to be this simple.
100 lb
25 lb
15 lb/ft
By changing the supports this problem is statically indeterminate so if we treat all the elements as rigid bodies we cannot solve this problem for all the forces, either external or internal by equilibrium alone.
V2
M2
N2
M1
V1
N1
a finite element
Notes: If we change the support conditions this problem is statically indeterminate, and we can solve for some but not all the forces at the connections and we therefore cannot solve for the internal forces and moments anywhere in the frame. However, if we break the entire frame into small elements and relate these internal forces and moments to the deformations of the frame, we can use this information to solve for all these internal forces and moments and for the forces at the connections. The finite element method uses this approach to solve this and much more complex problems.

## Slide 5
Here we want to provide a gentle introduction to the basic elements of the finite element method (pun intended).
We are going to ultimately develop a finite element program for the forces and deformations of a general system of interconnected linear springs , where we want to solve for the displacements at the ends of each spring and the forces that produce these displacements. To begin, let’s consider a very simple case where all the springs are identical, attached in series and fixed at the ends, and where a load P acts at one of the nodes between springs:
P
fixed
fixed
The elements here will be the individual springs. Note that this system is statically indeterminate (why?) so we cannot find the forces in the springs by equilibrium alone even though it is very simple.
Notes: To illustrate the finite element method, we are going to use a very simple problem so that we show the steps in the method with as few complications as possible. Specifically, we are going to look at a series of springs that are connected in series where one or more applied forces are applied at the spring connections and the ends of the spring system are fixed. This is a statically indeterminate problem since there are two unknown reaction forces at the fixed supports but only one equation of equilibrium. We will also let all the spring constants be the same. Although finite elements often uses virtual work ideas, here we will rely on only equilibrium and force-deformation ideas to discuss the method.

## Slide 6
Consider first a single spring:
node i
node j
km
mth element
forces
on mth element
displacements
or, in matrix form
element stiffness matrix, Km
these end forces are related to
the displacements through
the spring stiffness, km
internal force in the spring
… deformation (elongation)
in the spring
relation between
and
i
j
Notes: In this example the elements will be the springs themselves. If we look at a single element we can relate the internal force in the spring to the elongation of the spring in terms of the displacements at the ends of the spring, which we will call nodes. We can relate this internal force to the forces at the nodes and hence write a relationship between these end forces and the displacements in terms of a stiffness matrix for the element that contains the spring constant.

## Slide 7
note that equilibrium of the spring is satisfied since
or, equivalently
We now want to place the elements (springs) into a large stiffness matrix for all the springs.
To do this, let’s consider having six springs (and hence seven nodes) where the nodes are all numbered consecutively from 1 to 7 and P =100 lb is applied to the fourth node. The spring constant k = 400 lb/in for all the springs.
1
2
3
4
5
6
7
100 lb
(1)
(2)
(3)
(4)
(5)
(6)
node numbers
element numbers
Notes: The forces at the nodes will automatically be in equilibrium. Now we want to label the elements and the nodes which we will do here simply in a consecutive manner. Later, we will examine how to make these choices arbitrary. In this case we will have an applied force at node 4 and nodes 1 and 7 will have zero displacements. These are called the force and displacement boundary conditions

## Slide 8
Since there are seven nodes the “global” stiffness matrix for all the springs will be a 7x7 matrix. If we place the first element stiffness matrix into that initially empty global matrix we will have
If we add the second element stiffness matrix, we find
Notes: Since there are seven nodes and hence seven displacements the global stiffness matrix for the entire system will be a 7x7 matrix. If we initially place all zeros in this global matrix and start adding in contributions from the element stiffness matrices, we can fill this global matrix. On the right side of this matrix will be a column vector containing one or more forces at the nodes.

## Slide 9
and if we add in similarly all the other elements we have, finally
Note that at any node j that shares a pair of forces, if there is an applied force F at that node we have
so that the sum of the end forces is zero at each node unless a force is applied there, in which case the sum is just that applied force. At the start and end nodes, the end forces there are just unknown reaction forces R1 and R2 at those fixed supports where the displacements are assumed to be zero:
j
R1
R2
1
2
3
4
5
6
7
100 lb
(1)
(2)
(3)
(4)
(5)
(6)
Notes: This shows the global stiffness matrix when it is all filled in. As we see it is a matrix with most of its non-zero values near the diagonal. Such sparse matrices are typical of the finite element method. At the inner nodes, the sum of the end forces will vanish unless we have an applied force at that node, and at a fixed end the end force will just be the unknown reaction force at that node.

## Slide 10
so we have
We want to solve for the nodal displacements. Once we know those displacements, we can find the forces in the springs. But to do this we must first apply the known boundary conditions on the displacements U1 = U7 =0 . We can do this by eliminating the first and seventh rows and columns in the above matrix and the first and seventh components of {Ug} and {Pg} , giving
which we can write in matrix-vector form as
where [K] is a stiffness matrix for the reduced system, {Uf} is a vector of all the unknown “free” nodal displacements, and {P} is a vector of all the known applied forces.
which we can write in matrix-vector form
as
in terms of a global stiffness matrix, and global vectors of displacements and loads
Notes: By replacing all the sums of forces at the inner nodes with either zero or the known forces we have satisfied the force boundary conditions. However, we also need to satisfy the end displacement conditions U1 = U7 = 0. This is where we bring in displacement information that allows us to solve the problem. One way to satisfy these conditions is to simply delete all the rows and columns in the global stiffness matrix and the corresponding rows in the force vector on the right-hand side. This leads to a reduced stiffness matrix and vector of nodal forces that we can now solve for the “free” nodal displacements.

## Slide 11
Now, lets solve this system in Matlab. It is easy to generate this K matrix with the MATLAB diag function (later we will show how to assemble this matrix in MATLAB from the element stiffnesses). We place all the elements of the main diagonal in a vector D, and the elements above the main diagonal in the vector U and the elements below the main diagonal in the vector L and then use the diag function:
k=400;
U = -k*ones(1,4);
L = -k*ones(1,4);
D = 2*k*ones(1,5);
K = diag(D,0) + diag(U,1) +diag(L,-1)
K =
800 -400 0 0 0
-400 800 -400 0 0
0 -400 800 -400 0
0 0 -400 800 -400
0 0 0 -400 800
Notes: To solve this problem in MATLAB we will first assemble the reduced stiffness matrix directly. Later, we will show how this is done element-by-element when we describe a specific finite element program.

## Slide 12
Now, generate the known forces vector and solve for the free displacements.
P = [0;0;100;0;0];
Uf =K\P
Uf =
0.1250
0.2500
0.3750
0.2500
0.1250
Ug = [0;Uf;0]
n= 1:7;
plot(n,Ug)
xlabel('node')
ylabel('U, in.')
add in the zero end
displacements and plot
{P}
solution for {Uf}
Notes: Similarly, we will form up the force vector and then solve this system of linear equations with the MATLAB “backslash operator” , \ , for the free displacements. If we put the zero end displacements back into a global displacement vector we can then plot all the displacements.

## Slide 13
If we want to obtain the internal forces, we need to define the end and beginning nodal displacements for each element. The difference of these displacements is then the deformation (stretch) of the element and the force is just the stiffness times the stretch. As shown in the plots, the first three elements are in tension and the last three are in compression and there is a jump down of 100 lb at the load P. These calculations and plots are what in the finite element literature is called post-processing.
Ue = Ug(2:end);
Ub = Ug(1:end-1);
F = k*(Ue - Ub)
F =
50.0000
50.0000
50.0000
-50.0000
-50.0000
-50.0000
m = 1:6;
plot(m, F, 'bo')
xlabel(' element number m')
ylabel(' F, lb')
element number m
F, lb
end displacements
beginning displacements
internal forces (all k’s the same)
Notes: We know the the internal forces in the springs are just the spring constant times the difference of displacements at the ends of the spring so if we extract the start and end displacements from the global displacements for each element, multiplying by the spring constants then gives use the internal spring forces for each element, which are then plotted here.

## Slide 14
We have obtained a solution for our simple springs problem. We will shortly generate a Matlab finite element program that will allow us to handle a more complex system of springs such as:
P
fixed (displacement = 0)
F
fixed (displacement = 0)
(1)
(2)
(3)
(4)
(5)
(6)
1
2
3
4
5
Here all the movable supports (shown in red) will be assumed to ride in smooth guides that keep them vertical so that we only need to examine the forces in the horizontal direction
We will want to have the flexibility of labeling the elements and node numbers in any way we want. We will do this through a connectivity matrix which contains the appropriate node numbers for each element. For example
3
5
2
5
3 4
3 4
element
(1)
(2)
(3)
(4)
(5)
(6)
node numbers
connectivity matrix
Notes: Later, we will consider a more complex system of springs where we will show how to handle issues that were ignored or simplified in our example. In a more complex system, we will want to be able to give the elements and nodes any order or value that we want. This will be done through a connectivity matrix which contains the chosen start and end nodes for each element.

## Slide 15
We also want to change how we satisfy the boundary conditions, i.e., how we specified either the known displacements or forces at the appropriate nodes. We handled this previously by replacing the global stiffness matrix with a reduced matrix, but we want to instead simply modify the equations involving the global stiffness matrix appropriately, as this is how it is often done in practice for efficiency and so we do not lose the ordering of the displacements. From our previous problem, for example, we had
and we wanted to satisfy the displacement boundary conditions U1 =U7 =0 and the force boundary condition with all the other sums of forces at the inner nodes = 0.
Let us now define the procedure. We will use our previous problem to illustrate the details.
Note that the numbering we choose for the nodes will also affect how we assemble the
element stiffness matrices into the global stiffness matrix. We will describe the assembly process in detail later
or
Notes: The connectivity matrix will also allow us to place the element stiffness matrix elements in their appropriate places in the global stiffness matrix. Another change we want to make is how we satisfy the boundary conditions. Before, we changed the global matrix and force vectors by eliminating rows and columns in their global forms to solve for a different, reduced form. Here, we will instead keep those global forms and simply modify them so that we can then do the solution directly.

## Slide 16
1. initialize the right hand side force vector to zero:
2. If a force is specified at a node, place it in the appropriate nodal force location. In our example
Notes: Satisfying the force boundary conditions is easy since we just start with a zero vector and add in the known forces at the nodes where they are applied.

## Slide 17
3. If a displacement is specified as zero at the nth node, leave the right hand side force value as zero and replace the Knn term in the stiffness matrix by a large value N. For our previous example, choosing N = 109k we would have
The first and last equations are then simply U1 = U7 = 0 to a very good approximation.
Note that the reaction forces are missing at nodes 1 and 7 since we are modifying the first and seventh equations to satisfy the displacement boundary conditions at where those reactions act.
Notes: Satisfying displacement boundary conditions is a little more complex. Here we want the end displacements to be zero. If we multiply the diagonal terms in the stiffness matrix that correspond to these end displacements ( K11 and K77 here) by a very large number such as the 109 shown here, then to a good approximation the first and last equations give us U1 = U7 = 0. Thus, we will have satisfied all the force and displacement boundary conditions and we can use this global set of equations to solve for the global displacements.

## Slide 18
In the more general case where a displacement is specified as a non-zero value, C, at the nth node, then replace the right hand side value in the force vector at that node by CxKnnxN, where N is a large value and replace the Knn term in the stiffness matrix by the same large value NxKnn. Example: in our previous example if we had U1 =3 instead of U1 =0, we would have
Notes: If an end displacement was not zero, the same procedure can be used to satisfy such a non-homogeneous displacement boundary condition. In this case we must place the specified displacement times the large term appearing in the diagonal of the modified stiffness matrix in the appropriate column location in the force vector. This again satisfies the displacement boundary conditions to a very good approximation and we can use this system of equations to solve for the global displacements.

## Slide 19
As an example, let’s obtain the solution to our previous problem with this modified global stiffness matrix. Here are the steps in Matlab:
Kg = [ 400 -400 0 0 0 0 0;
-400 800 -400 0 0 0 0;
0 -400 800 -400 0 0 0;
0 0 -400 800 -400 0 0;
0 0 0 -400 800 -400 0;
0 0 0 0 -400 800 -400;
0 0 0 0 0 -400 400]
Kg =
400 -400 0 0 0 0 0
-400 800 -400 0 0 0 0
0 -400 800 -400 0 0 0
0 0 -400 800 -400 0 0
0 0 0 -400 800 -400 0
0 0 0 0 -400 800 -400
0 0 0 0 0 -400 400
P = [0;0;0; 100;0;0;0];
original global stiffness matrix
global force vector after we have initialized it to all zeros and then added in the force boundary conditions
define global stiffness matrix
Notes: Here is the solution to our previous spring problem done with such a modified global stiffness matrix. First, we form up the global stiffness matrix (rather than assemble it from the elements) and form up a force vector which satisfies the force boundary conditions.

## Slide 20
Kg(1,1) = Kg(1,1)*10^9;
Kg(7,7) = Kg(7,7)*10^9;
Ug= Kg\P
Ug =
0.0000
0.1250
0.2500
0.3750
0.2500
0.1250
0.0000
modify the global matrix to satisfy displacement boundary conditions ( we do not have to modify the load vector here since already has zeros at nodes 1 and 7.
solve for the displacements
This looks identical to our original solution but if we display more decimal places, we see the very small differences
format long
Ug= Kg\P
Ug =
0.000000000125000
0.125000000125000
0.250000000125000
0.375000000125000
0.250000000125000
0.125000000125000
0.000000000125000
Notes: Then we modify the global stiffness matrix and solve for the global displacements. This gives essentially the same solution as before. We can then obtain the internal spring forces in the same way as before. We can, however, also make use of a connectivity matrix in that calculation as that matrix tell us what the start and end nodes are for each element.

## Slide 21
Force-Based Finite Elements
The previous discussion should give you a basic feel of how finite elements works for simple structural problems. As seen, the method is based on displacements and the key quantity that is needed is the stiffness matrix so this can be called a stiffness-based finite element method where the fundamental unknowns are the displacements. Although we did not use virtual work ideas in developing the stiffness matrix, in practice that is often the route taken as opposed to the approach we used which was based on equilibrium of the elements. One of the key results, the values of the internal forces, was obtained in the post-processing only after the displacements were found. However, can we turn this around and solve instead for the internal forces in the elements and then obtain the nodal displacements in the post-processing? The answer is yes. That method we will call the force-based finite element method.
Stiffness-based finite elements is the approach found almost universally in the literature and in the research and commercial software found in practice, but force-based finite elements is in many ways closer to the heart of Statics, where equilibrium of the forces and/or moments plays a central role so we will give you a glimpse of this approach. A more detailed and advanced look at this method is in Schmerr, L.W., Advanced Mechanics of Solids, Cambridge University Press, 2021.
Notes: As we have seen the primary unknowns in the stiffness-based finite element method are the displacements. Can we formulate a finite element method where the fundamental unknowns are the internal forces? The answer is yes. Here, we will describe an alternative force-based finite element method.

## Slide 22
In our spring problem we started out with the forces at the ends of a spring element
node i
node j
km
mth element
forces
on mth element
displacements
and the internal force in the spring
…deformation in the spring
Now, let’s not relate the end forces to the nodal displacements but instead to the internal force
in the element:
i
j
From equilibrium
or
mth element
Notes: Again, we will start by examining a single element. In this case, though, we will write the end forces of the element in terms of the internal force through an element equilibrium matrix.

## Slide 23
or
element equilibrium matrix
For our previous spring problem with six elements, we could easily assemble these element
equilibrium matrix into a global 7x6 equilibrium matrix:
or
this is seven equations in eight unknown forces when we include R1 and R2. Even if we eliminate the first and last equilibrium equations, we have 5 equations in 6 unknown forces. This shows that our spring problem is indeed statically indeterminate.
Notes: We can then assemble those element equilibrium matrix into a global equilibrium matrix for the entire system. Again, the right-hand side force vector is the same as seen in the stiffness-based approach. These equilibrium equations show us that the system is indeed statically indeterminate (smaller number of equations than unknown forces) so we need to augment these equilibrium equations with some information on the deformations.

## Slide 24
To find the other equation(s), we need to remember that the internal force in an element is related to the internal deformation (elongation) in the element, which in turn is related to the difference of nodal displacements:
… deformation in the spring
Consider the deformations
or
If we assemble these relations for all the elements we have
which is of the form
were T denotes the matrix transpose
Notes: For a single element, the internal force is proportional to the internal deformation (elongation), which is in turn equal to the difference of the end displacements. We can also write this deformation-displacement relation in vector-matrix form and easily assemble all the elongations in terms of the global displacements. The matrix in this deformation-displacement relation is just the transpose of our global equilibrium matrix so actually we do not have to do the assembly here again.

## Slide 25
To this point we have
equilibrium equations
deformation-displacement relations
but we also have the internal forces and deformations related through
for each element
so for the entire system
where
is called the flexibility matrix
Notes: We can relate the internal forces and deformations to each other through a flexibility matrix that contains the reciprocal of the spring constants.

## Slide 26
Now. let us separate out the specified displacements, which here are U1 and U7 from the remaining “free displacements”, {Uf}, and write the deformation-displacement relations as
Since for fixed nodes the specified displacements are zero, we can eliminate the first term on the right-hand side. Later, we will examine the more general case when the specified values of displacement are not zero .We will write these equations as
where [E]T is a reduced matrix obtained from [Eg]T by eliminating the
columns associated with the known displacements
Notes: If we separate out the specified displacements from the free displacements, we see we can write the deformations in terms of the transpose of a reduced equilibrium matrix where that reduced equilibrium matrix is obtained by eliminating the equations involving the unknown reaction forces at the fixed supports.

## Slide 27
if we eliminate the rows in the global equilibrium matrix that
contain the unknown reaction forces , these rows correspond to the columns we eliminated to obtain the reduced equilibrium matrix [E] in the deformation-displacement relations. Similarly, eliminating the reactions from the global load vector, we obtain a reduced load vector {P} that contains only known forces and we have
which in our present problem are
Notes: Here are the reduced equations in the force-based method at this point. The equilibrium equations are 5 equations in terms of 6 force unknowns. The deformation-displacement equations are 6 equations in terms of 5 free displacements and the deformation-internal force equations are 6 deformations in terms of six internal force. Thus, we have seventeen equations total and seventeen unknowns ( 6 forces, 6 deformations, 5 displacements). These are enough equations to solve our problem, but we want to reduce the problem to one only involving the forces.

## Slide 28
Now, consider the deformation-displacement relationship
There are more deformations than free displacements so there must be some relationship between
the deformations where those displacements are eliminated, i.e., where
The matrix is called the compatibility matrix . If we can find the compatibility matrix, then we must
also have which is the compatibility equation(s) for the internal forces that we can combine
with the reduced equilibrium equations to solve for the internal forces.
We want to find the compatibility matrix that satisfies the compatibility equation
To obtain this compatibility equation for our spring problem is easy since we note that the distance between the fixed supports must not change so that the sum of all the deformations must be zero, i.e.
or
and the compatibility matrix is in this case the vector
Notes: Since there are six deformations in terms of five displacements, there must be a relationship between the deformations themselves, which we write in matrix-vector form as [S}{δ} = 0. This is called the compatibility equation(s). [S] is called the compatibility matrix. Since we can express the deformations in terms of the internal forces, we can write the compatibility equation in terms of the internal forces. This compatibility equation written in terms of the forces can then be combined with the equilibrium equations to give us the six equations we need to solve for the internal forces. We can get the compatibility equation easily in our present problem since we see that the sum of all the deformations (elongations) of the springs must be zero since they are between two fixed supports.

## Slide 29
and in terms of the forces the compatibility equation here is
or
and we could factor out the common 1/k terms if we want to. Here, we will just leave them in.
equilibrium of forces
compatibility of deformations (written in terms of the forces)
Notes: Here we write out explicitly our equilibrium and compatibility equations

## Slide 30
We now are in the position to combine the equilibrium and compatibility equations and solve for the forces
Let’s solve this in Matlab
k = 400;
Es = [ 1 -1 0 0 0 0; 0 1 -1 0 0 0; 0 0 1 -1 0 0;
0 0 0 1 -1 0; 0 0 0 0 1 -1; 1/k 1/k 1/k 1/k 1/k 1/k];
Ps = [ 0; 0; 100; 0 ; 0; 0];
F = Es\Ps
F =
50.0000
50.0000
50.0000
-50.0000
-50.0000
-50.0000
or
[Esys] matrix
load vector plus a zero from compatibility
solve for the forces
zero from compatibility eq.
same forces as before
Notes: We now combine the equilibrium and compatibility equations into a set of system equations which we then solve. Shown are the solutions in MATLAB which agrees with our previous results.

## Slide 31
To solve for the displacements, we start from the deformation-displacement relations written in terms of the forces
which we extend as
for the free displacements (and some zeros)
In our springs problem
Performing these steps in MATLAB:
GF = (1/k)*F;
Us = Es'\GF
Us =
0.1250
0.2500
0.3750
0.2500
0.1250
0.0000
free displacements (same as before) and a zero
We can then solve the equations
obtain [G]{F}
solve for Usys
Notes: To solve for the displacements, we can manipulate the deformation- free displacement equations into a relationship involving the free displacements (and one or more zeros) and the transpose of the system matrix, which we can then solve for the free displacements (and one or more zeros). Again, these agree with our previous results for those free displacements.

## Slide 32
1. Obtain stiffness matrix for an element
2. Assemble element matrices into global stiffness matrix and load vector
3. Apply boundary conditions to obtain
a modified global stiffness matrix and load vector
5. Solve for forces in the elements from difference of displacements in an element
Stiffness-based Finite Element Method
Force-based Finite Element Method
1. Obtain equilibrium matrix for an element
2. Assemble element matrices into global equilibrium matrix and load vector
3. Apply boundary conditions to obtain reduced
equilibrium matrix and load vector
4. Obtain compatibility matrix, [S], which for fixed supports satisfies and append to
equilibrium equations to form up a solvable system
4. solve for the global displacements {Ug}
5. solve for the forces {F}
6. Solve for the free displacements
(and some zeros), {Usys}, from
Notes: Here is a summary of the steps we took in the stiffness-based and force-based finite element methods. A key element in the force-based method was obtaining the compatibility matrix, which we will discuss further next.

## Slide 33
A crucial step in the force-based method is the determination of the compatibility matrix. For our problem we obtained that matrix from a physical argument (that the sum of all the deformations must be zero) but we would like a more direct way to obtain it in all cases. The [S] matrix defines a relationship between the deformations that must be independent of the free displacements. Thus, we must have
which must be true for all the free displacements so we must have
or, taking the transpose
In our springs problem this was explicitly
so we see that the columns of [S]T (Here we have only one column but in the general case there can be more than one column) are just solutions to the homogeneous equilibrium equations. There is a MATLAB function, null, that can obtain these solutions, so we have a direct way to obtain the compatibility matrix (or, more accurately, its transpose).
Determining the Compatibility Matrix [S]
Notes: Previously, we obtained the compatibility matrix by a simple physical argument. Here, we want to find a more general way to find this matrix. In the problem considered the transpose of compatibility matrix was just a column vector. That column vector was a solution to the homogeneous equations involving the reduced equilibrium matrix, i.e., a solution of [E]{F} = 0. This is also true when [S] is a matrix. Then the columns of [S]T will be one or more force vectors that satisfy those homogeneous equations. The MATLAB function null can obtain those homogeneous solutions and thus give us the transpose of the [S] matrix directly.

## Slide 34
E = [ 1 -1 0 0 0 0;0 1 -1 0 0 0; 0 0 1 -1 0 0;
0 0 0 1 -1 0; 0 0 0 0 1 -1]
null(E, 'r')
ans =
1
1
1
1
1
1
null(E)
ans =
0.4082
0.4082
0.4082
0.4082
0.4082
0.4082
norm(ans)
ans = 1.0000
Here is the transpose of the compatibility matrix obtained in MATLAB with the null function for our springs problem
reduced equilibrium matrix
calling the null function with the “rational” option
calling the null function without the rational option
in this case the result is normalized
Notes: Here we see the use of null to generate the compatibility equation for our spring problem. We can call this function with the “rational” optional argument, which gives us back the same values as we had before. If we call the null function without this argument the answer looks different because it is normalized. There is flexibility in expressing the compatibility matrix since we can combine different homogeneous solutions in many ways and still have a valid homogeneous solution.

## Slide 35
Both of these solutions with MATLAB are fine. The rational option solution is most appropriate when the [E] matrix contains elements that are whole numbers or ratios of whole numbers (such as what we have here). When that rational option is not chosen the null function produces a normalized result, which is also acceptable since any constant times a solution to a set of homogeneous equations is also a solution.
Thus, we have a direct way to obtain the compatibility equations in the force-based method, and this step (which is not present in the stiffness-based method) does not add any significant burden to obtaining the solution.
Notes: Thus, once we find the reduced equilibrium matrix, we only need to supply that matrix to the MATLAB null function and take the transpose of the output to get the compatibility matrix. That matrix multiplied by the flexibility matrix then gives us the additional equation(s) we need in conjunction with equilibrium to solve the problem.

## Slide 36
Before we leave the force-based finite element method we want to show how to include non-zero specified displacements at supports.
Let us begin by separating out the specified displacements, from the remaining “free displacements”, {Uf}, and write the deformation-displacement relations as
if the end displacements were non-zero.
where Us are the specified displacements and [E]T is a reduced matrix obtained from [Eg]T by eliminating the
columns associated with the known displacements. For example, for our springs problem we would have
Non-Zero Specified Displacements
Notes: In the stiffness-based method we showed how to find the solution for non-zero specified displacements. Here, we will show how we can handle that case with the force-based method. In this case, however, we will not have to modify the solution process for the forces but instead we will just modify the post-processing steps after those forces are found. To see this, go back to the deformation-displacement relations we saw we could write that relationship in terms of the specified displacements {Us} and the free displacements {Uf}, as well as the transpose of the reduced equilibrium matrix, [E], as well as a matrix [ER]T.

## Slide 37
if we eliminate the rows in the global equilibrium matrix that
contain the unknown reaction forces , these rows in [Eg] correspond to the columns in the [ER]T matrix that we removed from the transpose of the global equilibrium matrix.
Similarly, eliminating the reactions from the global load vector, we obtain a reduced load vector {P} that contains only known forces and we have
Notes: The rows in the global equilibrium matrix that we remove to obtain the reduced equilibrium matrix are related to the unknown reaction forces. Those same rows form the columns of the matrix [ER]T so it is easy to get this matrix from the global equilibrium matrix. Shown are the equations up to this point in terms of well-defined matrices and vectors.

## Slide 38
Now, consider the deformation-displacement relationship
and try to find a compatibility matrix where which we
see implies Again, the null function can be used to find [S].
It then follows that we can write the deformation-displacement equations as equations for the internal forces
equilibrium of forces
compatibility of deformations
which are additional equations for the internal forces that we can use in conjunction with the reduced equilibrium equations:
The only difference from the zero support displacements case considered previously is that we have a known non-zero right hand side to the compatibility equations
Notes: Again, if we obtain the compatibility matrix from homogeneous solutions for the reduced equilibrium matrix, we can write the compatibility equations in terms of a non-homogeneous set of equations involving the internal forces.

## Slide 39
If we combine the equilibrium and compatibility equations, we have a set of system equations we can solve for the forces.
To solve for the displacements, we start from the deformation-displacement relations written in terms of the forces
which we extend as
for the free displacements (and some zeros). Thus, we now have a complete solution for the forces and displacements in the more general case where we have non-zero specified displacements
We can then solve the equations
Notes: Combining these compatibility equations with the reduced equilibrium equations then allows us to set up a system of equations we can solve for the internal forces. If we include the non-zero specified displacements in the post-processing to obtain the free displacements, very similar steps to those in the case of zero specified displacements allow us to obtain the free displacements (and one or more zeros).

## Slide 40
Connection between the displacement-based (stiffness) approach and the force-based approach
Recall, we previously had a complete set of equations involving both the displacements ,the forces, and the deformations. These are sufficient to solve, in principle, for all these unknowns.
If we place the inverse of the deformation-force (flexibility) relation into the deformation-displacement relation and then place that result in turn into the equilibrium equations, we eliminate the forces and find an equation for the displacements we can solve:
where [G]-1 is the inverse of the flexibility matrix. Equivalently,
where
is a stiffness matrix (sometimes called a pseudo stiffness matrix since in the stiffness-based finite element method the stiffness matrix is generated from work energy principles and may be different from this [K])
Displacement-based Method
N equations for M forces
M equations relating
M deformations to N displacements
M equations for M deformations and
M forces
so there are 2M+N equations for 2M +N unknowns (the forces, deformations, and displacements)
Notes: The displacement-based and force-based approaches are closely related since they both arise from a more general set of equations involving the forces, displacements, and deformations. We can eliminate the forces and obtain a set of equations for the displacements, as shown here.

## Slide 41
Force-based Method
We can find the compatibility equations
by solving
The compatibility equations can then be written in terms of the forces only as
Combining the equilibrium and compatibility equations then allows us to solve for the forces directly
Thus, both the displacement-based (stiffness) approach and the force-based approach are simply different ways to reduce our original set of equations to a solvable set for either the displacements or the forces.
Again, this same complete set of equations is the starting point for the force-based method:
Notes: Alternatively, we can reduce the problem to one involving only the forces by combining equilibrium and compatibility equations. Thus, displacement-based and force-based methods are just alternate ways of considering the same general set of equations.