## Slide 1
Beam Singularity Functions
Notes: In this section we will examine the use of singularity functions to draw internal shear force and bending moment distributions.

## Slide 2
Learning Objectives
Definition of Singularity Functions
Use of Singularity Functions
Notes: We will define singularity functions and show their use in some examples.

## Slide 3
Shear and bending moment diagrams can be rather complex when there are a number of different loads acting on a beam. To write explicit equations we must consider separate free body diagrams for each section of the beam where the loads change. It would be nice if we could express the shear force and bending moment in terms of functions that are valid for the entire beam. Such functions are called singularity functions.
Example: consider a concentrated load, P, on a beam at x = a
x = a
P
for x < a
V = 0
M = 0
for x > a
P
V = P
x-a
M = P(x-a)
x
Notes: In the last section we showed how to sketch out shear and bending moment diagrams from the relationships that exist between these functions and the applied loads. While those sketches are important, if we want, for, example, to calculate the beam deflections, we will need to know the actual V(x) and M(x) distribution functions. As seen, even in the simple example considered in the last section, the applied loads on the beam cause changes in the free body diagram for the internal force and moment so we need to define the shear force and bending moment in a piece-wise fashion. But what if we could define the loading in terms of functions that are good for the entire beam? If we know how to integrate those functions, we could then obtain the shear force and bending moment explicitly for the entire beam. These functions are called singularity functions. For example, at a concentrated force, we can write the change in the shear force caused by that force from equilibrium.

## Slide 4
Here, we can express the shear force and bending moment in terms of ordinary functions in a piece-wise manner
or we can write these expressions in terms of singularity functions
where
are called singularity functions
Notes: We can, as done before, write these results in a piece-wise manner, but we can also write them as singularity functions, <x-a>n, as defined here, where x = a is where the concentrated force, P is located.

## Slide 5
As a second example consider a uniform load that starts at x=a (and continues forever):
w lb/ length
x = a
for x < a
V = 0
M = 0
for x > a
w(x-a)
x-a
(x-a)/2
V = w(x-a)
M = w(x-a)2/2
Notes: In the same fashion we can consider a constant distributed load that starts at a location x = a.

## Slide 6
which we can write as
or in terms of singularity functions as
Notes: where we see the shear force and bending moment can again be written as singularity functions.

## Slide 7
singularity functions can be differentiated and integrated like ordinary functions
Notes: What makes the singularity functions easy to use is that they obey differentiation and integrations that are analogous in form to those for the ordinary functions xn .

## Slide 8
Singularity Functions for describing the shear force and bending moments of various loads
x = a
P lb
V = P< x-a >0
M = P< x-a >1
C ft-lb
V = 0
M = C< x-a >0
w lb/ length
V = w< x-a >1
M = w/2< x-a >2
1
s lb/ length2
V = s/2< x-a >2
M = s/6< x-a >3
x = a
x = a
x = a
Notes: Here is a summary for a variety of applied loads. We can use combinations of these to generate many of the common loadings found on a beam.

## Slide 9
Consider a simple example
20 lb/ft
A = 50 lb
10 ft
10 ft
B = 150 lb
don't need
V
M
Notes: Here is an example where we have solved for the end reaction forces on the beam and use the singularity functions to describe the shear force and bending moment. We can, as we will see shortly, use MATLAB to draw these results and obtain sketches of V and M. However, since we have explicit functions of x here, we can easily obtain the values at any location we want as well. Note that in the bending moment expression we do not need the last singularity function since that function is zero for all x <= 20, so it does not affect the values anywhere in the beam. Including it, however, is also fine.

## Slide 10
Singularity Functions in MATLAB
function y = step_sf(x,a)
if x(1) == a
y = (x > a);
else
y = (x >= a);
end
1.0
function y = lin_sf(x,a)
y = (x-a).*(x > a);
x = a
function y = quad_sf(x,a)
y = ((x-a).^2).*(x > a);
function y = cubic_sf(x,a)
y = ((x-a).^3).*(x > a);
x = a
x = a
x = a
Notes: Here are some MATLAB functions that define four of these singularity functions. The step function looks a bit different since one must carefully define the values for that function so that the discontinuity at x = a is always plotted correctly.

## Slide 11
Consider this simple example
again:
x = linspace(0, 20, 1000);
V= 50*step_sf(x, 0) -20*lin_sf(x,10) +150*step_sf(x,20);
plot(x,V)
V
0
2
4
6
8
10
12
14
16
18
20
-150
-100
-50
0
50
M = 50*lin_sf(x,0)- 10*quad_sf(x,10);
plot(x, M)
0
2
4
6
8
10
12
14
16
18
20
0
100
200
300
400
500
600
M
20 lb/ft
A = 50 lb
10 ft
10 ft
B = 150 lb
Strictly speaking, from the distributed load
we should write:
x
y
10
20
V = -20*lin_sf(x,10) +20*lin_sf(x,20)
but this term has no contribution for x < = 20
Notes: Since we have these singularity functions defined in MATLAB, we can use MATLAB to plot them. Note that the constant distributed load as modeled by the singularity function -20<x-20>1 goes on forever while our load ends at x = 20. Thus, strictly speaking we should add another constant load 20<x-20>1 to cancel the load off. However, this added singularity function gives no contribution for x <= 20 so it can be omitted. We have also omitted the 150<x-20>1 term in the bending moment expression for the same reason. Keeping them in, if you like, is fine.

## Slide 12
Placing the shear force and bending moment into a variable allows us to plot those parameters. However, if we generate anonymous functions instead then we can also obtain any critical points in those plots as well.
V = @(x) 50*step_sf(x, 0) -20*lin_sf(x,10) +150*step_sf(x,20);
x = linspace(0, 20, 1000);
plot(x, V(x))
M = @(x) 50*lin_sf(x,0)- 10*quad_sf(x,10);
figure(2)
plot(x, M(x))
V
0
2
4
6
8
10
12
14
16
18
20
-150
-100
-50
0
50
0
2
4
6
8
10
12
14
16
18
20
0
100
200
300
400
500
600
M
For example, the maximum bending
moment occurs where V = dM/dx = 0, a location we can find with the fzero function
xm = fzero( @(x) V(x), 12) % find where V = 0, initial guess = 12
xm = 12.5000
M(12.5) % maximum bending moment
ans = 562.5000
Notes: Instead of using variables to hold the shear force and bending moment, if we generate anonymous functions then we can plot those functions and evaluate them at any point we want. Places where maxima occur are examples where this capability is particularly useful, as shown.

## Slide 13
V = @(x) -1000*lin_sf(x, -3)+8000*step_sf(x, 0) +1000*lin_sf(x, 3) ...
-5000*step_sf(x, 6) + 9000*step_sf(x, 9) - 4000*lin_sf(x, 9) +(2000/3)*quad_sf(x,9);
M = @(x) -500*quad_sf(x, -3) +8000*lin_sf(x, 0)+ 500*quad_sf(x, 3) -5000*lin_sf(x,6)...
-9000*step_sf(x, 6) +9000*lin_sf(x,9) -2000*quad_sf(x, 9)+(4000/18)*cubic_sf(x,9);
x = linspace(-3, 12, 1000);
plot(x, V(x))
figure(2)
plot(x, M(x))
8000 lb
5000 lb
9000 lb
1000 lb/ft
9000 ft-lb
4000 lb/ft
3'
3'
3'
3'
3'
x
=
but these have no effect
for x < = 12
Again, strictly speaking:
More complex
example:
Notes: Here is a much more complicated loading distribution for a beam where the reaction forces at the supports have already been calculated. Study the terms here carefully to understand where they come from. Note that we do have to describe the 1000 lb/ft load by two terms since we must ensure it ends at x = 3. Similarly, we describe the linearly varying distributed load by two terms, although strictly speaking we would need two additional terms to end the distributed load entirely at x =12. You can verify that those additional terms give no contribution and so can be neglected. We now are in a position to plot these distributions, which are shown on the next slide.

## Slide 14
V (lb)
x, ft
-4
-2
0
2
4
6
8
10
12
-4000
-3000
-2000
-1000
0
1000
2000
3000
4000
5000
6000
M (ft-lb)
x ,ft
-4
-2
0
2
4
6
8
10
12
-6000
-4000
-2000
0
2000
4000
6000
8000
10000
12000
V(0)
ans = -3000
M(0)
ans = -4500
values at some points:
Notes: Here are the shear and bending moments from x = -3 to x =12 ft. Drawing these by hand, while possible, is very tedious but the singularity functions make it rather effortless.

## Slide 15
V = @(x) -1000*lin_sf(x, -3)+8000*step_sf(x, 0) +1000*lin_sf(x, 3) ...
-5000*step_sf(x, 6) + 9000*step_sf(x, 9) - 4000*lin_sf(x, 9) +(2000/3)*quad_sf(x,9);
M = @(x) -500*quad_sf(x, -3) +8000*lin_sf(x, 0)+ 500*quad_sf(x, 3) -5000*lin_sf(x,6)...
-9000*step_sf(x, 6) +9000*lin_sf(x,9) -2000*quad_sf(x, 9) +(4000/18)*cubic_sf(x,9);
Note that once we have V(x) we can get M(x) by integration since
but the net constant term after all the integrations will be zero if M = 0 for x values less than the starting point in the integration (at x = -3 in this example), which is always the case.
We can do the integrations since for the singularity functions
couple
If there are any concentrated couples present, they must be added to the integrated shear force expression:
Notes: Since the shear force and bending moment distributions are related through integration, we only needed to define the shear force in terms of singularity functions, integrate those functions and add in the concentrated couple singularity function to obtain the bending moment expression. Since the shear force and bending moment expressions always start and end at zero values, any constant of integration term is zero. Here we compare the V and M expressions so you can see this process in action. Study these to see where each function comes from as well as its coefficient.