## Slide 1
A MATLAB Function for Resultants
Notes: These slides show us how to get a single resultant force and its location with a MATLAB function that solves r×R=M. This function is discussed in Appendix C of the addendum to the text.

## Slide 2
Learning Objectives
Solving for Resultant Location with MATLAB
Notes: Determining resultants requires us to solve the equation r x R = Mp where R is the resultant force and Mp is a moment that is perpendicular to R. Here, we set up a MATLAB function R_loc that performs this solution for us for general 3-D problems.

## Slide 3
Solving when
If we let
then performing the cross product gives three equations
We know that we cannot solve this system directly since there is not a unique solution ( if is a solution then is also a solution for any l , i.e., we can slide R anywhere along its own line of action and we will still have a solution )
However, we can choose x = 0 or y = 0 or z = 0 and then find a particular solution.
Notes: The solution of r x R = Mp is not unique since we can always slide a resultant force along its line of action. However, if we locate the resultant force in a particular plane, as we have seen in previous examples, we can find a unique point in a plane.

## Slide 4
suppose we set x = 0. Then the second and third equations give
as long as Rx is not zero. If Rx is zero then we cannot slide R along its line of action to find such y and z values and we must choose either y = 0 or z = 0 instead
Note that if we place this solution for z and y back into the first equation we obtain
x
y
z
R
or
which is just , which is satisfied identically
Rx = 0
Notes: For example, suppose we try to find a location in the y-z plane. Then we can always find a solution as long as Rx is not zero.

## Slide 5
If we had set y = 0 instead the first and third equations would give
as long as Ry is not zero
x
y
z
R
Otherwise we would need to set x = 0 or z = 0
The second equation in this case gives again just
Ry = 0
Notes: Similarly, we can always find a location in the x-z plane as long as Ry is not zero.

## Slide 6
Finally, if we had set z = 0 we would obtain from the first two equations
as long as Rz is not zero
x
y
z
R
Otherwise, we would need to set x = 0 or y = 0
The third equation in this case gives again just
Rz = 0
Notes: Finally, we can always find a solution in the x-y plane as long as Rz is not zero.

## Slide 7
All three of these cases and the conditions on the components of R can easily be placed in a MATLAB function R_loc
function r =R_loc(R, M, str)
%
% r=R_loc(R,M,str)solves r x R = M for the location of a single
% resultant force R that is statically equivalent to R and M.
% str is a string that must be either 'x=0' , 'y=0', or
% ' z=0', needed to determine a unique location for the resultant.
% R and M must be perpendicular to each other for a solution.
% The output, r, of the function is a vector containing the
% (x,y,z) coordinates of the location of the resultant.
description of the function
Notes: The MATLAB function handles all three of these cases. We merely need to give it the resultant force and moment and a string that defines the plane where we want to locate the resultant force. If we choose a plane where a solution is not possible, the function notifies us and allows us to choose another plane. If M is not perpendicular to R the function warns us and exits.

## Slide 8
eR = R/norm(R); % unit vector along R
eM = M/norm(M); % unit vector along M
if abs(dot(eR, eM)) > 1.0e-3 % check that dot(R,M) =0 approx.
warning('dot(eR, eM) >.001,likely no solution')
end
if strcmp(str, 'x=0') % try to set x =0
if abs(R(1))<eps
error('Rx is zero, cannot choose x=0') % if Rx=0, must make other choice
else
r=[ 0 -M(3)/R(1) M(2)/R(1)];
end
elseif strcmp(str, 'y=0') % try to set y =0
if abs(R(2)) < eps
error('Ry is zero, cannot choose y =0') % If Ry =0, must make other choice
else
r=[ M(3)/R(2) 0 -M(1)/R(2)];
end
elseif strcmp(str, 'z=0') % try to set z=0
if abs(R(3)) < eps
error('Rz is zero, cannot choose z=0') % if Rz =0, must make other choice
else
r=[ -M(2)/R(3) M(1)/R(3) 0];
end
else error(' str must be ''x=0'' or ''y=0'' or ''z=0''') % wrong string input
end
the body of the function R_loc
Notes: Here is the body of the R_loc function.

## Slide 9
Let's apply R_loc to the previous parallel force system (Example 3.2)
50 N
250 N
150 N
200 N
1.5 m
1.5 m
2 m
2 m
x
y
z
O
resultant force
location in y = 0 plane
moment about point O
Summary of previous results:
Notes: This is a problem we solved previously in the last section. Now, we want to solve it with R_loc

## Slide 10
R=[0 -50 0];
M=[300 0 -675];
r=R_loc(R,M,'y=0')
r =
13.5000 0 6.0000
r=R_loc(R,M,'x=0')
??? Error using ==> R_loc
Rx is zero, cannot choose x=0
r=R_loc(R,M,'z=0')
??? Error using ==> R_loc
Rz is zero, cannot choose z=0
cross(r,R)
ans =
300 0 -675
Check
Same as x and z values calculated
previously
Could not set x=0 or z =0
Notes: In MATLAB we give R_loc the resultant force and moment. We get the same values for the location in the x-z plane. Since this was a parallel force system with the resultant force in the y-direction we cannot locate the resultant in either the x-y or y-z planes. If we try, we see that R-loc tells us there is an error. We can check and see that r x R = M is indeed satisfied.

## Slide 11
x
y
z
75 lb
80 lb
50 lb
12 in
9 in
O
Reduce the force system to a wrench and locate the wrench in the xz-plane. Use the Matlab function R_loc.
This is the same problem we did earlier in Example 3.4 to determine a wrench.
Notes: Now, try the R_loc function on Example 3.4 where we determined an equivalent wrench.

## Slide 12
Results from the previous wrench Example 3.4
R = 0 50 155
Mperp = 900.0000 -131.4797 42.4128
for y = 0, we found x=0.8483 in. , z= -18 in.
R=[0 50 155];
Mperp=[900 -131.4797 42.4128];
r=R_loc(R,Mperp,'y=0')
r =
0.8483 0 -18.0000
Resultant force
Moment perpendicular to R
Location of wrench in x-z plane
Using R_loc we have
which gives us the same values as before
x
y
0.848 in
-18 in
O
z
plane parallel to yz-plane
Mparallel = 131.48 j + 407.59 k
Moment parallel to R
in-lb
Notes: Using the previous results for the resultant force and moment, we need to use the moment perpendicular to R in R_loc. In the x-z plane we get the same results.

## Slide 13
x
y
0.848 in
-18 in
O
z
x-y plane
5.807 in
Try other choices
r=R_loc(R,Mperp,'x=0')
??? Error using ==> R_loc
Rx is zero,cannot choose x=0
r=R_loc(R,Mperp,'z=0')
r =
0.8483 5.8065 0
This is another legitimate solution
Since we could also locate the resultant in the x-y plane:
in-lb
Notes: If we try the y-z plane we get an error because the resultant lies in a plane parallel to the y-z plane. If we try the x-y plane we can find a different location for the resultant, as shown.