## Slide 1
Equilibrium of Trusses - III
Notes: These slides will complete our current discussion of trusses. We will come back to trusses later, where we will examine statically indeterminate trusses.

## Slide 2
Learning Objectives
Method of Sections
Spatial Trusses
Notes: We will briefly address the method of sections. We will also examine spatial trusses

## Slide 3
Trusses – Method of Sections
Unlike the method of pins the method of sections is not very amenable to computer solution. However, it is a very efficient way of getting particular truss member forces by hand.
In the method of sections, we take a cut through the truss to expose the member whose force we want and then use the equations of equilibrium for the coplanar force system of the section of the truss we have cut off. In some cases we have to take more than one cut.
+
+
+
The moment equation here is especially useful since we can choose the point we take moments about to eliminate as many unwanted unknowns as possible.
A
B
C
D
E
F
G
H
I
1000 lb
500 lb
6 ft
each vertical section is 4 ft long
for each section:
Notes: In the method of pins, we often need to examine many equations of equilibrium even if we were only interested in analyzing the truss for a few specific forces. In the method of sections, we imagine slicing through the truss and exposing a section of the truss on which the force we are interested in is acting. For each section we have a coplanar set of forces so we have three equations of equilibrium we can apply. Often the moment equation here is particularly useful since if we take moments about the “right” point, we can often eliminate other unknowns and obtain the force we want directly. We will see the method of sections in action for the truss shown here.

## Slide 4
A
B
C
D
E
F
G
H
I
1000 lb
500 lb
6’
each vertical section is 4’ long
Example 5.2
Determine the force in member GH (which is buried deeply in the truss).
C
D
E
F
G
B
4’
4’
6’
4’
1000 lb
500 lb
FBC
FBG
FGH
+
FGH = 2333.3 lb C
imaginary
cut
Notes: Here we want to find specifically the force in member GH. If we tried to get the value for this force by the method of pins, we would have to go through many pins to get to GH and solve for many other unknowns along the way. However, if we take a cut through the structure as shown on the right and look at the free body diagram of the section above this cut, as shown on the left, we see that there are three unknown forces acting in this free body diagram. We have three equilibrium equations for this section so we could solve them for all three forces, but note if we simply take moments about point B we could get the force in GH directly, as shown. Note that if we had looked at the section below the cut then we would also have the reaction forces at A and I in that free body diagram and we could not find the force in GH until we know those reaction forces (which we could find from equilibrium of the entire truss). Thus, using the section above the cut is the most efficient way to go.
Statics courses often emphasize the method of sections since we can often use this method to solve problems easily with a hand calculator. However, the method of sections is not as easily implemented on a computer as is the method of pins, so for a complete solution for all the forces in a truss problem the method of pins together with MATLAB is the method of choice.

## Slide 5
Spatial (3-D) Trusses can also be solved with the method of pins or the method of sections. At each pin we have three equilibrium equations. There may be more equilibrium equations to consider but MATLAB can again be used effectively. Here, we will consider a solution via the method of pins.
Spatial Trusses
Example 5.3
Consider the space truss shown consisting of the five members AB, AD, DC, DB, and BC. The truss is supported by ball and socket joints at A and C and by a short, horizontal weightless link (two-force member) parallel to the y-direction at D. Members AB and BC lie in the x-y plane. Using the method of pins, determine all the forces in the members and the reactions at A, C, and D.
x
y
z
A
B
C
D
500 N
3 m
3 m
4 m
5 m
O
200 N
The truss is statically determinate since we have 3 equilibrium equations at each of the four pins for a total of 12 equilibrium equations. We have 5 unknown member forces and 7 reactions for 12 unknowns.
Notes: Spatial truss problems follow the same procedures used for planar trusses.

## Slide 6
A
B
C
D
500 N
200 N
x
y
z
Free body diagrams of the forces at the four pins are shown. To make these free body diagrams useful we need to define the unit vectors. Then we can form the force equilibrium equations at each pin and collect and solve those equations. We will use a symbolic MATLAB solution method.
First, get the unit vectors that define the directions of the member forces at the pins and the applied and reaction forces. Note that, as for the two-dimensional trusses, we will show the member forces at the pins as if those members are in tension so the unit vectors that define those forces will always act away from the pins along the various members.
Notes: Again, free body diagrams are useful. Here we cannot easily show the geometry on the free body diagrams. All that geometric information is in the definition of the unit vectors.

## Slide 7
DA = [ 3 0 -5];
eDA = DA/norm(DA);
DC = [ -3 0 -5];
eDC = DC/norm(DC);
DB = [ 0 4 -5];
eDB = DB/norm(DB);
eAD = - eDA;
AB = [ -3 4 0];
eAB = AB/norm(AB);
eCD = - eDC;
CB = [ 3 4 0];
eCB = CB/norm(CB);
eBD = - eDB;
eBA = - eAB;
eBC = - eCB;
A
B
C
D
500 N
200 N
x
y
z
x
y
z
A
B
C
D
500 N
3 m
3 m
4 m
5 m
O
200 N
Here are the unit vectors obtained from
the position vectors
Notes: Here we obtain the unit vectors. Since all the unknown truss member forces are shown in tension, the unit vectors will occur in equal and opposite pairs, i.e., eBC = - eCB etc.

## Slide 8
Having these unit vectors, we can then define the unknown force magnitudes symbolically, and then compute the resultant forces at each pin (which must, of course, be all zero):
syms Ax Ay Az Cx Cy Cz Dy Tda Tdb Tdc Tab Tbc
FD = Tda*eDA + Tdb*eDB + Tdc*eDC + [ 0 Dy 0]; % resultant forces at the pins
FA = [Ax Ay Az] + Tda*eAD + Tab*eAB;
FB = [ 200 0 -500] + Tab*eBA + Tdb*eBD + Tbc*eBC;
FC = [ Cx Cy Cz] + Tbc*eCB + Tdc*eCD;
A
B
C
D
500 N
200 N
x
y
z
Notes: Now we can define the resultant forces at all the pins

## Slide 9
We can form all these forces into a set of vector equilibrium equations and solve those equations, placing the results in a MATLAB structure, S:
Eqs = [FA; FB ; FC; FD];
S = solve(Eqs);
Sn = double( [ S.Ax; S.Ay; S.Az; S.Cx; S.Cy; S.Cz; S.Dy; S.Tab; …
S.Tbc; S.Tda; S.Tdb; S.Tdc])
Sn = % Forces in Newtons
-400.0000 Ax
333.3333 Ay
250.0000 Az
200.0000 Cx
66.6667 Cy
250.0000 Cz
-400.0000 Dy
-416.6667 Tab
-83.3333 Tbc
-291.5476 Tda
640.3124 Tdb
-291.5476 Tdc
Notes: Placing all these resultant forces at the pins into a complete set of equilibrium equations for the truss, we can solve those equilibrium equations and obtain all the truss member forces and reactions. Note that we again did not have to have ==0 present in these equations to obtain the solution with the solve function.