## Slide 1
Equilibrium of Cables
Notes: We will briefly examine the equilibrium of cables

## Slide 2
Learning Objectives
Solve for the tensions in cables that carry discrete loads
Notes: We will only examine cables that carry discrete forces. The case where the loads are distributed are also discussed in the addendum.

## Slide 3
A
B
C
D
E
x
y
We will examine cable problems such as this one where the cables are acted upon by known discrete loads and we specify the horizontal lengths (L's) .
This looks much like a truss problem since the cables only carry axial tensions (no compressive forces here).
However, unlike a truss the angles here are also unknown so unless we specify more information, we cannot solve the problem. The additional inform we will assume is that either one of the sags (y's) is specified or that we specify the maximum tension, which will always occur at one of the ends (A or E here)
Notes: To solve cable problems with discrete loads we will assume the loads and horizontal distances (L's) are known. To obtain a solution we will need one more known quantity. We will assume either one of the sags (y's) is known or that the maximum tension in the cables (which must occur at one of the ends) is known.

## Slide 4
A
B
C
A
B
C
D
E
x
y
(a)
(b)
Example: suppose the sag (y2) at C is known. Then the procedure is as follows.
Examine the free body diagram of the entire system (a)). There are 3 equations in 4 unknowns.
From equilibrium in the y-direction and moment equilibrium about A or E we can find Ay and Ey and we also find Ax = - Ex.
Since y2 is known the free body diagram in (b) shows that since all the necessary distances in the moment equation are known, we can sum moments about C to find Ax (and hence Ex). Thus, we have now found all the reactions.
Notes: Here are the steps in the solution procedure. The basic idea is to first find the end reactions and then work through the cable system, one connection at a time, just like the method of pins for a truss.

## Slide 5
x
y
A
B
C
D
4. Starting at A (or E) we can then work through the entire cable a connection at a time to find an unknown tension in a cable segment and the angle of that cable segment. This is like the method of pins for a truss except we are now finding the internal forces (which must be tensions) and the angle of the cable at each connection.
If the maximum tension in the cable was specified instead of specifying a sag, then we would repeat steps 1 and 2 again for the entire system and find Ay, Ey, and Ax = - Ex. If we find, say, Ay is bigger than Ey, then the maximum total reaction force must be at A. From a free body diagram of the pin at A we must also have the maximum known tension Tmax at A and we can use this free body and the known value of Tmax to determine Ax and q1 (and hence Ex also). Once the reactions are known we can again work through the system a connection at a time to find the remaining unknown tensions and angles.
A
Notes: The solution procedure is very similar if either a sag or a maximum tension is specified.

## Slide 6
5 m
5 m
5 m
5 m
1.5 m
1600 N
3000 N
A
B
C
D
x
y
Example 12.3
Consider the cable system shown. Note that the sag at B is known.
A
B
C
D
1600 N
3000 N
5
5
5
5
1.5
(a)
From equilibrium for the entire system
three equations in four unknowns
Notes: Here is an example of a cable system where the ends are at different levels. Note that the sag at B is known since the vertical distance from A is known.

## Slide 7
A
B
5
1.5
(b)
moment equilibrium about B gives one additional equation
We can solve these four equations for the four reactions. Let's do it symbolically in MATLAB but it is also easy to solve by hand as shown in the text.
syms Ax Ay Dx Dy
Eq(1) = Ax + Dx;
Eq(2) = Ay + Dy -4600;
Eq(3) = 5*Ax - 15*Ay +31000;
Eq(4) = -5*Ay -1.5*Ax;
S = solve(Eq);
double([ S.Ax S.Ay S.Dx S.Dy])
ans =
1.0e+03 *
-3.2632 0.9789 3.2632 3.6211
Notes: Taking moments about B where the sag is known in conjunction with equilibrium for the entire system gives us four equations for the four unknown reactions so we can determine those reactions

## Slide 8
A
B
1600
3000
C
Ay = 978.9 N
Ax = - 3263 N
x
y
we can now go through the system one connection at a time, starting at A
Notes: With the reactions known we then can work through the entire system one connection at a time. We have concurrent coplanar forces at each connection, so this looks much like the method of pins for a truss except here we are solving for unknown angles as well as the internal cable tensions.

## Slide 9
connection B
connection C
which gives
which gives
A
B
1600
3000
C
Ay = 978.9 N
Ax = - 3263 N
x
y
This completes the solution. We do not have to consider the pin at D, but we could use it as a check on our results
Notes: In this case we do not have to consider equilibrium at D since we have found all the unknowns using only A , B, and C but we could use equilibrium at D as a validation check.