## Slide 1
Equilibrium of Trusses -I
Notes: These slides will examine how to solve truss problems

## Slide 2
Learning Objectives
Method of Pins
Zero Force Members
Notes: First, we will examine in detail the method of pins. We will also briefly talk about identifying zero force members.

## Slide 3
A truss consists of an interconnected system of weightless members which are pinned together at their ends with smooth pins. Thus, all the members of the truss are two force members . The applied loads and support forces are all applied to the pins.
If all the members are straight, as in the truss shown above, the truss is called a planar truss.
If a truss consists of a series of interconnected triangular sections, as shown above, then the truss is called a simple truss.
Notes: A truss consists of a series of two force members connected by smooth pins. All the forces are assumed to be applied to the pins and any weights of the members are neglected.

## Slide 4
Simple trusses
Simple trusses can be statically determinate, statically underdetermined (statically indeterminate), or statically overdetermined.
If there are m members in the truss, n reaction forces on the entire truss and j pins, then a simple truss is statically determinate if
(the truss above is statically determinate:
11 members, 3 reactions, 7 pins)
The truss is statically indeterminate if
The truss is statically overdetermined if
(such trusses are unstable or not sufficiently
constrained to prevent motion)
Notes: A statically determinate truss is one where the total number of unknown forces is equal to the number of equilibrium equations. Since in the method of pins all the equilibrium equations will be written for the pins where there are two equilibrium equations at each pin in the x- and y-directions, the total number of equilibrium equations will be twice the number of pins. In contrast, a statically indeterminate truss will have more unknowns than equations of equilibrium and so cannot be completely solved by equilibrium alone. For such trusses we must consider the deformations of the truss members, which we will do later with the method of finite elements. A statically overdetermined truss will have more equilibrium equations than unknowns. Although we can solve for all the unknowns in this case, the truss, as we will see, is not constrained properly so this type of truss is avoided in practice.

## Slide 5
Statically determinate simple trusses
Number of unknown member forces
The number of external reaction forces
2 equilibrium equations at each pin
Notes: This is a statically determinate truss with eleven unknown forces in the bars of the truss and three unknown external reaction forces (shown in red). There are 7 pins, so we have 14 equations of equilibrium to solve for a total of 14 unknowns.

## Slide 6
1200 lb
3 ft
4 ft
5 ft
A
B
C
Determine the forces in all the
members of the truss and the reaction forces by the method of pins.
There are three reaction forces and three forces in the members = 6 unknowns
there three pins x 2 equations/per pin= 6 equations
If we were doing this solution via computer, we would set up and solve all 6 equations simultaneously. If we were doing this solution by hand, it is easier to use the three equations for the overall structure first and then we will have to solve only three equations from a subset of the six pin equations. We will show both solutions.
The method of pins (joints)
Example 5.1
Notes: Here we will solve how to solve a truss problem by hand and with the aid of MATLAB.

## Slide 7
1200 lb
4 ft
5 ft
A
B
C
Ax
Ay
Cy
Example solution by hand
FBD of overall structure:
x
y
3 ft
+
+
+
Notes: In solving the problem by hand, we first examine equilibrium of the whole truss. Since this is a coplanar force system, we have three equations of equilibrium which we can use to determine the three unknown external reaction forces.

## Slide 8
+
+
Pin C
1600 lb
0
FBC
+
Pin A
1200 lb
1600 lb
FAC
3
4
5
FAB
Note that we did not have to consider the x- force equation for pin C or either the x- or y- force equations for pin B to solve for all the unknowns
If we always draw the unknown forces in the members as pulling on the pin, this assumes the member is in tension. If the member force, therefore, comes out to be negative, we know the member is actually in compression.
Notes: When we examine equilibrium of a pin we will always draw the bar forces as if they were in tension, i.e., where the bars will always pull on the pin. If the solved result for bar force is positive, then indeed that bar will be in tension. If the result is negative the bar will be in compression. In this problem we see that we need only consider pins A and C to get all the truss bar forces.

## Slide 9
1200 lb
2000 lb
2000 lb
2000 lb
2000 lb
0
0
0
1600 lb
1600 lb
1600 lb
1600 lb
1200 lb
1600 lb
1600 lb
0
Solution (as it would normally be given)
x
y
For the truss members we give the magnitude of the forces and indicate explicitly if the member is in tension (T) or compression (C)
Notes: Here are FBDs for all the members and pins of the truss and the forces obtained from equilibrium. The results for the bar forces are usually given by the magnitudes of those forces followed by T or C to indicate if the bar was in tension (T) or compression (C).

## Slide 10
Numerical Solution with MATLAB
Here we will consider all three pins
Pin A
FAC
3
4
5
FAB
+
+
Ax
Ay
Pin C
Cy
FAC
FBC
+
+
Pin B
1200 lb
FAB
FBC
4
5
3
+
+
(1)
(2)
(3)
(5)
(6)
(4)
Notes: To solve a truss with MATLAB we draw FBDs for all the pins, as shown here. Then we write the equilibrium equations at all the pins. In this case there are 6 equilibrium equations and six unknown forces. From these equations we see we can solve directly for some of the forces, but we will not do that and instead enter all six equations.

## Slide 11
unknowns
Ax
Ay
Cy
FAB
FAC
FBC
X(1)
X(2)
X(3)
X(4)
X(5)
X(6)
0 0 0.6 1 0
0 1 0 0.8 0 0
0 0 0 0 -1 0
0 0 1 0 0 1
0 0 0 -0.6 0 0
0 0 0 -0.8 0 -1
[C] {x} = {b}
Linear system of equations
C =
b =
0
0
0
0
-1200
0
Notes: If we want to solve this problem numerically in MATLAB, we need to identify the unknowns as the components of an unknown column vector {x} and write our six pin equilibrium equations as a linear system of equations [C]{x} = {b} , where {b} is a column vector of known values and [C} is a matrix of values.

## Slide 12
In MATLAB
Ax
Ay
Cy
FAB
FAC
FBC
C= [ 1 0 0 0.6 1 0;
0 1 0 0.8 0 0;
0 0 0 0 -1 0;
0 0 1 0 0 1;
0 0 0 -0.6 0 0;
0 0 0 -0.8 0 -1]
C =
1.0000 0 0 0.6000 1.0000 0
0 1.0000 0 0.8000 0 0
0 0 0 0 -1.0000 0
0 0 1.0000 0 0 1.0000
0 0 0 -0.6000 0 0
0 0 0 -0.8000 0 -1.0000
b=[ 0 0 0 0 -1200 0]'
b =
0
0
0
0
-1200
0
C\b
ans =
-1200
-1600
1600
2000
0
-1600
Note that we never had to consider equilibrium of the entire structure as we did in the previous solution. This is because if every part of the system is in equilibrium, then the entire system must be in equilibrium.
Notes: Here we see the matrix [C] being defined in MATLAB as well as the vector {b}. We then can solve this system of linear equations for {x} by entering C\b in MATLAB, which then does the solution and returns the column vector {x} which we can identify with all the unknowns. Here we never had to write down equilibrium equations for the entire truss since by satisfying equilibrium for all the pins, equilibrium is assured for the entire truss. Thus, by doing the problem in MATLAB this is truly a method of only pins.

## Slide 13
Symbolic Solution with MATLAB
(1)
(2)
(3)
(4)
(5)
(6)
define forces and equations symbolically
Here are the six equations from the three pins
syms Ax Ay Cy Fab Fac Fbc
Eq(1) = Ax +0.6*Fab + Fac == 0;
Eq(2) = 0.8*Fab + Ay == 0;
Eq(3) = -Fac == 0;
Eq(4) = Cy + Fbc == 0;
Eq(5) = -0.6*Fab +1200. == 0;
Eq(6) = -0.8*Fab - Fbc == 0;
Notes: In MATLAB, however, there is a more direct way to solve the truss with the method of pins. First, we define symbols for all the unknowns and then write down all the equilibrium equations for the pins symbolically, placing the results in an equilibrium vector, Eq, as shown.

## Slide 14
S =solve(Eq)
S =
struct with fields:
Ax: -1200
Ay: -1600
Cy: 1600
Fab: 2000
Fac: 0
Fbc: -1600
Sn = double([ S.Ax S.Ay S.Cy S.Fab S.Fac S.Fbc ])
Sn =
[-1200, -1600, 1600, 2000, 0, -1600]
Solve the system of equations symbolically. The result is in a MATLAB structure
these values are still symbolic. Use the MATLAB function double to turn into numerical values
Notes: In MATLAB we can then solve this system of linear equations symbolically with the MATLAB function solve. The symbolic results are placed in a MATLAB structure, S, here, where the fields in S have the symbolic values for the forces. For example, S.Ax has the symbolic value of -1200, etc. We could leave these values in symbolic form but if we ever want to use these values in other numerical calculations, we can convert these symbolic values to numerical ones with the use of the MATLAB function double, as shown.
This example shows the ease with which we can solve truss problems with the method of pins and MATLAB. It is only necessary to write the equilibrium equations symbolically in forms almost identical to how we would express those equations on paper anyway, and then solve those equations with the MATLAB function solve.

## Slide 15
Solving truss problems with the method of pins in this symbolic manner is relatively easy. Most statics texts instead concentrate on the method of sections (which we will discuss shortly) where we do not have to solve as many equilibrium equations to get results for particular forces. However, with software such as MATLAB and its symbolic capabilities we see that the pins solution is very direct. There are homework problems that will allow you to try this symbolic approach with the method of pins for a truss with more members.
Our numerical MATLAB solution to this problem was less efficient than the symbolic approach since we had to set up a rather large matrix for the equilibrium equations even though many elements of that matrix were zero. It can be used, however, when the symbolic algebra capabilities of MATLAB are not available.
Summary
Notes: Some comments on solving truss problems.

## Slide 16
Zero Force Members
A truss may have members which do not carry any loads (zero force members) but which are needed for stability or for other reasons.
A
B
C
D
E
F
G
H
I
1000 lb
500 lb
Can you identify the zero force members?
A
B
C
D
E
F
G
H
500 lb
1000 lb
500 lb
Notes: If we examine the pins of a truss, we may be able to identify members that carry no force (zero force members). Such members do not contribute to the load-carrying capability of a truss, but they may be present for other reasons. Can you identify zero force members in these trusses? Note that there may be other members in the truss where, by the nature of the loading, the forces in those members may also come out to be zero, but to identify those other members we would have to go through the equilibrium equations for the truss explicitly.

## Slide 17
A
B
C
D
E
F
G
H
I
1000 lb
500 lb
the zero force members
A
B
C
D
E
F
G
H
500 lb
1000 lb
500 lb
Notes: In the truss on the left, if we examine pins F, C, and H we see that only members DF, CG, and BH have any horizontal force at those pins, so by summing forces in the x-direction at those pins the forces in those members must be zero. For the truss on the right, at pin D there are no applied forces so the only force acting at that pin in the x-direction is the force in DE and the only force acting in the y-direction is the force in DC, so both those members must be zero force members. At pin F, there is no force in a direction normal to EF and FG other than the force in member CF, so that must be a zero force member also.