## Slide 1
Frictional Forces
Notes: Friction is a common type of reaction force found at rough surfaces that we want to analyze. A frictional force differs from other reaction forces in that it is limited in its size.

## Slide 2
Learning Objectives
Conditions for slipping impending
Conditions for tipping impending
Slipping impending of flat belts or ropes
Examples
Notes: The magnitude of a friction force is limited in its magnitude so that if the force becomes too large a body may lose equilibrium and slide. Similarly, a body might lose equilibrium by tipping, which is another case we will consider. The frictional contact of belts or ropes with rough surfaces also is a case where slipping can occur. A variety of examples will be given.

## Slide 3
Frictional Forces
A frictional surface, unlike a smooth surface, can exert tangential frictional forces as well as normal forces on a body. However, these frictional forces are limited in how large they can get.
Example:
q
rough plane
block of weight, W
N
F
W
q
x
y
if the block begins to slip when
then
If we define the static coefficient of friction
, ms, as
then
when the body begins
to slip
Notes: A block on an inclined rough plane is a classic problem used to describe friction. The plane will exert both a normal force N and a tangential force F on the block. If the angle of the block is increased, there will be a maximum angle θmax at which the block will begin to slide. If we define the tangent of that maximum angle as a static coefficient of friction, μs then it follows that Fmax = μsN when slipping impends.

## Slide 4
Thus, for equilibrium, we must have
When the friction force has reached its maximum value and slipping is imminent (slipping impending)
and the direction of F is opposite to the direction of impending motion
However, having the frictional force required for equilibrium exceeded so the body slips is not the only way bodies in frictional contact can lose equilibrium. It is also possible for the body to tip over.
W
q
Notes: For equilibrium the magnitude of the friction force must be less than the static friction coefficient times the normal force. The direction of the force also must be opposite to the direction in which the slipping motion will begin to occur. In the inclined plane example, slipping is not the only way the block may start to move. The block may also tip if the angle of the plane is too large (and the height of the block relative to its width is too large).

## Slide 5
q
W
W
F
N
d
As long as d > 0 the body will not tip
q
If, when
d =0 then tipping will be impending
W
F
N
d = 0
q1
If
then the normal force would
have to act outside the bottom of the block
for equilibrium. This is not possible so the block will tip.
N
F
W
d
Notes: The normal force and frictional force are resultant reaction forces that act on the base of the block. They came from an unknown distribution of forces on that base. To have moment equilibrium, the line of action of the weight of the block must pass through the base of the block at a distance d from the edge where the normal force N is located along the base. The distance d, however, cannot be smaller than zero (why?) so the angle where d = 0 is the angle at which tipping impends.

## Slide 6
Difference between static and kinetic coefficients of friction
P
W
N
F
F
P
ms N
mk N
no motion
block slides
P
Notes: As shown, if we push a block with a force P then the friction force F will equal P up until it reaches its maximum value where motion impends. Once the motion starts, the friction force drops slightly to a smaller value during sliding where F = μkN, where μk is called the kinetic coefficient of friction.

## Slide 7
2 ft
2 ft
4 ft
P
300-lb block
Determine the maximum force P that can be exerted on the block before motion impends.
(a) assume slipping impending
P
300
N
direction of impending slipping
F = ms N
Example 10.1
Notes: Here is an example where we ask for the maximum force P that can be exerted on the block before motion impends. The type of impending motion is not specified so we must examine all the ways the block can lose equilibrium. Here there are two possibilities. Either the block slides or the block tips. We must analyze both to see which occurs first. If we assume slipping impends, we set the friction force equal to its maximum value and put it is a direction opposite to the impending motion. We find P = 150 lb.

## Slide 8
(b) assume tipping impending
P
300 lb
N
F
direction of impending tipping
O
4 ft
1 ft
alternatively:
P
300 lb
N
F
4 ft
1 ft
O'
d
so d = 0 when P = 75 lb
+
+
Notes: If we assume tipping impending, we can place the normal force at the front edge of the block since as P increases it will tend to tip the block about that edge. We can then solve for P =75 lb. Alternatively, we could examine the distance d from the point at which N acts to the edge as a function of the load P and solve for P when d = 0.

## Slide 9
In some cases, there may be more than one way a system can lose equilibrium by slipping
Find the smallest force P at which sliding impends.
free body diagram for A
T
N
0.2N
A
100 lb
4
3
100 lb
60 lb
20 lb
m = 0.2
m = 0.25
m = 0.2
4
3
P
A
B
C
Example 10.2
Notes: Now consider a set of blocks that are in frictional contact with each other and the floor and we apply a force P to the center block. It is obvious that block A cannot slide since it is held by an inclined string. But B could slide relative to both A and C (with C remaining stationary) or blocks B and C could slide together as a unit relative to block A and the floor. We must examine all possibilities. First, we examine a free body diagram of A . Regardless of the impending motion of B and C the frictional force between A and B will have to be at its maximum value but note since B will be sliding in either case to the left the frictional force A exerts on B must be to the right. However, in this free body diagram we are showing the frictional force that B exerts on A, so it must be to the left. Another way to see that the direction shown is correct is to note that when B starts to move it will tend to drag block A to the left. From equilibrium we can find the normal force that B exerts on A.

## Slide 10
possibility 1: B moves alone
B
87 lb
(0.2)(87) lb
N1
0.25N1
60 lb
P
we know both forces
from equilibrium of A
Notes: Now consider the first possibility where B moves alone. In this case we must have the maximum frictional forces developed between B and A and between B and C and they must be opposite to the impending motion, which is to the left. We can use equilibrium to find the load P = 54.2 lb when this motion impending occurs.

## Slide 11
possibility 2: B and C slide together
87 lb
(0.2)(87) lb
60 lb
20 lb
P
N2
0.2N2
we know both forces
from equilibrium of A
Notes: Now consider the case when B and C move together and draw a free body diagram of that combination. Now the maximum frictional forces are developed between B+C and block A and B+C and the floor. Again, their directions are opposite to the impending motion, In this case we find P = 50.8 lb, which is slightly smaller than the previous value calculated so this is the largest load we can apply before motion impends. Note that since the values are not too different there is no way we could come to this conclusion without examining both possibilities.

## Slide 12
Find the maximum distance d that a 75 kg person can climb before the ladder slips if (a) m = 0.25 at all surfaces, (b) m =0.25 at the wall and m = 0.4 at the floor. Neglect the weight of the ladder.
part (a)
N1
F1 = 0.25 N1
N2
F2 = 0.25 N2
60o
d
mg = (75)(9.81) = 735.5 N
5 m
A
+
Example 10.3
(a)
d
75 kg
60o
5 m
Notes: Here is a typical friction problem. When the ladder begins to slip the frictional forces at both the ground and the wall must be exceeded and the directions of the friction forces must be as shown in the free body diagram. Applying equilibrium, we find d = 2.33 m when both coefficients are the same.

## Slide 13
part (b)
N1
F1 = 0.4 N1
N2
F2 = 0.25 N2
60o
d
mg = (75)(9.81) = 735.5 N
5 m
A
+
Notes: In this case there is a larger coefficient of friction at the ground, so the distance d is larger than before, which is reasonable.

## Slide 14
The force P pushes on a block of weight W. The coefficient of static friction between the block and the plane is m. Motion is assumed to be impending up the plane:
using MATLAB, solve the equilibrium equations symbolically and obtain the force, P, as a function of W, m, and q for motion impending up the plane
Let W = 50 lb, m = 0.4. Plot the force P required to have motion impending as a function of the angle q from zero to 45 degrees
What is the maximum angle that q can have and still produce impending motion up the plane with a finite pushing force, P ?
(take m = 0.4 again)
30o
q
P
W
m
Example 10.4
Notes: MATLAB can be used effectively to solve friction problems symbolically and numerically. This example of trying to push a block up the plane is used to show the calculations.

## Slide 15
Declare symbols
Define two equations
Solve equations for N, P
P
N
P (better form)
N (better form)
part (a) answer
syms N P W mu t
Eq(1) = N -cosd(30)*W - P*sin(t);
Eq(2) = P*cos(t) - mu*N - W*sind(30);
S = solve(Eq, N , P)
S =
struct with fields:
N: (W*sin(t) + 3^(1/2)*W*cos(t))/(2*(cos(t) - mu*sin(t)))
P: (W + 3^(1/2)*W*mu)/(2*(cos(t) - mu*sin(t)))
part (a)
pretty(S.P)
W + sqrt(3) W mu
----------------------
2 (cos(t) - mu sin(t))
pretty(S.N)
W sin(t) + sqrt(3) W cos(t)
---------------------------
2 (cos(t) - mu sin(t))
30o
q
P
W
N
mN
from equilibrium normal
and tangential to the plane
n
t
Notes: Here we define all the variables symbolically . Note that the angle t = θ is in radians. We define the two equilibrium equations and solve them symbolically for N and P. We use the pretty function to give the symbolic results in a more readable form.

## Slide 16
Substitute W, m values
P as a function of t = q
Make vector of angles (rad)
Substitute angles
Plot
Alternatively, we can do all substitutions at once
angr =linspace(0, pi/4, 100);
Pn2 =subs(S.P, {W, mu, t}, {50, 0.4, angr});
plot(angr*180/pi,Pn2)
xlabel(‘ Angle, degrees’)
ylabel(‘Force, P (lb)’)
Gives same plot
0
5
10
15
20
25
30
35
40
45
40
50
60
70
80
90
100
Angle, degrees
Force, P (lb)
Must put values in a cell array
Pt = subs( S.P , { W , mu} , [50, 0.4])
Pt =
(20*3^(1/2) + 50)/(2*(cos(t) - (2*sin(t))/5))
angr = linspace(0, pi/4, 100);
Pn = subs( Pt, angr);
plot(angr*180/pi , Pn)
part (b)
Notes: To find the value of the load P for specific values of the weight and coefficient of friction we need to substitute them in the symbolic expression for P, which gives us a symbolic expression as a function of θ only. Then if we generate a series of angles (in radians) from 0 to 45 degrees we can substitute those values into the P expression and plot it. We can do all the substitutions at once but then we are substituting both scalar values and a vector so we must place all those into a cell array indicated by the brackets { }.

## Slide 17
part (c)
or
P goes to infinity when
Notes: If we make the angle θ too large then any finite P cannot push the block up the plane (this is obvious the case when θ = 90 degrees, for example). To find the maximum angle, find the angle when P goes to infinity, which occurs at approximately 68.2 degrees.

## Slide 18
q
r
q
r
W
The coefficient of friction is m at all surfaces. Design this broom holder so that no matter what the weight, W, of the broom, the broom cannot drop (self-locking). Neglect the weight of the small cylinders.
W
N1
N1
F1
F1
free body diagram of broom
(by symmetry)
+
Example 10.5
Notes: Here is a design problem where we want to make a broom holder so that it can support a broom under conditions that guarantee it cannot slip, a situation that is called self-locking. If we look at a free body diagram of the broom, we can use the symmetry of the load to relate the friction force holding the broom to the broom weight.

## Slide 19
free body diagram of left cylinder
q
r
N1
F1 =W/2
q
O
N2
F2
A
d
d
from the first Eq.
(second Eq. gives
which is the same value)
+
+
or
we can only use one of these equations because we have only 3 independent equations of equilibrium here
+
+
Notes: Since the system is symmetric, we only need to examine one of the cylinders. We have three equilibrium equations here where it is convenient to use two moment equations and a force equation to solve for the normal forces on the cylinder.

## Slide 20
broom will never slip if
F1 = F2 < m N2 = m N1
or
0
10
20
30
40
50
60
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
q
sin(q)/(1+cos(q))
Notes: There will never be slipping of the cylinder either on the inclined surface or the contact surface with the broom if the friction force does not reach its maximum value, a condition which tells us that the static coefficient of friction must be greater than a given function of θ. Plotted is the value of that function, which shows us the coefficient needed so that the mechanism is self-locking.

## Slide 21
Each cylinder has a 10 in. diameter and weighs 100 lb. m = 0.4 at all surfaces. Determine the maximum allowable load P before the cylinders move.
P
A
B
C
60o
The cylinders B and C must both slide at their contact points with A.
Whatever happens to C must happen to B by symmetry
First look at whole system to find a relationship between P and N for C
P
N
N
F
F
B
10"
summing moments about B
100 lb
100 lb
100 lb
+
Notes: Consider a set of stacked cylinders where we push on the cylinders and cause them to move. First examine equilibrium of the entire stack to relate the normal forces at the floor to the applied load. These forces as well as the friction forces must be equal by symmetry.

## Slide 22
Now, examine C
O
An
0.4An
100 lb
0.5P +150
30o
Cf
Assume that slipping only occurs at the top
Notes: Because of symmetry we do not need examine both B and C so consider C. Since A must move vertically down when equilibrium is lost, A must slide on both B and C so we have shown slipping impending at the contact with A. At the floor, however, there are two possibilities. Either C will also slip at the floor or else it will simply roll to the left on the floor to allow A to drop. Let us assume that it rolls at the floor and determine the friction force at the floor needed for such rolling to occur. We can relate this friction force to the normal force An at the contact with A, and also write An in terms of P.

## Slide 23
Finally, look at A
P
100 lb
0.4An
0.4An
An
An
30o
putting
into the above equation and solving for P
gives
Then
Notes: Now, if we look at A we see that we can also develop another equation for An and P so we can use this equation together with the one developed from the free body diagram of C to find An and the load P. We also can now find the friction force Cf at the floor as well as the normal force N there.

## Slide 24
O
100 lb
N =200 lb
30o
42.29 lb
Check: mN = (0.4)(200) = 80 lb > 42.29 lb so C (and B) must roll, not slip at the floor while sliding on A, as assumed at P = 100 lb
Here is C under our assumptions
Notes: Here are all our forces on C at this point. A check will show that the friction force at the floor satisfies Cf < μN so there is no slipping at the floor as we assumed and so our solution P = 100 lb is correct. If the maximum friction force was exceeded, we would have to rework the problem with slipping also assumed at the floor and find a new value for P.

## Slide 25
A carpenter pushes horizontally on a long board and holds it up to keep it from tipping . The board has a uniform weight of 3 lb/ft and the saw horse has a weight of 15 lb and a center of gravity at G. Neglect the width of the top of the saw horse. As the carpenter increases the horizontal force she (he) applies, determine how the system loses equilibrium and the value of the horizontal force.
18 ft
10 ft
m = 0.5
1 ft
1 ft
3 ft
m = 0.3
G
Example 10.6
Notes: Here is the problem of a carpenter pushing on a long board. Before we start this problem, ask yourself how many ways are there that equilibrium can be lost for this system? What are they?

## Slide 26
(a) assume the board slides on the saw horse
54 lb
Px
1 ft
N
F = 0.5N
Py
+
A
(b) assume the saw horse slides
Px
48.6 lb
15 lb
N1
F1 = 0.3N1
N2
F2 = 0.3N2
force needed to keep board from sliding
force needed to keep
saw horse from sliding
9 ft
Notes: Let’s first assume that the board slides on the saw horse. From a free body diagram (FBD) of the board we find we need to have a horizontal force of 24.3 lb. If instead, we assume the saw horse slides at the floor we need 19.08 lb. Note the horizontal force at the top of the horse is just the pushing force from the carpenter. Why is it directed as shown?

## Slide 27
(b) assume the saw horse tips
Px
48.6 lb
15 lb
N2
F2
B
3 ft
1 ft
Thus, the saw horse will slide at Px = 19.1 lb
force needed to keep saw horse from tipping
Notes: Now, lets assume the saw horse tips. In that case the left leg begins to lift, so the force there is zero. In this case we need 21.2 lb. Thus, the saw horse will slide on the floor at a 19.1 lb push.

## Slide 28
A person holds a stack of books by applying compressive forces of 80 N to the ends of the stack. The mass of each book is 0.95 kg and the coefficient of friction between the person's hands and the books is 0.6. The coefficient of friction between any two books is 0.4. Determine the largest number of books that can be supported.
Let n = the number of books that can be supported. There are two possibilities:
(a) all of books except the two in contact with the hands slip out
mg(n-2)
80 N
80 N
(0.4)(80) = 32 N
32 N
Example 10.7
Notes: Consider now the problem of holding a stack of books by pressing them together. Again, we need to decide what the possible ways are that the system can lose equilibrium. Certainly, it is possible that the entire stack could slide from the hands. Or, only some of the books in the stack could slide out from the others. But note that the coefficient of friction is the same between all the books so certainly the weight of the total stack minus the two held by the hands would cause the stack to slide before any smaller number of books would. Thus, consider first the possibility that all the books except the two in contact with the hands slip. In that case we can only support n = 8.87 books but n must be an integer so n = 8 is the maximum we could support.

## Slide 29
(b) all the books slip out of the hands
mg(n)
80 N
80 N
(0.6)(80) = 48 N
48 N
Thus, 8 books at most can be supported
Notes: Now assume all the books slide from the hands. In that case we get n =10 when rounded down so at most we can have is n = 8 books.

## Slide 30
A 10 foot long chain that weighs 0.5 lb/ft is draped a distance ,d, over the edge of a rough inclined plane. The coefficient of friction between the plane and the chain is 0.3. Assume the upper edge of the plane is rounded and smooth so that the tension in the chain is fully transmitted around the corner. Determine the largest and smallest values that d can have for the chain to be in equilibrium.
3
4
d
Example 10.8
Notes: Consider a 10 ft chain that is draped over an inclined rough plane. If we drape too much chain over the top edge the amount hanging down can pull the chain up the plane. If we drape too little of the chain over the edge, the weight of the chain on the inclined rough surface can pull the entire chain down the plane. We want to find the range of values for d that can prevent either of those losses of equilibrium to occur.

## Slide 31
T =0.5d
10-d
(a) assume slipping impends up the plane
N
3
4
0.5(10-d)
x
y
T
(0.5)(d) lb
0.3N
Notes: Let’s assume slipping impends up the plane. Then the FBDs of the chain on the plane and the hanging portion are as shown. The tension T is the same because we assumed the top edge was rounded and smooth. In that case the tension is transmitted unchanged as we go around the edge. If we sum forces on these diagrams, we find d = 4.57 ft.

## Slide 32
T =0.5d
10-d
(a) assume slipping impends down the plane
N
3
4
0.5(10-d)
x
y
0.3N
same as before
Thus, for equilibrium we must have 2.65 < d < 4.57 ft
T
(0.5)(d) lb
Notes: Now, assume instead that the chain has slipping impending down the plane. In this case equilibrium gives us d = 2.65 ft. Thus, to stay within these two possible ways to lose equilibrium we must have 2.65 < d < 4.57 ft.

## Slide 33
Flat belts or ropes in contact with rough surfaces
b
TL
TS
x
y
T
T+dT
dN
dF
dq/2
dq/2
dq/2
dq/2
ds
so that the above equations become
q1
q2
Notes: Consider a flat belt or rope in contact with a rough curved surface over a region defined by the angle θ1 and θ2 . If we examine a very small segment dθ of the contact region the FBD on the right shows that the small normal force dN and small friction force dF are related to the tension T and its small change dT. This shows us that the friction is taking up some of the tension in the rope.

## Slide 34
when slipping is impending
so
Notes: When this little element is at the verge of slipping, we have dF = μdN so we get a relationship dT/T = μdθ that we can integrate over the angular extent, β , of the contact region between the rope and the surface to obtain TL/TS =exp(μβ) where TL is the larger and TS is the smaller tension on either sides of the contact region. Thus, we now have a relationship that tells us the difference of the two tensions in the rope when slipping is impending.

## Slide 35
2000 lb
TS
Consider a rope which is wrapped twice around a post for which m = 0.5. If TL = 2000 lb, find Ts.
Example 10.9
Notes: Consider a rope wrapped twice around a post where we want to support a tension of 2000 lb on one side of the post with a smaller tension, TS, before slipping occurs. Here the angular extent is 4π so the relationship we just found gives TS = 3.8 lb. Thus, we can hold a very large force in this manner by letting the friction carry most of the tension.

## Slide 36
Example 10.10
Consider the previous chain problem and let coefficient of friction be 0.3 around the corner, with full contact of the chain and surface.
T
(0.5)(d) lb
T1
10-d
N
3
4
0.5(10-d)
x
36.87o
53.13o
126.87o
y
0.3N
(a) assume slipping impends up the plane
Notes: Let us revisit the problem of a chain draped over the edge of an inclined plane but now let us assume the chain is in full contact with a rough corner with the same static coefficient as the plane. In this case the tension changes around the corner. If we assume slipping occurs up the plane, then T > T1 and we can use our relationship in conjunction with equilibrium to find d = 6.2 ft.

## Slide 37
T1
10-d
(a) assume slipping impends down the plane
N
3
4
0.5(10-d)
x
y
0.3N
same as before
Thus, for equilibrium we must have 1.56 < d < 6.2 ft
Recall, without friction we had
2.65 < d < 4.57 ft
Notes: If motion impends down the plane, then T1 > T so when we use our relationship and equilibrium, we find d = 1.56 ft. Thus, we must have 1.56 < d < 6.2 ft. This makes sense. We can drape more of the chain over the edge (in comparison to the smooth case) before the chain is pulled up the plane since the friction is working with the weight of the chain on the inclined surface to oppose the amount of weight draped over the edge. On the other hand, the weight of the draped portion of chain works with the friction to prevent the remainder of the chain sliding down the plane so we need less chain draped over the edge for equilibrium.