## Slide 1
Equilibrium, Reactions and Free Body Diagrams
Notes: This section will lay the foundations for solving static equilibrium problems

## Slide 2
Learning Objectives
Equilibrium Equations in 3-D and 2-D
Reaction Forces
Free Body Diagrams
Notes: We will define the equilibrium equations for rigid bodies and examine the various types of constraint (reaction) forces that can exist at supports. The free body diagram concept will be discussed.

## Slide 3
Equilibrium
A system of forces and couples acting on a body is said to be in equilibrium if the resultant of the force system is zero.
For a general system of forces and couples equilibrium implies
which is equivalent to six scalar equations
where
x
y
z
ex
ey
ez
Notes: Equilibrium of a body is when the resultant force and moment acting on the body are both zero. In three dimensional problems this is equivalent to six scalar equations of equilibrium for the components of the resultant force and moment.

## Slide 4
2-D Equilibrium
For 2-D force-couple systems
the only non-zero equilibrium equations are the three scalar equations
x
y
Note that the point we take moments about for either 2-D or 3-D systems is arbitrary. If we satisfy equilibrium
where moments are taken about a point P, then it is easy to show that equilibrium is satisfied for moments taken about any other point Q:
Notes: In two-dimensional (coplanar) problems, there are only forces acting in a plane and moments acting normal to that plane so there are only three equations of equilibrium. Note that we only need to guarantee that the resultant moment is zero only about one point since if that is true and the resultant force is also zero then the resultant moment about any other point will also be zero.

## Slide 5
Equilibrium Equations
In applying these equations, we must include all forces and couples acting on a body. These are usually of two types:
(1) applied forces or couples, some or all of which may be known
(2) reaction forces or couples which arise from the body interacting with other bodies. These are generally unknown.
To ensure that we have included all the forces and couples in the equilibrium equations we typically remove all the physical interactions of a body with other bodies and replace them with equivalent reaction forces and couples. A diagram of all the forces acting on the body is called a free-body diagram.
We can use the free body diagram(s) to directly solve an equilibrium problem
if we include all the pertinent dimensions in the diagram(s).
Notes: The equilibrium equations must include all the forces and couples acting on a body. These include applied forces, such as gravity, as well as reaction forces which come from the attachment of the body to other bodies. Thus, when applying equilibrium equations one usually first draws a diagram of all the forces and couples on the body under consideration. This is called a free body diagram (FBD) since we include the reaction forces by imagining we have cut off (i.e., freed) the body from its supports. Normally, we also place in the free body diagram all the dimensions needed to solve the problem.

## Slide 6
Reaction Forces and Couples
Reaction forces and couples between bodies always occur in equal and opposite pairs if every body in a system of interconnected bodies is in equilibrium:
300 lb
Example 1: consider a simply supported beam. Solve for the reactions at the supports
300 lb
A
B
A
B
5 ft
5 ft
5 ft
5 ft
+
+
+
x
y
This is a free-body
diagram of the beam !
A
B
Here are the equal
and opposite reaction forces acting on
the ground. This is not a free body diagram. Why?
Notes: Here is a simple example of drawing a FBD for a beam and solving for the unknown reaction forces. Since the forces A and B are the reaction forces that the ground exerts on the beam, there are equal and opposite forces that the beam exerts on the ground. The problem is symmetrical so we could have written down the reactions directly as each being half the applied force.

## Slide 7
Now, imagine cutting the beam at 3 ft from A. Find the internal force and moment acting in the beam at that point
150
300
3 ft
2 ft
5 ft
V1
M1
V2
M2
150
A
+
+
+
+
This is a free-body
diagram
B
these are internal reaction forces and couples
Apply equilibrium to both parts
This is a free-body
diagram
Notes: The forces A and B in the previous example were external reaction forces we obtained by cutting a body from its external supports. But we can also imagine cutting a body itself into parts and examining the equilibrium of each part. This will require including internal reactions. For the beam we need to have an acting internal force (called a shear force) and an internal couple (called a bending moment). Again, these reactions always occur in equal and opposite pairs since these internal reactions must cancel when we put the beam back together. We see that we can apply equilibrium to either part and obtain the shear force and bending moment. This proves that the internal reactions are indeed equal and opposite.

## Slide 8
150
300
3 ft
150
450
150
450
150
A
B
2 ft
5 ft
300 lb
150
150
5 ft
5 ft
the system in parts
the system put back together
Notes: Here are free body diagrams of the cut beam and the entire beam with all the forces and couples acting that are in equilibrium.

## Slide 9
Example 2
smooth
50 lb
25 lb
200 lb
whole system
200 lb
50 lb
25 lb
T1
N1
N2
25 lb
T1
N1
200 lb
50 lb
N2
individual
parts
(and the rope)
T2
T2
T2
T2
Notes: Here is a problem where a 200 lb horizontal force is applied to one of two blocks that are connected to each other and to a wall by horizontal ropes and are sitting on a smooth (frictionless) surface, We want to draw FBDs of the system of both blocks and the individual blocks. Since the surface is frictionless it can only exert a vertical (normal to the surface) force on either block. The system of both blocks thus shows these normal forces and the reaction force T1 , which the rope exerts on the 25 lb block, and the two weights. Note that the rope is in tension so that it must always pull on the 25 block to the left. It cannot push on the block (unless it was frozen like a brick, of course). When we look at the individual blocks we also see the tensions that the middle string exerts on the blocks. These again occur in equal and opposite pairs which we can see clearly by also showing the FBD of the rope itself between the blocks, where the forces at the rope ends by equilibrium must be equal and opposite.

## Slide 10
75 lb
whole system
75 lb
A
FAx
MA
individual parts AB and BC
FAx
MA
B
20 lb
FAy
FAy
20 lb
75 lb
20 lb
FBy
FBy
FBx
FBx
MB
MB
FAx
MA
FAy
reactions on the wall
(not a FBD)
C
Example 3
fixed (built-in)
support
Notes: Here is a slightly more complex example of FBDs for a L-shaped beam where the beam is “built-in”, i.e., fixed, to a wall. In this case the wall must exert both forces on the beam (to prevent its motion in the horizontal and vertical directions) as well as a couple to prevent the beam from rotating. We could solve for those wall reactions by equilibrium. If we imagine taking a cut through the beam at B we will also expose internal reaction forces and a couple at B, which are show for both parts of the cut beam. Again, these occur in equal and opposite pairs, and we can also find those internal reactions from equilibrium.

## Slide 11
Typical supports and the types of reactions
they generate
wire or rope
q
q
T
T
smooth surface
q
N
N
q
q
smooth roller or pin on rollers
N
rocker
N
Notes: Here we show some of the common types of external supports we will consider. A wire or rope, as shown, always exerts a tension on a body. The magnitude of the tension is unknown but the direction, which is along the wire or rope, is usually known. For a smooth surface acting on a body, the force exerted must be normal to the surface at the point of contact (by being smooth it cannot provide a force along the surface to prevent motion) so its direction is usually known. Note that the normal force must always push on the body, i.e., be positive when drawn as shown. For a body in contact with the ground by a smooth roller, a pin on smooth rollers, or a smooth rocker the force must be normal to the ground.

## Slide 12
smooth pin
x
y
Ax
A
Ay
z
x
y
y
z
x
z
x
y
y
z
x
Rx
Ry
Ry
Rx
Rz
Rx
Rx
Ry
Ry
Rz
Mx
Mx
My
My
(a)
(b)
(c)
(d)
bearings
smooth bearing in
alignment
with end stop
smooth bearing
not in alignment
smooth bearing
in alignment
smooth bearing not
in alignment with
end stop
Notes: At a smooth pin (shown for a two-dimensional problem) the pin can exert forces in either the x- or y- directions. For a smooth bearing and shaft in alignment in three dimensions there can only be forces in plane perpendicular to the z-axis of the bearing, so it acts like a smooth pin in two dimensions. If, however, we put a stop on the smooth bearing in alignment, the stop also allows us to support a force along the shaft as well. When a smooth bearing is not in alignment (which is not a desirable situation since such non-alignment causes bearing wear) there can be couples exerted on the bearing as well, as shown, in the x- and y- directions. There cannot be a couple supported in the direction of the shaft (the z-direction) since the bearing is assumed to be smooth (well-lubricated). If there is friction in the bearing, however, then we can support a couple in the z-direction. If there is an end stop in the non-aligned bearing, then it also can support a force in the z-direction along the bearing axis.

## Slide 13
x
y
z
(c) hinge not in alignment
(d) hinge not in alignment,
axial stop
(b) hinge in alignment,
axial stop
(a) hinge in alignment
Hinges have cases similar to the bearing cases
Notes: Hinges, like bearings can be either in alignment or not and may include an end stop.

## Slide 14
smooth ball and socket joint
x
y
z
Rx
Ry
Rz
smooth ball support
N
Notes: Here are some more three-dimensional supports. A smooth ball between a surface and the body, for example, can only support a normal force to the surface. If we have a smooth ball and socket joint, the joint allows us to support forces in all three directions ( since it usually consists of a sphere in smooth contact with a surrounding cup) but it cannot support couples.

## Slide 15
fixed (built-in) support
x
y
z
Rx
Ry
Rz
Mx
My
Mz
fixed (built-in) support
(coplanar force system)
x
y
Ry
Rx
Mz
Notes: A fixed (‘built-in”) support can prevent translations or rotations in any direction so it can support three forces and three couples, in general. For coplanar problems, as we have considered previously, we can support two forces in the x-y plane and a couple in the z-direction.

## Slide 16
Two-force member (weightless link) in equilibrium
A
B
Let there be smooth pins at A and B which connects the link
to other bodies. Then there can be only forces at A and B acting on the link.
If there are no external forces or couples acting on the link (other than at A and B) and if the weight of the link can be neglected, then the forces at A and B are equal and opposite and directed along the line AB
Notes: A two-force member (also called a “weightless link’) is a member whose weight can be neglected is only connected to other bodies by two smooth pins at A and B (there can be no other forces acting along the link). As we will see on the next slide the forces at A and B must then be equal and opposite and act along the line AB.

## Slide 17
A
B
FA
FB
rAB
From equilibrium of forces
FA + FB = 0
FA = - FB
From equilibrium of moments about A
rAB x FB = 0
rAB is parallel to FB
A
B
FB
-FB
two force member (weightless link)
Notes: Here is a proof of the fact that forces at A and B must be equal and opposite and acting along AB if the link is to be in equilibrium. Note, however, unlike a wire or rope the forces at A and B can be stretching the member, as shown, or they could be compressing the member so the member can be either in tension or compression.

## Slide 18
Three-Force Member in Equilibrium
If three forces act on a body and are in equilibrium , then from the parallelogram law these forces must add up to zero and all lie in a common plane, as shown. From moment equilibrium d = 0 so these forces must all go through the same point, i.e., they must be concurrent.
plane containing F1, F2, F3
A
d
A
(a)
(b)
(c)
Notes: A three-force member is where a body is acted upon by only three forces. In this case the forces must form a concurrent system, i.e., their lines of action must all pass through a common point.

## Slide 19
wire or rope over a pulley on a smooth axle of rotation
A
+
if the axle of rotation at A was either rough or locked to prevent rotation, there
would also be a couple at A and then the tensions need not be equal
Notes: The last example we will give is a wire or rope which runs over a smooth pulley. The wire must always be in tension so the forces T1 and T2 must be as shown, but if we draw a FBD of the pulley and wire and sum moments about the smooth bearing of the pulley, we see the tensions on either side of the pulley must be equal. For a pulley with friction in the pin at A or where the axle of the pulley at A was locked the tensions might be different if the pulley wheel is not smooth, a case we will examine when we consider frictional forces.