## Slide 1
Solving Equilibrium Problems -II
Notes: In this section we will study the main topic in Statics, namely how to use free body diagrams (FBDs) and the equations of equilibrium to determine the forces and/or couples that are acting on a body.

## Slide 2
Learning Objectives
Equilibrium with Multiple Free Body Diagrams
MATLAB solutions
Notes: We will see examples where we typically must break a system of bodies up and use multiple FBDs to solve for the unknown forces or couples. MATLAB will be shown to be of great value in these efforts, using either a direct numerical approach, or in solving problems symbolically and then turning the symbolic results into numerical answers.

## Slide 3
Since in the most general case we have six equations of equilibrium, that must be satisfied for a body it would appear that we could at most solve for six unknown forces or couples. However, these six equations of equilibrium must apply also to every part of the body. Thus, in fact we can solve for many more than six unknowns.
Notes: For any one body we have six possible non-trivial equations of equilibrium – three force equations and three moment equations. Of course, in many problems we will not need all these equations since some may be automatically satisfied. Since we can take moments about different points, in some cases we can substitute one or more moment equations for the force equations. However, we still can only use at most six equations total.

## Slide 4
For a coplanar force system there are only three non-zero equilibrium equations
Consider the following structure, where there are two bars, each weighing 100 lb, and an applied force of 200 lb acting on the pin at B. The bars are attached to each other and to the floor via smooth pins. Determine the forces in the bar and the external reactions on the structure.
200 lb
A
B
C
6 ft
8 ft
Example 4.1
Notes: For two-dimensional problems, there are only three equilibrium equations we can use – two force equations and one moment equation. We will begin by analyzing such a coplanar system. Consider, for example , the problem of two bars that are pinned to each other and to the floor through smooth pins and where a 200 lb force acts as shown. We want to find the forces in the bars and the external rection forces.

## Slide 5
If we look just at the entire structure, it would appear we cannot solve for all the unknown reaction forces since there are four of them
200 lb
Ax
Ay
Cx
Cy
x
y
However, now break the system up into parts
100 lb
100 lb
Notes: If we look at a FBD of the entire structure, we see there are four unknown reaction forces but only three equations of equilibrium, so it appears we cannot solve for all these forces (Note, however, we can solve for some of them (which ones?). However, by breaking the system up we will see we can solve for all the unknowns.

## Slide 6
200 lb
Ax
Ay
Cx
Cy
100 lb
100 lb
Bx
By
Bx
By
B'x
B'y
B'x
B'y
There now are eight unknown reaction forces.
How many non-zero equilibrium equations are there?
8 ft
6 ft
6 ft
[ Note: study carefully these free body diagrams ]
Notes: Here are FBDs of the two bars and the pin at B. We need to look at the pin because the problem states the 200 lb force is applied there. Note that if there was no force applied to the pin we need not draw it since then the force pairs Bx and B’x and By and B’y will always be equal and opposite. Altogether we have eight unknowns.

## Slide 7
Ax
3 eqs. –coplanar
system
2 eqs. –concurrent
system
3 eqs. –coplanar
system
0 = 0
Thus, there are 8 equations and 8 unknowns.
The problem is statically determinate
200 lb
Ax
Ay
Cx
Cy
100 lb
100 lb
Bx
By
Bx
By
B'x
B'y
B'x
B'y
8 ft
6 ft
6 ft
Notes: Looking at the equilibrium equations for the two bars and the pin we see there are a total of eight equilibrium equations, so we have enough equations to solve for all the forces.

## Slide 8
Let's write down these eight equations. For the moment equations we will take moments about point A for the left bar and moments about C for the right bar
Ax
200 lb
Ax
Ay
Cx
Cy
100 lb
100 lb
Bx
By
Bx
By
B'x
B'y
B'x
B'y
8 ft
6 ft
6 ft
We could set up a system of 8 equations and 8 unknowns and solve all of these equations at once, but in that case we would likely have to use some software. But in many problems like this one we can sequentially work our way by hand through the system.
Notes: Here are eight equilibrium equations where we take moments about A and C to get the moment equilibrium equations. We can solve this system of eight equations for the eight unknowns, as we will do shortly, but in some cases, like this one, we can solve the system by hand in a sequence of steps.

## Slide 9
(1)
(1) gives
(3) gives
(6)
(3)
(4) gives
(4)
(5) gives
(5)
(6) gives
(2)
(2) gives
(7)
(7) gives
(8) gives
(8)
Notes: This shows how if we solve these equations in the right order, we can obtain the results directly without solving simultaneous equations. This, however, is not always the case and we may be forced to solve a set of simultaneous equations. Most Statics texts try to avoid solving simultaneous equations but with MATLAB available, such solutions are not difficult to obtain.

## Slide 10
200 lb
200 lb
100 lb
0
300 lb
100 lb
100 lb
0
200 lb
200 lb
200 lb
200 lb
8 ft
6 ft
6 ft
200 lb
0
200 lb
If we put the system back together and look at the entire structure, we see
200 lb
100 lb
100 lb
200 lb
8 ft
300 lb
100 lb
6 ft
By inspection we see the forces are balanced. What about the moments?
Take moments about B
B
so moments are balanced also. This shows that if we guarantee all parts of a structure are in equilibrium, the entire structure must also be in equilibrium
4 ft
Notes: Here is the complete solution drawn for the three free body diagrams we used. If we put the two bars back together, we see a solution for the entire system. Note that we never directly guaranteed the equilibrium of the entire system but if all the parts of the system are in equilibrium, as guaranteed here, then the entire system will also be in equilibrium.

## Slide 11
If we had wanted to solve the entire system of equations we could just write them down in the same order as before:
(1)
(6)
(3)
(4)
(5)
(2)
(7)
(8)
and let
giving
Notes: Now, let us set up the problem as a system of eight equations in eight unknowns, We write the eight unknowns as a 8x1 column vector (eight rows and 1 column) and the equations as an 8x8 matrix of coefficients times that unknown column vector equal to a known 8x1 column vector of forces and moments. Thus, we have placed our system of eight simultaneous linear equilibrium equations in a matrix-vector form ideally suited to solution in MATLAB.

## Slide 12
We can solve this system in MATLAB
First, we enter the
matrix of coefficents
C = [ -6 0 0 0 0 0 0 0;
1 0 1 0 0 0 0 0;
-1 0 0 0 -1 0 0 0;
0 0 0 0 1 0 1 0;
0 0 0 0 -6 8 0 0;
0 0 0 0 0 1 0 1;
0 -1 0 0 0 -1 0 0;
0 1 0 1 0 0 0 0]
C =
-6 0 0 0 0 0 0 0
1 0 1 0 0 0 0 0
-1 0 0 0 -1 0 0 0
0 0 0 0 1 0 1 0
0 0 0 0 -6 8 0 0
0 0 0 0 0 1 0 1
0 -1 0 0 0 -1 0 0
0 1 0 1 0 0 0 0
Notes: First, in MATLAB we need to define the 8x8 coefficient matrix, C

## Slide 13
Then we enter the right hand side column vector
b =[ 0 0 -200 0 400 100 0 100]'
b =
0
0
-200
0
400
100
0
100
Notes: Then we need to write the known 8x1 column vector, b, on the right side of these equations.

## Slide 14
Then we solve this system of
8 linear equations
C\b
ans =
0
-200
0
300
200
200
-200
-100
Notes: In MATLAB we can directly solve this system by entering C\b. If we identify the eight elements in the x-vector with our unknowns, we then have the solution.

## Slide 15
Solving Equations Symbolically in MATLAB
The previous MATLAB solution required that we turn the equilibrium equations into an equivalent equilibrium matrix and known vector so that we could solve a set of simultaneous equations numerically. But we can also just enter the equations symbolically and solve them in MATLAB. This is a very direct way to solve equilibrium problems.
First, define the eight unknowns as symbols and symbolically enter
the eight equations. Here Bpx, Bpy are B’x and B’y
syms Bx By Cx Cy Bpx Bpy Ax Ay
Eq(1) = -6*Bx == 0;
Eq(2) = Cx + Bx == 0;
Eq(3) = 200 - Bx -Bpx == 0;
Eq(4) = Ax + Bpx == 0;
Eq(5) = 8*Bpy - 6*Bpx -400 == 0;
Eq(6) = Ay + Bpy -100 == 0;
Eq(7) = -By - Bpy == 0;
Eq(8) = Cy + By -100 == 0 ;
Notes: In the previous MATLAB solution we had to 1) translate the unknowns into specific elements of an x-vector, 2) place the known terms in a b-vector, and 3) put the coefficients of the unknowns in the 8x8 matrix C. Here, we will show we can do the problem in MATLAB much simpler by just declaring our eight unknowns as symbols and then writing our eight equations symbolically in exactly as the same form as they originally appeared. Each of these equations are placed in a MATLAB symbolic vector (called Eq) which has eight components.

## Slide 16
Next, solve these eight equations. The results are placed in a MATLAB structure S
S = solve (Eq)
S =
struct with fields:
Ax: -200
Ay: -100
Bpx: 200
Bpy: 200
Bx: 0
By: -200
Cx: 0
Cy: 300
NS = double( [ S.Ax S.Ay S.Bpx S.Bpy S.Bx S.By S.Cx S.Cy])
NS =
-200 -100 200 200 0 -200 0 300
these values are still symbolic so if we want to make these values numerical we need to use the function double:
Here is a vector of the numerical values
Notes: Then we can simply solve these eight equations symbolically with the MATLAB solve function. The result is placed in S which is a MATLAB structure that contains eight fields with the symbolic values of the symbolic variables (You can look up the MATLAB documentation if you want to understand more about MATLAB structures. For our purposes we only need to know how to access the elements, which we will now address). Each symbolic variable in the S structure can be accessed by writing S followed by a dot and the symbolic name of one of the unknown variables. For example, typing S.Ax will return a symbolic value of -200, which is the value of Ax. If we want to use these values in further calculations, we can convert the symbolic values in S to double precision numerical values, which we do with the double function, as shown.
Note the directness of this approach in MATLAB. We can simply place the unknowns and equations in MATLAB in a symbolic form which is very close to how we wrote the equations by hand, and then solve those symbolic equations. We can effortlessly do many Statics problems in this manner that would be very tedious if done by hand or even if done numerically in MATLAB, as we have seen.