## Slide 1
Area Moments
Notes: We have already examined centroids of areas. In this section we will consider another geometrical property of areas called area moments.

## Slide 2
Learning Objectives
Definition of Area Moments
Calculation by Integration
Parallel Axis Theorem
Radius of Gyration
Composite Areas
Values in Rotated Axes
Principal Moments and Principal Axes,
Area Moments with Matrices, MATLAB
Mass Moments of Inertia
Notes: We will define area moments and examine a wide range of topics including their calculation by integration and the use of the concept of composite bodies. We will see how area moments change with translation and rotation of the coordinate axes and compute the axes about which the area moments have their largest and smallest values called the principal moments. We will use matrices and MATLAB to demonstrate effective ways to determine principal moments and their directions. Finally, we will examine related concepts such as mass moments of inertia.

## Slide 3
Area Moments
We have already examined the concept of the location of the centroid of an area, A. We defined the location of the centroid as first moments of an area, given by quantities such as
divided by the total area
which gave the x- and y-coordinates of the centroid as
We can also define second moments of an area in a similar fashion. Ixx and
Iyy called area moments and Ixy is a mixed area moment:
x
y
A
dA
x
y
distance from x-axis
distance from y-axis
Notes: Area moments, like centroids involve integrating products of distances times area except in the case of area moments we use distances squared so these are sometimes called second area moments.

## Slide 4
Ixx is also sometimes written as Ix and Iyy as Iy
These area moments are geometrical properties of an area A and are important in Strength of Materials for relating the internal moment, M(x), acting in a beam to the vertical deflection, v(x), of the beam. In fact
x
z
y
A
where
and E is Young's modulus (a material property). v is the deflection in the y-direction
is a second moment of the cross-sectional area, A, of the beam (in the y-z plane) through the centroid of A
-v
moment-curvature relation
Notes: Area moments appear in problems involving the bending of beams when we relate the vertical deflection of the beam to the internal bending moment acting in the beam. A material property called Young’s modulus also appears in the relation, called the moment-curvature relation (where the curvature of the beam, for small deflections and slopes, is just the second derivative of the deflection curve v (x)).

## Slide 5
Area Moments of some simple areas:
C
x
y
x
y
b
h
For centroidal axes of a rectangle
similarly,
and
C
x
y
-x
y
axis of symmetry
If either the x- or y-axis is an axis of symmetry for an area A then also
for that area
x
y
Notes: For simple shapes like rectangles new can easily calculate the area moments. These are usually tabulated for axes that go through the centroid., as shown here. If one of the axes about which the area product Ixy is being calculated is an axis of symmetry, then Ixy = 0.

## Slide 6
The area moments depend on the choice of axes:
x
x
y
b
h
C
x
y
x
y
b
h
y
Notes: The values of the area moments depend on the choice of axes. For a rectangle we have Ixx = bh3/12 for the x-axis at the centroid while Ixx = bh3/3 for an x-axis at the base. We can combine rectangles to make other important shapes, so it is useful to remember these two specific area moments.

## Slide 7
Area moments of simple area shapes are usually tabulated with respect to centroidal axes. If we want to find area moments with respect to a set of non-centroidal axes that are parallel to a set of centroidal axes where the area moments are known, we do not have to redo the integration but can use the parallel axis theorem
x
y
x'
y'
xc
yc
x',y, are centroidal
axes
parallel axis theorem
similarly
C
y
y'
x
x'
dA
these must be for centroidal axes
Notes: If we have area moments tabulated about a specific set of centroidal axes (as are found in tables) and we want to compute the area moments about a different set of axes that are parallel to the centroidal axes, then instead of doing the integration we can use the parallel axis theorem shown here.

## Slide 8
C
x'
y'
b
h
x
y
h/2
b/2
Notes: Here, for example, is the use of the parallel axis theorem for a rectangle.

## Slide 9
x
y
x
y
b
h
Area Moments by 2-D integration
Example 14.1
Consider the triangular area shown in Fig. 14.6. Compute the area moments with respect to the x- and y-axes shown by (a) two-dimensional integrals and (b) one-dimensional strip integrals. Perform the integrations both by hand and with the use of MATLAB.
Notes: Here is an example of calculating the area moments of a triangular section by 2-D integration.

## Slide 10
Use of strip elements (1-D integration)
x
y
x
b
h
dAs
for dAs:
ls
x
y
b
h
dAs
y
ls
dx
dy
for dAs:
note: can't use
since the strip is distributed over many y-values
Notes: Like with centroids it is useful to use strip elements, so we only have one integration to do. For the first example above, we can’t use the definition of Ixx directly since there are many y values in the strip area, but we can compute the total area moment as a sum of area moments of a thin strip about its own base. For a horizontal strip there is no problem in just using the definition directly. We show calculations for Ixx here, but Iyy calculations proceed in the same manner. Note that for Ixy calculations with a strip elements one must use the fact the Ixy = 0 for centroidal axes of the strip and then use the parallel axis theorem to calculate the Ixy about a different set of parallel axes.

## Slide 11
We can also do these integrals symbolically in MATLAB
syms b h x y
Ixx = int(h^3*x^3/(3*b^3), x, 0, b)
Ixx =
(b*h^3)/12
Ixx = int(y^2*(b -b*y/h), y, 0,h)
Ixx =
(b*h^3)/12
for a vertical strip
for a horizontal strip
Ixy =int(int(y,y,0,h*x/b)*x, x, 0 ,b)
Ixy =
(b^2*h^2)/8
for a 2-D integration
Notes: We can use symbolic integration in MATLAB and do either 1-D or 2-D integrations.

## Slide 12
Radius of Gyration
Given an area, A, and an axis b-b, we can calculate Ib. The radius of gyration, kb , is defined as
b
b
A
kb
Notes: If we take the square root of an area moment divided by an area, we get a length which is called the radius of gyration. This length has a physical meaning in areas such as dynamics.

## Slide 13
Composite Areas
If a cross-section can be decomposed of simpler parts, we can often use the parallel axis theorem to sum up the contributions for each part
A1
A2
A3
b
b
Notes: We saw in the case of centroids we could decompose an area into simpler parts and calculate the centroid for such composite areas directly. In the case of area moments, we can often use the parallel axis theorem to deal with composite areas.

## Slide 14
Example 14.2
Compute Ix and Iy for the I-beam shown.
x
y
2"
3"
3"
2"
A1
A2
A3
d2
d3
3"
3"
2"
Notes: An important example is the case of an I-beam cross section which is composed of three rectangular areas as shown. Using the parallel axis theorem and the formulae for the area moments of a rectangle about centroidal axes we can compute Ixx and Iyy directly. Because the y-axis of the I-beam is an axis of symmetry Ixy = 0.

## Slide 15
Changes of the area moments with rotation of axes
x
x'
y
y'
q
similarly, we find
Notes: The parallel axis theorem tells us how the area moments change as we translate the axes from a set of centroidal axes. If we rotate our axes the area moments will also change. If we relate the coordinates of the two sets of axes in terms of the angle of rotation, we can use the integral definitions to evaluate the area moments in the rotated axes in terms of those in the original axes.

## Slide 16
These relations are often placed in terms of the angle 2q, using
Notes: These relations for how the area moments change with angle of rotation are often written in a different form using the double angle relations from trigonometry.

## Slide 17
Principal Area Moments and Axes
Problem- find the directions along which the area moments Ix'x' and Iy'y' are a maximum or minimum. These are called the principal directions or principal axes and the corresponding area moments are called principal moments.
If Ix'x' is a maximum or minimum then
consider
so
If q = b is a root of this equation then q = b + p/2 is also a root. Thus,
there are two principal directions and they are orthogonal to each other
(we get the same equation if we had considered Iy'y' instead)
Notes: Since the area moments change with the orientation of the axes, we could ask to find those directions where the area moments take on their largest and smallest values. These values are called the principal area moments. We can get an extremum (max or min) if we set the derivative of an area moment with respect to theta equal to zero. There are two angles that satisfy this criterion so the two axes along the largest and smallest values of the area moments, called the principal directions, are at 90 degrees to one another.

## Slide 18
2q
The two principal values of the area moments can be obtained by substituting
into
principal area moments
Notes: Expressions for the principal area moments can be found by placing the solution for the principal directions into the transformation equations.

## Slide 19
If we look at the mixed area moment, Ixy , along the principal directions, i.e. when
is satisfied, we find
becomes
2q
so Ixy is zero for the principal axes
Since Ixy is zero if either the x- or y-axis is an axis of symmetry it follows that if an area A has an axis of symmetry, it must also be a principal axis
Notes: If we examine the mixed area moment, Ixy , along the principal x and y directions we find it is zero. Thus, if an area has an axis of symmetry that axis is also a principal axis.

## Slide 20
Principal Moments - Summary
The values of the principal moments are
The principal directions are the two angle values obtained from solving
for q, q + p/2
But which principal value goes with each angle here?
To determine this correspondence, we can plug a particular q into
and see which principal value appears for
we can solve instead
for the angle associated
with Ip1. Then the other principal area moment is at right angles to this angle
or, as shown in the text
Notes: Here is a summary of the formulae that define the principal area moments and their directions.

## Slide 21
x
y
C
12"
6"
Example 14.3
Determine the principal area moments and the principal directions with respect to the centroid of the triangle shown.
x
C
309.8
50.2
16.850
y
from tables:
and qp2 = 106.15o
Notes: Here is an example of calculation of principal area moments and directions.

## Slide 22
Example 14.4
Determine the principal area moments of the circular area with respect to a set of axes through the origin O and the corresponding principal directions.
x
y
x'
y'
C
dy
dx
a =2"
(2,2)
from tables
O
Notes: In this example we use the parallel axis theorem to calculate the area moments about the x-y axes

## Slide 23
36p
4p
45o
similarly
Notes: We then can use the formulae for the principal area moments and their directions. Note how one axis is an axis of symmetry here.

## Slide 24
q
x
y
x'
y'
The transformation equations for area moments due to a rotation of axes are:
n
t
We can write these relations in terms of the components of the unit vectors n, t acting along the x' and y' axes, respectively, where
Area Moment Matrices
and where ex , ey are unit vectors along the x and y- axes.
ex
ey
1
nx
ny
q
1
tx
ty
q
t
n
Notes: We can write the transformation equations for area moments in matrix terms. This is, as we will see, a very useful way to consider these equations in Matlab.

## Slide 25
We find
These relations can be written in matrix notation as
or
where
is called the direction cosine matrix
cosine of the angle between the x and y' axes,
etc.
Notes: If we form up a matrix of area moment values (note Ixy is placed in the matrix as –Ixy) then we can write the transformation equations as a matrix multiplication of this area moment matrix with so-called direction cosines matrices. The columns of the direction cosine matrix is simply the components of unit vectors taken along the rotated axes.

## Slide 26
Example 14.5
Consider the previous triangle example (in MATLAB). Determine the area moments with respect to a set of rotated axes through the centroid as shown.
Ixx = 288 in4
Iyy = 72 in4
Ixy = -72 in4
[Q] .. direction cosine matrix
remember this is -Ixy
x'
y'
x
C
30 0
y
n
t
q
q
n
t
M=[288 72;72 72]
M = 288 72
72 72
ang=30*pi/180;
n = [cos(ang) sin(ang)]
n = 0.8660 0.5000
t = [-sin(ang) cos(ang)]
t = -0.5000 0.8660
Q=[n' t']
Q =
0.8660 -0.5000
0.5000 0.8660
note that n and t are made to be column vectors here
Notes: Here is an example of the computation of the area moments about a rotated set of axes for the triangular area we considered earlier. We define the area moment matrix and the direction cosine matrix

## Slide 27
Ix'x' = 296 in4
Iy'y' = 64.6 in4
Ix'y' = 57.5 in4
[Mr] = [Q]T [M] [Q]
remember this is -Ixy
>> Mr=Q'*M*Q
Mr =
296.3538 -57.5307
-57.5307 63.6462
Notes: We then can do a matrix multiplication by the direction cosine matrix and its transpose to find the values in the rotated axes.

## Slide 28
It is also very easy to determine the principal values and principal directions in this matrix form of the relations
Suppose we can find a set of coordinates where the unit vectors along the principal axes have components Nx, Ny and Tx ,Ty . Then
where I1, I2 are the principal area moments, and the mixed area moment is zero in the principal axis coordinates
If we multiply both sides of the above equation by [Q] we find, since
which gives
Notes: Matrices are also very useful in obtaining principal area moments and their directions. We know that we have a diagonal matrix in the principal directions which we can relate to the matrix in an original set of x and y axes.

## Slide 29
This is equivalent to the two sets of equations:
Thus, we see to find either the principal area moment I1 and its principal direction N or the principal area moment I2 and its principal direction T we need to solve the system of equations
where the unit vector U can be either N or T and I can be either I1 or I2
Notes: This leads to trying to find a solution to the system of equations shown.

## Slide 30
The system of equations
Since this eigenvalue problem can be rewritten as
which can also be written as
is called an eigenvalue problem, whose solution is a scalar eigenvalue, I, which here corresponds to a principal area moment, and a corresponding eigenvector, U, which corresponds to the components of the unit vector along the corresponding principal direction.
to find a solution we must solve the system of equations
Notes: Solving this system is an example of solving what is called an eigenvalue problem, a problem that shows up in a wide variety of physical problems.

## Slide 31
But this is a homogeneous set of equations which only has the solution U = 0 unless the determinant of the matrix of coefficients is zero, i.e.
Expanding this equation, we obtain a quadratic equation for I:
which has the two roots
which we see are just the principal area moments
Notes: We can write an eigenvalue problem as a homogeneous system of equations which only has a solution if the determinant of those homogeneous equations vanish, a condition that leads to our previous expressions for the principal area moment.

## Slide 32
if we place one of the principal values back into the above system of equations then we can solve for the corresponding principal direction. However, since we have set the determinant of this system equal to zero, the two equations above are not independent. Thus, we can only solve one of them for a ratio of unit vector components. Thus, for example, from the first equation and using I = I1 we have
But since U is a unit vector we have
which we can solve for Uy in terms of the above ratio as
Note: this is equivalent to solving for q via:
Notes: If we place one of these principal values into the system of equations, we can obtain the previous expression we gave for the angle to the principal direction and we can find the components of the unit vector in that direction also.

## Slide 33
and then we can find Ux since the ratio Ux/Uy is known. Note that we only get the vector solution to within a plus or minus sign since both U and –U are principal directions. If we repeat the process for I2 then we can find the second principal direction.
Notes: The unit vectors along a principal direction can only be defined to within a sign of plus or minus one since if, say, the positive x-axis defined a principal direction the –x axes would also define the principal direction.

## Slide 34
It can be shown that the eigenvalues I1 , I2 of the eigenvalue problem
are always real and the eigenvectors U1 , U2 are real and orthogonal to each other since the matrix [ I ] is a real, symmetrical matrix.
Notes: Since the area moment matrix is a real, symmetric matrix, mathematically one can show that the principal area moments are always real values and the principal directions are at right angles to each other, as we showed they should be.

## Slide 35
In MATLAB we can get both principal values and directions directly by just forming up the area moment matrix
and then giving that matrix to the built-in function eig which solves the eigenvalue problem. the MATLAB call is:
[ pdirs, pvals] = eig(M)
The matrix pdirs will then have the principal direction components (in columns) as
Principal Area Moments and Directions as an Eigenvalue Problem
and the matrix pvals will have the corresponding principal values
Notes: Solving eigenvalue problems in MATLAB is very easy since there is a built-in function eig that produces both the principal values and principal directions.

## Slide 36
Example 14.6
Consider our triangle example again:
M = [ 288 72;72 72];
[pdirs, pvals] = eig(M)
pdirs =
0.2898 -0.9571
-0.9571 -0.2898
pvals =
50.2002 0
0 309.7998
atand(pdirs(2,2)/pdirs(1,2))
ans = 16.8450
angle (in degrees)
for 309.8 value
I1 =50.2
U1 = 0.2898 ex - 0.9571ey
I2 =309.8
U2 = -0.9571 ex - 0.28981ey
corresponding
values
The eig function does not always give us unit vectors along a right-handed set
of coordinates. Check the determinant of pdirs. It must be +1 to have a right-handed
system. If not, change the signs on one of the unit vectors. Here det(pdirs) = -1
so we could change U2 to U2 = 0.9571 ex + 0.28981ey . Then U1 and U2 form
a right-handed system
Notes: The eig function produces two matrices. One matrix gives the principal area moments along its diagonal. Since the off diagonal terms are zero, this is actually the full area moment matrix for the principal directions. Eig also generates a matrix with the components of the unit vectors along the principal directions in its columns. As shown, if we want to find the angles of these axes we can do so easily. Note however, that eig does not always make the principal directions so they form a right-handed system so that you may have to change a sign on one of the unit vectors to ensure this is the case. An easy test to see if the unit vectors given do form a right-handed system is to evaluate the determinant of the pdirs matrix. If it is +1 the system is right-handed.

## Slide 37
If you do not have MATLAB available (as on a test) it is still possible to solve for the principal area moments and the principal directions, since as we have seen, the principal area moments are given by:
and if we let I1 be either one of these principal values, the angle from the positive x-axis to the I1 principal direction is just
and the other principal direction is at
Notes: MATLAB makes all the calculations very easy but if MATLAB is not available you can always fall back to the formulae we gave previously.

## Slide 38
One of the reasons for treating the transformation of area moments by a matrix approach is that it easily generalizes to more complex problems. For example, in dynamics the three-dimensional angular motion of a body (such as a spinning satellite, for example) is controlled by the mass moments of inertia defined as
where r is the mass density and dV is a volume element
Mass Moments of Inertia
Notes: Area moments appear frequently in Strength of Materials problems. Similar quantities such as mass moments of inertia appear in Dynamics. In that case there can be as many as six mass moments involved.

## Slide 39
In this case the mass moments transform due to a rotation of axes in just the same manner as we have already discussed. If we let unit vectors n, t, v be along the x', y', z' axes (which are assumed to be orthogonal to each other and right-handed), then
x
y
z
x'
y'
z'
n
t
v
Notes: The transformation of mass moments follows the same pattern we saw for area moments. Change of mass moments of inertia with a 3-D rotation of axes, for example, can again be expressed as a matrix multiplication of a mass moment of inertia matrix with direction cosine matrices.

## Slide 40
We see that again we have
In this case there are three principal mass moments of inertia and three corresponding principal directions. These are again determined by the solution of the eigenvalue problem
Notes: Similarly, finding principal mass moments of inertia and principal directions can be expressed as an eigenvalue problem.

## Slide 41
Using MATLAB, we can solve for the principal mass moments of inertia and the principal directions with the same eigenvalue function eig. Consider the following problem where the mass moment of inertia matrix is given:
I=[100 20 30; 20 300 50; 30 50 200]
I =
100 20 30
20 300 50
30 50 200
[pdirs, pvals]=eig(I)
pdirs =
0.9670 -0.2166 0.1337
-0.0322 0.4169 0.9084
-0.2525 -0.8827 0.3962
pvals =
91.4995 0 0
0 183.7468 0
0 0 324.7537
mass moment of inertia
matrix
principal directions (in columns)
(x, y, z components of a unit vector along the principal axis)
principal mass moments
of inertia
define a symmetric
mass moment matrix
solve eigenvalue problem
corresponding
values
Example 14.7
Notes: The use of MATLAB and the eig function makes obtaining principal values and principal directions easy as this example shows. Again, MATLAB may not give principal directions that form up a right-handed system, but we can easily change the signs of one of the unit vectors to make the system right-handed.