## Slide 1
The Dot Product and Direction Cosines
Notes: This section will discuss two vector-related quantities: the dot product and direction cosines.

## Slide 2
Learning Objectives
Vector Dot Product
Direction Cosines
Notes: We will define dot products and direction cosines and give examples of their use.

## Slide 3
Scalar (Dot) Product of Two Vectors
Let A, B be two vectors and let q be the smallest positive angle between them. Then the scalar (dot) product of A and B, A B is given by
.
A
B
q
Note 1:
Note 2:
Note 3: If the dot product A B =0 then either A =0 or B =0 (or both) or
A B (A is perpendicular to B)
.
Note 4: The dot product between two unit vectors is the cosine of the angle between them
eA
eB
a
Notes: One can multiply vectors together using either a cross product or a dot product. Here we define the dot product and give some of its properties. We can use the property in Note 4, for example, to determine direction cosines. The dot product is closely related to Cartesian components since if we dot any vector F with a unit vector in a given direction, we obtain the Cartesian component of F in that direction.

## Slide 4
60o
300 lb
7
24
25
A
B
Find the scalar and vector rectangular components of the 300 lb force which are parallel to inclined plane AB
x
y
scalar
component
vector
component
Example 1.8
Notes: If we write both the 300 lb force and a unit vector along AB in terms of their Cartesian components, then we can use those vectors and the dot product to calculate the scalar component along AB and this scalar component multiplied by the unit vector along A gives us the vector component of the 300 lb force along AB.

## Slide 5
in MATLAB
F = [ 300*sind(60) 300*cosd(60) 0 ];
AB =[ 24 7 0];
e =AB/norm(AB);
FAB = dot(F, e)
FAB =
291.4153
FV = FAB*e
FV =
279.7587 81.5963 0
note use of sind and cosd
functions. If we use sin and cos functions instead then we must place angles in radians !
alternatively,
unit row vector
FAB = F*e'
FAB =
291.4153
scalar component of F along AB
vector component of F along AB
We wrote all the vectors here in 3-D but we could have written
them as 2-D vectors also
Notes: We can easily generate the force and the unit vector along AB in MATLAB. There is a built in MATLAB function dot we can use to calculate the dot product, or we can multiply the force, written as a row vector, by the unit vector written as a column vector. The rules of matrix-vector multiplication then also gives us the dot product.

## Slide 6
Direction Cosines
x
y
z
i
j
k
x
y
z
eF
i
j
k
unit vector along F
qx
qy
qz
so
similarly
Notes: Writing a vector in x-y-z Cartesian coordinates and taking the dot product of that vector with the unit vectors along the (x, y, z) axes gives the magnitude of the force times the direction cosines. Knowing the direction cosines, we can compute the angles themselves with an inverse cosine function. Note: unlike computing the inverse sine function there is never any problem in using the inverse cosine since the angles with respect to the axes always are given as “principal” values between 0 and 180 degrees.

## Slide 7
u
Fu
40o
x
y
(a) Determine the (x,y,z) scalar components of the force F
(b) Express the force in Cartesian vector form
(c) Determine the direction cosine angles of the force
F = 1000 lb
25o
x
y
z
F = 1000 lb
25o
(a)
(b)
(c)
Example 1.9
40o
Notes: Here is an example of computing by hand the direction cosine angles. Note that we get the Cartesian components of F by first breaking F up into its z and u components and then further breaking the u component ( in the x-y plane) into the x and y components.

## Slide 8
We can do this very simply in MATLAB:
magF=1000;
eu= [ -sind(40) cosd(40) 0];
F= magF*cosd(25)*eu + magF*sind(25)*[0 0 1]
F= -582.5634 694.2720 422.6183
unit vector in u-direction
magnitude of the force
angs =acosd(F/magF)
angs =
125.6310 46.0308 65.0000
angles in degrees
writing the vector F as
force divided by its magnitude gives a vector of direction cosines
so taking inverse cosine gives the angles themselves
Notes: We can also do the problem shown on the last slide by the same steps using in MATLAB.

## Slide 9
Position Vectors
If we have two points A and B the vector from A to B, rAB, is the position vector between those two points.
x
y
z
A
B
If we know the location of A and B relative to a given point P,
then we can use vector relations to find the position vector
x
y
z
A
B
P
Position vectors are very useful in obtaining the unit vectors needed
to define other vectors such as forces, as the next example shows
Notes: Position vectors describe a vector that goes between two specified points. Dividing a position vector by its magnitude gives us a unit vector along the line between the two points.

## Slide 10
x
y
z
P
R
(2, 3, 0)
(3.5, 0, 2.6)
O
55 lb
Example 1.10
A platform is held in the horizontal x-z plane by a cable that is attached to a vertical wall at P and the platform at R, as shown. The tension in the cable is 55 lb. Determine the vector force in the cable in terms of its Cartesian coordinates. The coordinates are all measured in feet.
To determine the force, we need the unit vector along its direction. We can find these from position vectors:
Notes: Here is an example of using position vectors to define a force vector that acts along a line between two points, such as a force in a cable that is attached to the two points.

## Slide 11
Using MATLAB the steps are the same:
OR = [ 3.5 0 2.6];
OP = [ 2 3 0];
RP = OP - OR;
eRP = RP/norm(RP);
F = 55*eRP
F = -19.4400 38.8801 -33.6961
Notes: Here is the same solution in MATLAB