## Slide 1
Equivalent Force-Couple Systems (3-D)
Notes: This section will deal with the concept of equivalent force systems and the concept of a resultant for 3-D cases.

## Slide 2
Learning Objectives
Equivalent Force-Couple Systems
Resultants
Wrenches
Notes: We will define equivalent force-couple systems and resultants. In some important special cases the resultant will be a single force, but in general we will show the resultant is what is called a wrench.

## Slide 3
Equivalent Force-Couple Systems and Resultants
Definition: Two sets of forces and couples are said to be statically equivalent if they produce the same total force and moment with respect to any point.
The resultant of a set of forces and couples is said to be the simplest system that is statically equivalent to the original set.
Given any set of forces and couples, we can always reduce the system to a single force, R, and single couple, M, if we set
F1
F2
FN
r1
r2
rN
C1
CM
=
R
M
O
O
As stated previously:
Notes: Recall, a pair of systems of forces and couples are said to be equivalent if they produce the same net force and moment. Obviously, any system can always be reduced to a single force R and a single couple M at any point. We will repeat some of the slides shown previously in discussing the coplanar force system case.

## Slide 4
R
M
For general force and couple systems a single force and couple in the form of a wrench (which we will discuss later) is the simplest equivalent system. However, in some special cases we can reduce the system to a single resultant force.
We can do this if we can place R at some location, r, where
R
O
r
=
O
Notes: Here, we want to examine when we can further replace the force R and couple M by a single resultant force R, acting at some location.

## Slide 5
The equation
has a solution only if R and M are
perpendicular to each other since
so that if this equation is satisfied we must have
also
Important force-couple systems where R and M are perpendicular are:
Planar (2-D) force-couple systems
x
y
=
R
M
=
R
resultant
line of action
Notes: We can find such a single force resultant only if R and M are perpendicular to each other. In coplanar (2-D) force-couple systems, this is always the case. Note that the resultant single force can be located anywhere along its line of action. We have covered this case already so we will look at other cases.

## Slide 6
parallel force systems
=
R
M
=
R
a trivial special case is also a concurrent force system
P
=
P
R
resultant
resultant
x
y
z
x
y
z
Notes: Another important case where R and M are perpendicular is the case of a parallel system of forces. Thus, again, we can replace this parallel system by a single force resultant. Concurrent systems of forces obviously are a special case where, by simply adding up the forces and placing the sum at the point of concurrency, we obtain a single resultant force.

## Slide 7
Determine the resultant of this parallel force system and the intersection of the line of action of the resultant with the x-z plane.
50 N
250 N
150 N
200 N
1.5 m
1.5 m
2 m
2 m
x
y
z
O
50 N
675 N-m
300 N-m
O
i
j
k
Example 3.2
13.5 m
6 m
50 N
O
Notes: Here is an example of a parallel system. By locating the resultant in the x-z plane (i.e., choosing y = 0) we can find a definite point for locating the resultant along its line of action.

## Slide 8
Here we use MATLAB to set up the equation for the location of the resultant and then use the MATLAB solve function to locate it in the x-z plane
ey = [0 1 0]; % unit vector in y-direction
F1 = 250*ey; % the forces
F2 = 50*ey;
F3 = -150*ey;
F4 = -200*ey;
R = F1 + F2 + F3 + F4; % total force
r1 = [ 1.5 0 2]; % the position vectors
r2 = [ 0 0 4];
r3 = [ 3 0 4];
r4 = [ 3 0 2];
M = cross(r1, F1) + cross(r2, F2) + cross(r3, F3) + cross(r4, F4);
syms x z
r = [x 0 z];
S = solve(cross(r,R) - M);
xn = double(S.x)
xn = 13.5000
zn = double(S.z)
zn = 6
Notes: This is the MATLAB solution. First, we calculate the resultant force and moment and then use the solve function to locate the resultant in the x-z plane.

## Slide 9
Replace the force by a force and couple at C. all distances are in mm.
i
j
k
x
y
C
z
300 mm
400 mm
500 N
500 mm
600 mm
A
B
x
y
C
650 mm
z
Notes: In this case we want to simply replace the force by an equivalent force and couple at a particular point. Here are all the calculations done by hand. Try this in MATLAB.

## Slide 10
If the resultant force and moment are not perpendicular to one another then we cannot reduce the system to a single force, but we can always eliminate that part of the moment that is perpendicular to the resultant force R. The resultant force and couple (which is parallel to R) is called a wrench
R
M
R
solve
we can solve this equation since we can always move R over in a plane that will eliminate the perpendicular component of M, leaving just the parallel component of M
Reduction to a Wrench
=
if
P
P
r
Notes: We saw that for special force systems where the resultant force and moment are perpendicular, we can always replace the system by a single resultant force. If the net force and moment are not perpendicular, we can still replace the resultant force and that component of the moment that is perpendicular to the resultant force by just the resultant force, but we will still be left with the component of the moment that is parallel to the resultant force. The combination of the resultant force and parallel moment is called a wrench. Thus, every force-couple system can be reduced to a wrench.

## Slide 11
(4) solve
x
y
z
75 lb
80 lb
50 lb
12 in
9 in
O
the general procedure to follow is:
(1) calculate R, MO
(2) find unit vector along R
Reduce the force system to a wrench and locate the wrench in the xz-plane and xy plane.
(3) determine moment along R
remainder is then part of M that is perpendicular to R
Example 3.4
Notes: Here is an example of reducing a force system to a wrench. The steps outlined in the process are given.

## Slide 12
in MATLAB
R = [0 50 (75+80)]
R = 0 50 155
M =[75*12 0 50*9]
M = 900 0 450
eR =R/norm(R)
eR = 0 0.3070 0.9517
Mpar = dot(M , eR)*eR
Mpar = 0 131.4797 407.5872
Mperp = M-Mpar
Mperp = 900.0000 -131.4797 42.4128
resultant force
resultant moment about O
unit vector along R
x
y
75 lb
80 lb
50 lb
12 in
9 in
O
z
Notes: These steps can be easily carried out in MATLAB. First, we add up the forces to get the resultant force and compute the moments about O and place these results in MATLAB vectors. Then we compute a unit vector along the resultant force and use it to determine the components of M that are parallel and perpendicular to the resultant force.

## Slide 13
R = 0 50 155
Mperp = 900.0000 -131.4797 42.4128
i
j
k
the second and third equations
both give x = 0.8483 in.
with y = 0 the first equation
gives z = -18 in.
x
y
0.848 in
-18 in
O
z
plane parallel to yz-plane
resultant force R
let r = xi + yj +zk
from the last slide;
Now, solve
this part we will do by hand:
in-lb
Notes: Then we locate the wrench in the x-z plane.

## Slide 14
If we set z = 0 instead we obtain x = 0.8483 in. , y = 5.807
x
y
0.848 in
-18 in
O
z
5.807 in
location of
previous solution
in-lb
Notes: Here is the resultant located in the x-y plane.