## Slide 1
Centroids and the Center of Gravity
Notes: These slides will cover centroids and center of gravity concepts.

## Slide 2
Learning Objectives
Center of Gravity
Centroids
for volumes
for areas
for lines
Centroids by Integration
Centroids of Composite Bodies
Notes: Center of gravity and centroids are defined as integrals so we will examine the types of integrals involved and the way we can perform the integrations. Complex bodies can be handled by breaking them up in simpler components.

## Slide 3
Consider a body occupying the volume V and let the gravitational field act in the –y direction
Center of Gravity
x
y
z
V
dV
r
dR
(x,y,z)
gravity
If g is the force/unit volume acting on the body from gravity, then the force of gravity acting on the small volume dV is
and the total force, R, acting on V is
where W is the total weight of the body
O
Notes: Consider first the concept of center of gravity. The force of gravity acts on every part of a body so it can be represented as a weight/unit volume. The total weight is then an integral of the weight per unit volume over the volume of the body.

## Slide 4
Gravity acting on dV produces a moment about the origin O given by
so the total moment of the force of gravity about O is
x
y
z
V
dV
r
dR
(x,y,z)
O
Notes: We can also compute the total moment generated by the weight/unit volume as integrals of that weight per unit volume multiplied by coordinate distances.

## Slide 5
since M0 is perpendicular to R we can replace the distributed force of gravity on the body by a single force acting at a point (xG , yG , zG ) called the center of gravity
R
rG
(xG , yG , zG)
Notes: Since the force of gravity is a distributed parallel force system, it can replaced by a single force whose magnitude is the total weight acting at a point called the center of gravity.

## Slide 6
To find the center of gravity we must satisfy
which gives
if gravity acted in a direction not parallel to the y-axis we would also find
Notes: Here is how we calculate the center of gravity. In the example shown above we can only locate the (x, z) components of the center of gravity because we can move the resultant anywhere along its line of action parallel to the y-axis, but if we change the orientation of the body we can define a y-coordinate of the center of gravity also in a similar way.

## Slide 7
If g is a constant, we can factor it out of the integrals and obtain instead
where the point (xc , yc , zc) is called the centroid of the volume V (a geometrical parameter)
The Centroid
Notes: When the weight/unit volume is a constant, we can factor it out. The resulting center of gravity is then a quantity dependent only on the geometry of the body called the centroid.

## Slide 8
In a similar manner we can define centroids of areas
y
dA
or centroids of lines
A
x
y
dL
L
x
Notes: In addition to volumes, we can define centroids for other geometrical objects like areas and lines.

## Slide 9
If we use r = mass/unit volume instead of g = the weight/unit volume, we can define the coordinates of the center of mass as
Notes: If instead of using the weight/unit volume, we use the mass/ unit volume we can define a point called the center of mass of the body. When gravity is constant throughout the body, the center of mass and center of gravity coincide.

## Slide 10
Centroids of Areas
Note that if the area has a line of symmetry the centroid must lie on that line
c
c
y
x
-x
dA
dA
Notes: When a body has a line or plane of symmetry, we must have the centroid on that line or plane. Here is an example for a symmetrical area.

## Slide 11
calculation by 2-D integration
a
b
2-D integration
similarly
x
y
let u =b – y, du =-dy
C
area first moment
Example 7.2
Determine the location of the centroid of the shaded area.
Notes: We calculate centroids by integrals. Here is an example using 2-D integration to calculate what is called the first moment of the area. By dividing by the area/2(which we could also obtain by integration) we get the centroid.

## Slide 12
calculation by 1-D integration –horizontal strip
a
b
1-D (strip) integration
where
dAs
dy
area of the strip
distance to centroid of the strip
note the ½ factor
dAs
first moment integral
Notes: Generally, when doing these problems without MATLAB it is easier to write the integration for areas as integrating over strips since then we only have to do a 1-D integration. We can view the first moment integral as summing up the products of the distance to the centroid of the strip times the area of the strip. Here is the integration shown as a 1-D integral for a horizontal strip. It obviously gives the same answer.

## Slide 13
calculation by 1-D integration – vertical strip
a
b
dAs
or
if we had done y-integration first
where
dx
but again
Notes: Here is the same integration using a vertical strip.

## Slide 14
Use of strips and 1-D integration: summary
D=D(y)
x
y
y
dy
x
dx
H=H(x)
x
y
D/2
H/2
Notes: This is a summary of the difference between using horizontal and vertical strips.

## Slide 15
Example 7.3
Locate the centroid of the area between the curve and the line y = b.
choose a strip element
dy
x
y
a
b
or
Notes: Consider the specific area shown in this example, where we use a horizontal strip.

## Slide 16
syms y a b
hs = a*y^2/b^2;
xs = a*y^2/(2*b^2);
ys = y;
A = int(hs,y,0,b)
A = (a*b)/3
xA = int(xb*hs, y, 0 ,b)
xA = (a^2*b)/10
yA = int(yb*hs, y, 0 , b)
yA = (a*b^2)/4
xc = xA/A
xc = (3*a)/10
yc = yA/A
yc = (3*b)/4
Here is the same 1-D integrations done symbolically in MATLAB
define symbolic variables
define the x- and y- centroids of the strip, xs and ys
compute the area A
compute the first moment of the area, xc A
compute the first moment of the area, yc A
compute the x-location of the centroid, xc
compute the y-location of the centroid, yc
hs = dAs/dy , the height of the strip
Notes: MATLAB can do all the integration work for us. Here is the same problem as just considered where we set the problem up with symbolic variables and then do the 1-D integrals symbolically with the MATLAB integration function int. We need to define the integrand to be integrated in this function, the integration variable, and the limits of the integral.

## Slide 17
It is also easy to do all the integrations as two-dimensional integrations in MATLAB.
We use a set of nested int functions:
x
y
a
b
or
syms x y a b
A = int(int(1, x, [0 a*y^2/b^2]), y, [0 b])
A = (a*b)/3
xA = int(int(x, x, [0 a*y^2/b^2]), y, [0 b])
xA = (a^2*b)/10
yA = int(int(y, x, [0 a*y^2/b^2]), y, [0 b])
yA = (a*b^2)/4
xc=xA/A
xc = (3*a)/10
yc = yA/A
yc = (3*b)/4
Notes: If you find the use of 1-D integrals difficult, try using 2-D integrations with MATLAB as that is a very direct way to perform the integrals in a uniform manner, as shown.

## Slide 18
Locate the center of mass of the right circular cone if its mass density is proportional to the vertical distance from the xy-plane
By symmetry
Let r = k z and choose a cylindrical differential volume
element of height dz and radius u:
z
u
dz
r
h
x
y
z
Notes: Here is an example of computing the center of mass location for a cone whose mass is distributed non-evenly.

## Slide 19
x
y
12 in.
24 in.
Example 7.4
Locate the centroid of the curved slender rod.
dL
y
x
dL
dy
dx
x
dL
Notes: This example considers finding the centroid of a curved rod (line) in 2-D. Here, the integrals are much more complicated so we should likely consider using MATLAB (unless you have very good integration skills or a very good table of integrals handy). Shown here is the calculation of the length of the line and its first moment in the x-direction.

## Slide 20
let
then
which integrates to
dL
x
12 in.
24 in.
Notes: Here is the first moment in the y-direction and then the calculation of the centroid coordinates. Note the centroid does not lie along the line.

## Slide 21
Here are the same calculations in MATLAB
syms y
Ls = sqrt(y^2 +9)/3;
xb = y^2/6;
yb = y;
L = int(Ls, y, 0, 12);
xL = int(xb*Ls, y, 0, 12);
yL = int(yb*Ls,y, 0,12);
xc = xL/L;
yc = yL/L;
double([ L , xL, yL, xc, yc])
ans =
27.8807 304.9623 207.2784 10.9381 7.4345
x- and y-locations to a length element dL
Ls = dL/dy
total length of line
first moments of the line
centroid locations of the line
turn all the symbolic values calculated into numerical values
xc
yc
L
xL yL
first moments
Notes: Here are the same calculations done symbolically in MATLAB. If we want to use these results in numerical calculations, we need change the symbolic results to numerical values. we do this easily with the double function.

## Slide 22
Centroids of Composite Areas
A1
A2
similarly
x
y
Notes: Now, consider more complicated areas that can be decomposed into simpler parts whose results are much easier to obtain. These are called composite areas. By using the definition of the centroid locations, we can show that these centroids can be defined as a sum of a weighted sum of the areas of the parts divided by the total area, where the weighting factors are just the centroid locations for the individual parts.

## Slide 23
Composite Lines, Volumes, Weights or Masses
lines
volumes
weights
masses
etc.
etc.
etc.
etc.
Notes: In an entirely similar manner' we obtain centroids of volumes, lines, centers of gravity, and centers of mass.

## Slide 24
75 mm
75 mm
50 mm
75 mm
75 mm
A1
A3
A2
A2 is the area of a quarter-circle
x
y
Example 7.5
Locate the centroid of the shaded area in the x-y coordinates
Notes: Here is an example of a composite area. We need to define the centroid locations and areas numerically for the components and then use the weighted values in the composite body formula. Note that the square hole is area removed from the body, so we treat it as a negative area in the weighted sum.

## Slide 25
A(1) = 50*150;
A(2) = pi*(150)^2/4;
A(3) = -75*75;
x(1) = 75;
x(2) = 4*150/(3*pi);
x(3) = 75/2;
y(1) = 25;
y(2) = 50 + 4*150/(3*pi);
y(3) =50 + 37.5;
At = sum(A);
xc = sum(x.*A)/At
xc = 75.5412
yc = sum(y.*A)/At
yc = 87.1711
Here is the MATLAB solution
areas, put A(3) in as negative
x- and y- distances to centroids
centroid locations of the composite area
total area
Notes: In MATLAB we enter the areas and the coordinates of the centroids of the components into vectors and then do sums or weighted sums. Note the use of .* which represents element–by-element multiplication of the components of the two vectors to yield a vector of the same size containing the products. This is a very easy way to get the weighted terms we need. The MATLAB function sum then sums up these products.

## Slide 26
Centroids and Resultants of Distributed Loads
x = a
x = b
w = w (x) lb/unit length
x
w(x)
resultant force
=
R
xR
area under loading curve
location of centroid of area under loading curve
x
Notes: Another place where centroids are useful is where we must replace loads distributed along a line (such as the case of a distributed load on a beam, as shown) by a single resultant force and determine the value of that total resultant force and its location so that the resultant is statically equivalent to the original distributed load. The resultant force is just the area under the distributed loading diagram and the location where we place that resultant force is just the first moment of the load distribution divided by the total force. This is just the location of the centroid of the area under the loading diagram.

## Slide 27
w force/length
L
R = wL
L/2
w force/length
L
R = wL/2
L/3
Examples:
Notes: Here are some examples for a uniform load and a linearly increasing load.

## Slide 28
Example 7.6
Determine the resultant force R of the distributed load and locate it with respect to the origin, O.
x
y
2.5 kN/m
5.0 kN/m
2m
4m
O
1
2
2 m
2 m
4/3 m
=
15 kN
4.22 m
O
O
R1 = 10 kN
R2 = 5 kN
2/3 m
Notes: We can use the idea of composite areas also here where we break up the distributed loading diagram into simpler parts and use the composite body formula.