## Slide 1
Stability
Notes: Bodies can be in stable or unstable equilibrium so we will examine the conditions that determine stability.

## Slide 2
Learning Objectives
Examine the different ways that structures can lose stability
Load Bifurcation
Limit Load Instability
Snap-Through Buckling
Notes: We will consider three types of instability: bifurcation instability, limit load instability, and snap-through buckling. These cover many of the commonly occurring types of instability.

## Slide 3
Principle of Virtual Work
If we write the external work in terms of a "work potential"
then the virtual work principle becomes
where
is the total potential energy
It follows that the total potential energy is stationary (dV =0) at equilibrium
Notes: The principle of virtual work, which as we have seen is equivalent to equilibrium, can be written in terms of potentials where the total potential energy is stationary at equilibrium

## Slide 4
A simple example is a ball of mass m on a curved surface y = f(x):
and the ball is in equilibrium when
y
x
A
B
C
Thus, A, B, C are equilibrium positions but are they stable positions? The answer:
point B is a stable equilibrium position
point A is an unstable equilibrium position
point C is a neutrally stable equilibrium position
Notes: A classical example to illustrate stability criteria is a ball of mass m on a curved surface under the action of gravity. At various equilibrium locations on the surface, we can identify stable, unstable, and neutral equilibrium positions as where the second derivative of the total potential energy is positive, negative and zero, respectively.

## Slide 5
The ball on the curved surface is an example of a single degree of freedom system where the potential energy can be described in terms of a single variable such as x. We will only examine other single degree of freedom systems. We will classify such systems by plotting the external force as a function of the single variable (called a load path) and examining the load path behavior of the system. There are three types of load paths we will consider:
x
P
bifurcation
point
bifurcation
A load path where P increases in a stable manner with x = 0 and another curved path (which here is unstable). The two paths intersect at a bifurcation point . Pcr is called the critical load. Beyond Pcr the original path is also unstable.
P
x
stable
unstable
limit load
limit load
A load path where the load increases in a stable manner and then reaches a maximum value beyond which the system is unstable.
Pcr is the critical (limit) load
stable
unstable
P
x
stable
unstable
stable
Pcr
snap-through buckling
The load increases in a stable manner to a critical load where the system becomes unstable and jumps to a new stable position at a different x
unstable
Notes: In other problems where the total potential energy depends on only one variable (called single degree of freedom systems), we can use the same criteria developed for the ball on a surface to examine stability. We will consider three types of instability – bifurcation instability, limit load instability, and snap-through buckling instability. In bifurcation instability, as the load increases on a system there reaches a load (called the critical load) where there are multiple load paths, i.e., the load curves split (bifurcate). Some or all of these alternate load paths may be unstable. In the case of a limit load instability, the load increases to a maximum load beyond which the load path is typically unstable. In snap-through buckling, a load increases to a value where there is an adjacent stable position to which the system "jumps".

## Slide 6
P
L
q
k
P
L
O
(a)
(b)
L
Ox
Oy
Example 14.5 (bifurcation instability)
Consider a rigid bar that is pinned on one end and where a force P acts at the other end (Fig. 14.14(a)). The top end of the bar is attached to a linear spring whose other end moves in a smooth slot so that the spring always remains horizontal. The spring is initially unstretched when the bar is vertical. Determine the conditions for equilibrium and examine the stability of these equilibrium positions.
work potential
internal potential energy of the spring
total potential energy
Notes: Here is an example of a bifurcation instability where a force is applied to a vertical bar. As we will see the bar cannot remain vertical for all values of the force since the system becomes unstable if the load is too large. We can examine the free body diagram of a deflected bar to obtain the terms in the total potential energy.

## Slide 7
at equilibrium
which has two solutions:
1. q = 0, P arbitrary ( a vertical line at q = 0)
2.
To examine stability consider
(the curved load path)
P
unstable
bifurcation
point
unstable
unstable
stable
B
0
90
-90
angle, degrees
1. along vertical line ( q = 0)
so
stable
unstable
and Pcr = kL
2. along curved path
unstable
… critical load
Notes: For the bar to be in equilibrium it must either be vertical or be a function of θ along a curved load path. But an analysis of the second derivative of the total potential energy shows that all paths are unstable except the vertical load path for P < kL . Thus Pcr = kL. At any value beyond this critical load the bar must fall either to the left or right to the floor.

## Slide 8
Example 14.6 (limit load instability)
The system of Fig. 14.18 (a) contains a rigid bar and a spring, but the force is now applied to small rigid extension, as shown. The spring is again unstretched when the bar is vertical and rides in a smooth slot, so it always stays horizontal. Determine the conditions for equilibrium and examine the stability of these equilibrium positions.
P
L
q
k
P
L
rigid
O
(a)
(b)
L
e
e
Ox
Oy
at equilibrium
Fig. 14.18
Notes: If we take the same bar-spring geometry but apply the force P eccentrically at the top of the bar, then the behavior of the system changes, as we will see. Again, we can write the total potential energy from the geometry.

## Slide 9
-1.5
-1
-0.5
0
0.5
1
1.5
0
0.2
0.4
0.6
0.8
1
1.2
1.4
1.6
1.8
2
e/L = 0.1
e/L = 0.1
e/L = 0.01
e/L = 0.01
stable
unstable
unstable
q, radians
equilibrium
force versus q is plotted for different e:
To examine stability:
for negative q so the only stable curves are for q positive
we find
Thus, we see a typical limit load type of behavior. The critical load Pcr occurs where dP/dq = 0, which can be written as
We must find this value of q numerically. For e/L = 0.1 Pcr = 0.7463 kL
at q = 0.4346 radians, approximately
Notes: In this case the behavior of the equilibrium load curves depend on the eccentricity, e. We can show that all curves for negative angles are unstable and the curves for positive angles exhibit a limit load behavior where the critical load depends on the eccentricity. At the critical load, the path becomes unstable so the bar must fall to the right to the floor.

## Slide 10
Example 14.7 (snap-through buckling instability)
Consider the deformable truss shown in Fig. 14.21(a) where the initial height is much smaller than the length of a truss member. Under these conditions, this is called a shallow truss. When the force P is applied, the pin at which the force acts has a displacement, u, that changes the height and length to values of (y, L), respectively, as shown in Fig. 14.21 (b). Each two-force member in the truss acts like a very stiff linear spring with spring constant k.
P
a
a
L0
L0
y0
y
L0
L0
L
L
(a)
(b)
u
Since the shortening of a truss member is D = L – L0, the total potential energy of the truss is
Fig. 14.21
Notes: This is an example where we apply a force to a very shallow truss, i.e., where the members are nearly horizontal. The truss members act as springs so again we can write down the total potential energy which we will consider as a function of the displacement u at the force.

## Slide 11
at equilibrium
which gives
A
B
stable
unstable
stable
C
D
-0.5
0
0.5
1
1.5
2
2.5
-2
-1.5
-1
-0.5
0
0.5
1
1.5
2
at A
at B
This results in the plot shown
where
The limit load at A is approximately
at
At this load the truss can jump to a new stable position, i.e., the truss "snaps-through" to a new stable
equilibrium position.
Notes: If we plot the force versus u at equilibrium, we see the load path shown, where the load reaches a maximum value in a stable manner (which we can verify by looking at the second derivative of the total potential energy). At that critical load, however, there is another configuration of the truss that is stable, so the truss abruptly jumps to that new stable position. In that new stable position, we can then continue to increase the force and the truss remains stable, or we can decrease the force in a stable manner. However, if we decrease it too much, the force will reach a critical negative value (shown as C on the curve) where the truss will jump back to a new stable position D.
Shallow domes, for example, can exhibit this type of instability if they encounter snow loads in excess of a critical value.