## Slide 1
Equilibrium of Beams
Notes: Beams are structures used frequently in construction. Here we will examine equilibrium for beams.

## Slide 2
Learning Objectives
Internal Forces
Axial Force, Shear Force, and Bending Moment distributions
Relationships for Shear Force and Bending Moment
Notes: Beams typically carry loads along their top surface. These produce internal forces and moments in the beam that vary along the beam length. These distributions of internal forces and moments determine the strength of the beam and how the beam deflects when it is treated as a deformable body. We examine such distributions and see that equilibrium requires that the internal forces, moments, and distributed loads satisfy general relationships to each other.

## Slide 3
Beams are structures where the internal forces are more complex than trusses. While a truss bar only carries an internal axial force that is constant in the bar, beams can carry internal axial forces, shear forces, and internal moments (couples) that can vary along the length of the beam.
A
B
3000 lb
4 ft
2 ft
4
3
Ay
Ax
V (shear force)
N (axial force)
M (bending moment)
P
P
The directions shown are the ones normally taken for positive internal forces and moments on a "right side" cut
P
These internal forces and moments are the resultants of distributed internal forces acting on the beam cross section.
Notes: Here is a typical beam where a known force acts along its surface. It is a statically determinate problem so we can find the reaction forces at A and B by equilibrium of the entire beam. However, if we examine a portion of the beam, we see that an internal axial force, shear force, and bending moment are required to keep this portion in equilibrium. These internal forces and moments are produced by distributed forces acting across the surface of the cut beam at P. In a Strength of Materials course, one examines those distributions in more detail but in Statics we will just deal with the net internal forces and moment that are statically equivalent to those internal distributions.

## Slide 4
Ay
Ax
V
N
M
P
As with all internal forces and moments, these always occur in equal and opposite pairs:
B
3000 lb
4
3
P
N
V
M
Thus, on a "left side" cut, the positive values for these internal forces and moments are opposite to those on a "right side" cut
right side cut
left side cut
Notes: The internal forces and moments in beams always occur in equal and opposite pairs since if we imagine putting the portions back together, they must all cancel. It is a common convention to draw a normal force N (axial force) acting to the right on a right side cut of a free body diagram, as shown. Similarly, a shear force V is taken as being down on this same cut and the direction of the bending moment M is taken to produce a counterclockwise moment.

## Slide 5
To determine internal forces, we must first find the external reactions. If the beam is statically determinant, this is always possible. Here is an example.
A
B
2400 lb
4 ft
2 ft
Ay
Ax
B
1800 lb
+
+
+
A
B
3000 lb
4 ft
2 ft
4
3
Notes: To find the internal forces/moment we must know the external reactions, which we can always find if the beam is statically determinate, as it is in this case.

## Slide 6
A
1600 lb
2400 lb
4 ft
2 ft
800 lb
1800 lb
B
1800 lb
With these external reactions known, we now can find the internal forces and moment at any cut. For a cut 2 ft to the right of A, for example:
A
800 lb
1800 lb
N
M
2 ft
P
+
+
+
V
Notes: To obtain the internal forces/moment at a specific location we must draw a free body diagram of the portion of the beam cut off and then simply apply the equilibrium equations. It is usually convenient to take moments about the location of the cut as then both V and M do not enter into the moment equation.

## Slide 7
These internal values depend on the location of the cut. For example, for a cut 0.5 ft to the right of the load:
A
2400 lb
4 ft
0.5 ft
800 lb
1800 lb
1800 lb
P
N
M
+
+
+
Note that if we had looked at equilibrium of the section to the right of the cut, we would get the same values:
1600 lb
1.5 ft
N
V
M
V
P
B
Notes: Of course, if we take cuts at different locations we will obtain different internal force/moment values. Note that sometimes it is easier to examine equilibrium of the portion of the beam to the right of the cut if the loading is less complex for that portion. However, we must draw the normal force and shear force and bending moment as shown above for section PB if we want to be consistent with the convention we used for section AP.

## Slide 8
The previous examples showed the values of the internal reactions at specific locations. In general, these values change with location so they are really functions of the distance x of the cut to the right of A. By letting this distance be arbitrary, we can obtain the internal force and moment distributions as a function of x.
Note, however, whenever the loading causes the free body diagram to change, these functions will also change their form. In this case we have, for 0 < x < 4 ft
A
800 lb
1800 lb
N(x)
M(x)
x
P
V(x)
+
+
+
Notes: We can use the same procedures for cuts at specific locations to examine the internal forces/moments at any location, x, in the beam by making the cut there. However, whenever the free body changes we must apply equilibrium to the new free body diagram to get the force/moment values. In the above example, these internal force and moment distributions are valid for 0 < x < 4 since the free body diagram shown is valid for any of those x-values.

## Slide 9
But for 4 ft < x < 6 ft
A
2400 lb
x
800 lb
1800 lb
1800 lb
P
N
M
+
+
+
V
Notes: However, if let 4 < x < 6 then the free body diagram changes and we can obtain the distribution of internal forces/moment for anywhere in this portion of the beam.

## Slide 10
N(x) lb
x
4'
2'
1800
V(x) lb
x
800
-1600
M(x) ft-lb
x
3200
1600
1
800
1
Here are the expressions for the internal forces and moment and plots of their distribution in the beam
Notes: We can now give complete expressions for the distributions of internal force/moment and draw those distributions.

## Slide 11
There are relationships between the applied vertical loads, the shear force diagram, and the bending moment diagram we can observe. For the problem previously considered:
x
4 ft
2 ft
800 lb
V(x) lb
x
800
-1600
M(x) ft-lb
x
3200
2400 lb
1600 lb
+ 800
-2400
1600
1
800
1
+1600
Notes: If we examine the applied forces and the shear force and bending moment distributions, we see there are some relationships between them. For example, we see that wherever a concentrated applied force exists along the beam there is a corresponding jump in the shear force diagram at that location in the same direction as the direction of the applied force. We also see that the slope of the bending moment diagram is equal to the value of the shear force. These relationships seen in this problem will in fact be general relationships, as we will see shortly.

## Slide 12
We can use those relationships to easily draw shear force and bending moment diagrams for many problems. Consider a beam with different types of loads:
A
B
distributed loads
concentrated loads
concentrated couples
x
dx
Examine equilibrium of a small element of length dx at a distance x along the beam:
dx
w(x) load/unit length
V(x)
V(x) +dV(x)
M(x)
M(x) + dM(x)
P
Notes: We will learn what general relationships exist for a beam that can have distributed loads, concentrated forces, and concentrated moments acting along its length. Consider a small section of the beam under a distributed load. Since the shear force and bending moment vary from location to location, we have indicated those small changes from values V, M, to values V+dV and M+dM, as shown.

## Slide 13
dx
w(x)dx
V(x)
V(x) +dV(x)
M(x)
M(x) + dM(x)
P
dx/2
+
higher order term, can neglect
+
Notes: Since the section is small the distributed load will be nearly a constant and its resultant will be wdx acting at the centroid of this nearly uniform value. Summing force and moments, we see there is a differential relationship between V(x) and w(x) and between M(x) and V(x).

## Slide 14
slope of shear force diagram at x = value of distributed load at x
slope of bending moment diagram at x = value of the shear force at x
x
4 ft
2 ft
800 lb
V(x) lb
x
800
-1600
M(x) ft-lb
x
3200
2400 lb
1600 lb
1600
1
800
1
w = 0
w = 0
Notes: If we examine these differential relationships, we can see them explicitly for the problem we just considered.

## Slide 15
At concentrated loads we have jumps in the shear force diagram. At concentrated couples we have jumps in the bending moment diagram.
P
V-
V+
jump in the shear force at x = the value of the concentrated load at x
+
+
C
M-
M+
any moments of
shear forces present are negligible
jump in bending moment at x = the value of the concentrated couple at x
Notes: Now, let us examine what happens at concentrated applied forces and moments. Applying equilibrium to a very small element about a concentrated force or moment we see that there is a jump of the internal shear force equal to the value of the magnitude of the concentrated force (and in the same direction up or down as that of the applied force) and a jump of the internal bending moment equal to the magnitude of the concentrated couple (and the direction of the internal moment jump is up if the applied couple acts clockwise, as shown, or down if the applied couple acts counterclockwise).

## Slide 16
jump in the shear force at x = the value of the concentrated load at x
jump in the bending moment at x = the value of the concentrated couple at x
x
4 ft
2 ft
800 lb
V(x) lb
x
800
-1600
M(x) ft-lb
x
3200
2400 lb
1600 lb
+ 800
-2400
+1600
no concentrated couples so bending moment curve is continuous
Notes: Applying these jump relations to our previous problem, we see the jumps in the shear force satisfy these relations (there are no concentrated couples so no jumps in the internal bending moment).

## Slide 17
If we integrate these relations between locations x1 and x2
change in shear force between x1 and x2 = the area under the distributed load between x1 and x2
change in bending moment between x1 and x2 = the area under the shear force diagram between x1 and x2
Notes: If we take the differential relations we have developed and integrate them we can get a relationship between the change in shear force and area under the distributed load and the change in bending moments and the area under the shear force distribution. We can use these integral relationships in addition to the differential ones to help us draw internal shear force and bending moment diagrams which will give us complete descriptions of the distributions of this internal force and moment. Note that the internal normal (axial) force is not coupled to either V or M so we always can draw that internal force diagram separately, if it is present.

## Slide 18
x
4 ft
2 ft
800 lb
V(x) lb
x
800
-1600
M(x) ft-lb
x
3200
2400 lb
1600 lb
w = 0 so no change in V
A
B
C
Notes: Here is how we can go from left to right, starting with the applied loading diagram and draw both the shear force and then the bending moment diagrams without ever doing an explicit cut to obtain the actual V(x) and M(x) distributions.
Starting at the left at V = 0, there is an immediate jump up in V of 800 lb. Since w = 0 in AC the slope of the shear force must be zero, the shear force is a constant 800 lb in that section. At C a concentrated force of 2400 lb causes a jump down in the shear force to a value of -1600 lb. In CB again there is no distributed load so the shear force is a constant -1600 lb in that section. At B there must be a jump up equal to the reaction force at B so the shear force ends up at zero.
Now, consider the bending moment. Starting at a zero value, the slope of the bending moment must be a constant in AC since the shear force is a constant. In going from A to C the change in moment must be equal to the area under the shear force diagram from A to C so we find the bending moment at C must be 3200 ft-lb. In CB the shear force is a negative constant so the slope of the bending moment diagram again must be constant in CB. The change in bending moment from C to B is equal to the area under the shear force diagram, which is -3200 ft-lb, so the bending moment must be zero at B. Thus, we have completely drawn these shear and bending moment diagrams.

## Slide 19
Summary of Relationships
+
+
a concentrated load in the vertical direction causes a jump up in the shear force
a clockwise concentrated couple causes a jump up in the bending moment
change in the shear force between x1 and x2 = the area under the distributed load between x1 and x2
change in the bending moment between x1 and x2 = the area under the shear force diagram between x1 and x2
the slope of the shear force diagram at x = the value of the distributed load at x
the slope of the bending moment diagram at x = the value of the shear force at x
Notes: Here is a summary of all the differential relations, jump conditions, and integral relations. If the loading of the beam is not too complex, we can, as in the last example, use these relationships to determine and sketch the shear force and bending moment internal distributions.