## Slide 1
Moments and Couples
Notes: These slides will discuss concepts of moments and couples, how they are calculated, and how they can be used.

## Slide 2
Learning Objectives
Moment of a Force about a Point
Cross Product
Couples
Notes: We will see that the moment of a force is given by a vector cross product and that couples are examples of “pure” moments.

## Slide 3
Moment of a Force about a Point
F
d
In addition to the pulling or pushing action of a force, which is described by the force vector itself, forces have the capability to turn or rotate a body. Thus, we need a measure of the turning effect of a force. This measure is another vector quantity called the moment of a force about a point P, Mp.
P
From experience we know the magnitude of the turning effect of a force about a point P depends on both the magnitude of the force F and the distance d
Notes: From our experience with turning a bolt nut with a wrench we know that the strength of the turning effect depends on both the force F we apply and the distance d from the nut. The moment of a force, which is a measure of the strength of this turning effect, must therefore depend on both F and d.

## Slide 4
From our experience with balances, we know that turning effects cancel (are equal in magnitude but opposite in direction) when the product of the magnitude of the force and distance are equal:
100 lb
3 ft
50 lb
6 ft
so we will set the magnitude of the moment of a force about a point P equal to product of F and d
MP = |MP| = Fd
Note that thus works even when F is inclined as long as we take (a) the distance, d in the product Fd to be the distance along a line from P to F that is perpendicular to F and use the total force F or (b) take the F in the product Fd to be the component of F that is perpendicular to the line from P to the force F, and let d in the product be the total length of the line from p to F
F
r
P
f
f
d
Notes: From a balance we know if the product of the forces and distances are equal the turning effects of the forces are equal so we expect that the magnitude of the moment must be equal to the product Fd. This is still true if we apply the force at an angle if we use the perpendicular distance to the force, as shown. However, we also get the same result if we take the total distance r from the nut to the force and use the perpendicular component of the force, as shown.

## Slide 5
We can specify the direction of the moment (turning effect) either by giving the sense of rotation that the force induces explicitly:
P
150 lb
3 ft
x
y
or we can use the right-hand rule to assign a unit vector direction
where k is a unit vector in the z-direction
Notes: In cases where a force lies in a plane, such as the x-y plane shown. we can specify the direction of the turning effect (moment) of a force by either giving the sense of turning (rotation) by a curved arrow or by assigning a unit vector to the moment from that curved arrow with the right-hand rule. For 2-D cases when the force lies in the x-y plane this unit vector will be in the plus or minus z-direction.

## Slide 6
F
r
e
P
d
plane containing r, F
moment of the force about point P
where e is a unit vector determined by
rotating r into F and using the right-hand rule
r
F
e
The example just shown is where the force and line from P to the force are in the x-y plane but the same ideas also work in 3-D cases where the vector F and the position vector, r, from P together define a plane that contains both vectors and we take the direction of the moment to be perpendicular to that plane, as determined by the right-hand rule
Notes: We can use the same ideas when a 3-D force is located in 3-D by a 3-D position vector. In that case, we simply consider the force and position vector in the plane that contains both vectors and apply the same definition. In this case we get a direction for the moment defined by a unit vector that is in a direction perpendicular to that plane, a direction which is determined by the right-hand-rule when we rotate the position vector into the force vector.

## Slide 7
Here is why it is called the right-hand rule. Suppose we have a force that tends to rotate a body about a point along a particular axis. If we curl the fingers of our right hand to define the sense of rotation, as indicated by the curved arrow in the figure below, then the axis of rotation (direction of the moment) will be defined as a unit vector acting along a line that points in the direction of the thumb.
rotation in the plane
containing r and F
Notes: This slide shows how the direction of the moment of a force about a point is obtained from the right-hand-rule, using the sense of rotation the force makes about a point P in the plane containing the position vector r and the force F (which are not shown here).

## Slide 8
F
r
e
P
d
plane containing r, F
moment of the force about point P
This description of the moment of a force about a point can be put in the form of a vector cross product since if we let A and B be two vectors and let q be the smallest positive angle between them then the vector cross product of A and B, AxB, is defined as
where e is a unit vector perpendicular to both A and B and is in a direction given by the right-hand rule when A is rotated into B through the acute angle q
q
A
B
e
Vector Cross Product
Notes: The definition we have given for the moment of the force can be put in the form of a vector cross product of the position and force vectors. The definition of the vector cross product for any two vectors A and B is given above.

## Slide 9
F
r
e
P
d
plane containing r, F
moment of the force about point P
Now, let A = r and B = F in the cross product r x F
q
q
Then
Again, we can interpret this in two ways:
Notes: If we identify A and B in the vector cross product with the position vector from point P to the force and the force vector itself, then the cross product gives the moment of the force about point P. Again, this moment can be viewed as the perpendicular component of r times the total force or the total distance r times the perpendicular component of the force.

## Slide 10
We can let the position vector r, in the calculation of the moment of a force about a point P to be the vector from P to any point on the line of action of F without changing the value of the moment of F about point P
F
r
e
P
d
plane containing r, F
moment of the force about point P
r
or
Notes: Note that we can take the position vector in the cross product as a vector from the point P to any point along the line of action of the force vector without changing the moment of the force about the point P since the perpendicular distance d is again unchanged.

## Slide 11
Moment of a Force as a Cross Product
Some properties of cross products
1.
3. A × B = 0 if A = 0 or B = 0 (or both = 0) or if A is parallel to B
2.
4.
i
j
k
x
y
z
another way to remember these
i
j
k
+
-
Notes: Here are some of the properties of vector cross products. The cross products of the unit vectors along a Cartesian coordinate system are given as shown. An easy way to remember these relations is to put i, j, k on the face of a clock ,going clockwise. Then if we go clockwise around the face, the cross product of the first two unit vectors we encounter is the third unit vector. If we go counterclockwise the cross product of the first two unit vectors we encounter is the negative of the third unit vector. For example i x j = k while j x i = -k. Similarly k x i= j etc. Note that we have to associate these unit vectors with a right-handed coordinate system for this convention to be valid. In a right-handed system if you rotate the x-axis into the y-axis with your right hand, your thumb will point in the z-axis direction.

## Slide 12
We can use property 4 to calculate the rectangular components of the moment of a force in terms of the rectangular components of r and F:
so that
Notes: If one writes the position vector and force in a vector cross product in terms of their Cartesian components, then using the rules for the cross products of the unit vectors along those Cartesian axes we can obtain expressions for the Cartesian components of the moment. However, rather than memorizing these expressions, it is usually easier to simply write the position and force vectors out and perform the cross products of the unit vectors appropriately as just outlined.

## Slide 13
Another way to get the cross product is to expand the 3x3 determinant
MATLAB makes cross products easy
Example: r = 4i +3 j -2k ft ; F = 60i + 30j – 50k lb
r = [ 4 3 -2];
F = [ 60 30 -50];
M = cross(r, F)
M =
-90 80 -60
ft-lb
row vectors
rc = [4; 3; -2];
Fc = [60;30;-50];
M = cross(rc, Fc)
M =
-90
80
-60
column vectors
Notes: We can also get the cross product by writing it in the form of a 3x3 determinant. We can expand this determinant in terms of 2x2 determinants times the unit vectors, as shown, and then evaluate those smaller determinants. In MATLAB performing cross products is even easier as there is a built-in function cross that can do the cross product of two vectors, where the vectors can be written as row or column vectors in MATLAB.

## Slide 14
We can also use the determinant expression for the cross-product to do this problem symbolically. Given r and F as the row vectors seen before
syms i j k symbolic unit vectors
cross_mat = [ i j k; r ; F ]
cross_mat =
[ i, j, k]
[ 4, 3, -2]
[60, 30, -50]
M = det(cross_mat)
M =
80*j - 90*i - 60*k
ft-lb
the 3x3 matrix whose determinant we want to find
find the determinant
This answer is in symbolic form
Notes: Another way to do the cross product in MATLAB is to use the determinant expression. In this case the result is a symbolic expression of the cross product.

## Slide 15
Still another way to do a cross product of two vectors is to write
the cross product as a matrix-vector multiplication
Consider, for example the moment M = r x F. we can write this cross product as an anti-symmetrical matrix multiplied by the force vector as
For our previous example we have
M = [ 0 2 3; -2 0 -4; -3 4 0]*F.'
M =
-90
80
-60
Note:
is the transpose of the row vector F. It used here since we must have the force written as a column vector. The moment M is also a column vector
Notes: Still another way to do a cross product is to write it as a matrix-vector multiplication where the components of the position vector in the cross product are placed in a 3x3 anti-symmetrical matrix and a matrix-vector product is performed. Generally, it is easier to just use the MATLAB cross function.

## Slide 16
We can move a force F anywhere along its own line of action and we do not change the moment of that force about a given point P
F
r
e
P
d
plane containing r, F
moment of the force about point P
F
or
F
Notes: Note that we can move the force vector anywhere along its line of action since such sliding does not change the perpendicular distance d in the cross product definition.

## Slide 17
A force F is sometimes called a sliding vector since the moment does not change when we slide a force anywhere along its line of action. In Statics and Dynamics of rigid bodies it is only the net force and moment that determine the equilibrium or motion of the rigid body, so that for the analysis of rigid bodies we can always consider the force to be a sliding vector. However, for a deformable body we cannot slide a force without potentially changing the effect that the force has on the deformation. Example: consider two forces that act along the same line of action and squeeze a deformable block
unloaded block
If we move those forces along their line
of action so their positions are interchanged, the deformation of the block has now been changed to a stretching
Notes: A force F is sometimes called a sliding vector since moving it along its own line of action does not change either the force and the moment. For a rigid body, the net force and moment are the only quantities used in determining the conditions of equilibrium for the rigid body, so such sliding of the force has no effects on those equilibrium conditions. For a deformable body, however, sliding a force along its line of action can produce quite different deformation effects.

## Slide 18
Determine the moment of the force
F = i + j + k lbs, acting at a point Q, about the point P. All distances are in ft.
OP = 4j + k ft
OQ = i + 2j + 3k ft
r = OQ-OP = i - 2j + 2k ft
(0,4,1)
(1,2,3)
O
P
Q
F
x
y
z
r
solve in MATLAB with cross function
OP = [ 0 4 1];
OQ = [1 2 3];
r = OQ - OP;
F = [ 1 1 1];
M = cross(r,F)
M = -4 1 3
Example 2.1
solve by hand the cross product
in determinant form
Notes: Here is an example of computing the moment of a force either by expanding the determinant expression or by using the MATLAB cross function.

## Slide 19
syms i j k
cross_mat = [ i j k ; 1 -2 2; 1 1 1]
cross_mat =
[i, j, k]
[1, -2, 2]
[1, 1, 1]
Mp = det(cross_mat)
Mp =
j - 4*i + 3*k
we can also do this problem symbolically in MATLAB
Notes: Here is the use of the determinant expression to compute the moment expression symbolically in MATLAB.

## Slide 20
Determine the moment of the 500 lb force, which lies in the x-y plane, about point P.
(1) Use of M = Fd
P
d
b
a
Example 2.2
45o
x
y
2 ft
2 ft
P
4
3
5
500 lb
a
500 lb
We will solve this problem in
four different ways
500 lb
Notes: Here is the computation of the moment of the force in two dimensions using four different methods. The first method computes the force times the perpendicular distance.

## Slide 21
(2) Use of
P
b
b = 8.13o
500 lb
Notes: The second method uses the total distance and the perpendicular component of the force.

## Slide 22
(3) use of rectangular components
2 ft
2 ft
300 lb
400 lb
P
+
Notes: The third method uses the Cartesian components of the position vector and the force and takes the products of those components with the appropriate perpendicular distances along the x- and y-axes.

## Slide 23
x
2 ft
2 ft
P
4
3
5
500 lb
y
(4) use of vector cross product
r
(4) in MATLAB the cross function
gives
r = [ 2 -2 0];
F =[300 -400 0];
M = cross(r,F)
M =
0 0 -200
try in MATLAB doing the
determinant symbolically
Notes: The fourth method computes the vector cross product by either expanding the determinant expression by hand or by using the MATLAB cross function

## Slide 24
Couple
A couple is a vector quantity that represents a pure turning or twisting action on a body. It has the dimensions of a moment of a force (force x distance) and like a force is represented as an arrow but in 3-D we normally also shown the direction of the turning action of the couple as determined with the right-hand-rule so we can distinguish couples from forces
150 ft-lb
plane perpendicular to the couple
In 2-D , we normally just show the direction of the turning action and the magnitude:
30 in-lb
C
x
y
C =
which is the same as
C = 30 k in-lb
Notes: In addition to forces, which describe “pushes” or “pulls”, Statics deal with vectors that describe a “torque” or “turning effect” called couples. Couples can also be represented as arrows but to distinguish them from forces we also show the turning effect the couple has in a plane perpendicular to the line of action of the couple with a curved arrow. In two dimensions, we need only show the curved arrow.

## Slide 25
A couple is a representation of a pure twisting action (i.e., with no net “push” or “pull” action) in the same way a force is a representation of a push or pulling action, but a couple can also be generated by a pair of forces if those forces are equal and opposite and separated by a perpendicular distance, D:
F
-F
=
D
e
plane containing F and -F
Notes: One way to get a couple is with a pair of forces (i.e., a “couple” of forces) separated by a distance D. This pair generates no net force, but it does produce a turning effect in a plane of the two forces so that they produce a couple.

## Slide 26
In terms of cross-products, we see the couple of a pair of forces is:
F
-F
e
r1
r2
r12
P
D
Q
but note that unlike the moment of a single force the moment of a couple is independent of the point we take moments about since
r'2
r'1
so we do not have to indicate the point we take moments about
and we simply write the couple as M (or C)
plane containing F and -F
Notes: Unlike a moment of a force the moment of a couple is independent of the point we take moments about. Thus, a couple is called a free vector since for a rigid body we can freely move it about. Thus, if we do not change its magnitude or direction, a couple can be placed anywhere on a rigid body and not change its effect. Obviously, that is not true for deformable bodies.

## Slide 27
Determine the moment of the force couple where the forces act at points P and Q. All distances are in ft.
x
y
z
P = (1,1,0)
Q = (2,2,3)
3i lb
-3i lb
O
r12
Example 2.3
syms i j k
cross_mat = [ i j k ; -1 -1 -3 ; 3 0 0 ];
M = det(cross_mat)
M = 3*k - 9*j
in MATLAB
expand the determinant by hand
Notes: Here is example of computing the moment of a couple, either using a determinant that is either evaluated numerically or symbolically in MATLAB.

## Slide 28
Determine the moment of the couple and the perpendicular distance between forces.
4 ft
4 ft
4 ft
4 ft
2 ft
x
y
z
Example 2.4
Notes: Here is another example where we calculate the moment of a couple and determine the perpendicular distance between the two forces in the couple. In this case we use a determinant expression.

## Slide 29
r1 = [ -4 4 4];
r2 = [ 4 2 0];
F1 = [-70 -120 -80];
C = cross(r1-r2, F1)
C =
320 -920 1100
d = norm(C)/norm(F1)
d =
9.1652
in MATLAB
position vectors to the forces in the couple
force F1 in the couple
position vector r12 = r1 – r2
perpendicular distance between
forces in the couple
Notes: In this case we use the MATLAB cross function.

## Slide 30
Equivalent Couples
200 lb
200 lb
3 ft
P
200 lb
200 lb
3 ft
P
P
200 lb
200 lb
3 ft
=
=
100 lb
100 lb
6 ft
P
=
P
=
200 lb
200 lb
3 ft
Notes: We can translate a couple in its plane without changing it. We can also rotate the couple in its plane without changing it. We can change the perpendicular distance between the forces in a couple and the equal and opposite forces if the product Fd is unchanged. Finally, we can translate the plane of the couple itself. All of these are equivalent couples, i.e., they have the same turning effect on a rigid body.