## Slide 1
Equilibrium of Frames and Machines
Notes: This section will examine the more complex structures of frames and machines.

## Slide 2
Learning Objectives
Equilibrium of sections
MATLAB solutions
Notes: We will see that like trusses we can examine parts (sections) of a frame or machine to solve for the unknown forces. MATLAB will continue to be very useful for obtaining solutions.

## Slide 3
3 ft
1 ft
400 lb
D
E
G
0.5 ft
1 ft
1 ft
2 ft
A
B
C
F
Consider a 400 lb load (which acts at the center of gravity, G) that is held on one side of a dock by a hydraulic cylinder CF, which is pinned to member ACD and the dock, as shown. The platform is held by two other pinned members DCA and EB. There is an identical hydraulic cylinder and supports on the other side of the dock, but we will analyze only this side as if the other side were absent. All the unknown forces obtained here can then be simply divided by two due to the symmetry of the geometry. Determine (1) the force in the hydraulic cylinder, and (2) all the forces at the pinned supports, which are assumed to be smooth.
Example 6.1
Notes: Here is an example of a frame-like structure that is used to lower a payload from a dock. In this problem we want to (1) find the force in the hydraulic cylinder CF and (2) obtain all the forces at the pinned supports. There are identical supports and a hydraulic cylinder on the other side of the dock so we can account for that situation by analyzing only one side and dividing all the forces obtained by two.

## Slide 4
3 ft
1 ft
400 lb
D
E
G
0.5 ft
1 ft
1 ft
2 ft
A
B
C
Ax
Ay
FH
FB
4
3
Note that even if we recognize EB is a two force member, there are four unknown forces for the entire structure so we must break the system up.
(EB is a two-force member)
Notes: A good place to start in any frame problem is to examine a free body diagram for the entire structure by cutting that structure off from its supports. Here we see such a FBD. Note that the hydraulic cylinder is a two-force member as is the bent member EB . Thus, the size of the forces in those two members is unknown but we do know their directions at the pinned ends. In contrast, DCA is not a two-force member (why?) so we must show two unknown force components acting at pin A. There are four unknowns here and only three equations of equilibrium. We cannot, therefore, solve for the force in the cylinder directly from this FBD. We will have to break the system up and examine equilibrium of one or more parts. Doing such a break-up efficiently is a matter of experience in solving such problems, so a good way to proceed is to examine several possible FBDs to find the best combination.

## Slide 5
Ax
Ay
FH
FB
4
3
400 lb
3 ft
1 ft
7/2 ft
400 lb
FB
4
3
Dx
Dy
1 ft
(EB is a two-force member)
0.5 ft
1 ft
2 ft
(1) we can easily solve for cylinder force by hand with two moment equations
(1)
(2)
Notes: Here we show the FBD of the entire structure and the FBD of the payload and its platform. We see that this new FBD adds two more unknown forces ( Dx and Dy) but we now have an additional three equilibrium equations so we see by considering both FBDs we have a total of six equations and six unknowns and we can solve for all these forces, including the asked for force in the hydraulic cylinder, FH. However, by leveraging the moment equations and the choice of what points about which to take those moments we can solve the problem in just two steps: (1) by summing moments about D to get the force FB in member BE, and then summing moments about A to get the force in the hydraulic cylinder.
This first part of this problem is much like a typical frame/machine problem covered in Statics texts, where only a particular force in a rather complex structure is asked for. It is similar to the method of sections for trusses since we need to find a “good” part or set of parts and a choice of equilibrium equations to consider for the structure to obtain the unknown force with a minimum of effort. However, in most structural problems all the forces are of interest so, unlike most Statics courses, we will also consider the second part of this problem where we ask for all the unknown forces.

## Slide 6
Ax
Ay
FH
FB
4
3
400 lb
3 ft
1 ft
7/2 ft
400 lb
FB
4
3
Dx
Dy
1ft
(2) solution for the six unknown forces with MATLAB
FH
FH
D
E
Notes: The two FBDs we already considered gives us enough information to solve for all six unknown forces present in this problem. For completeness we have also shown the FBD of the hydraulic cylinder, although that FBD is not needed for the solution. Here, we write down explicitly the six equilibrium equations for the six forces.

## Slide 7
(1)
(2)
(3)
(4)
(5)
(6)
6 unknowns
FH x(1)
FB x(2)
Ax x(3)
Ay x(4)
Dx x(5)
Dy x(6)
6 equations
C =
1.0000 -0.6000 1.0000 0 0 0
0 0.8000 0 1.0000 0 0
-3.0000 0.8000 0 0 0 0
0 -0.6000 0 0 1.0000 0
0 0.8000 0 0 0 1.0000
0 0.8000 0 0 0 0
Want to solve linear system [C]{x} = {b}
0
400
-1400
0
400
-200
b =
Notes: As in previous cases we will show both numerical and symbolic solutions with MATLAB, although the symbolic solution is, as we have seen, more efficient. Here is the setup for the numerical solution.

## Slide 8
C\b
ans =
400
-250
-550
600
-150
600
FH x(1)
FB x(2)
Ax x(3)
Ay x(4)
Dx x(5)
Dy x(6)
after defining C and b, solve the system of linear equations
Notes: And here is the MATLAB numerical solution for this set of simultaneous equations.

## Slide 9
Symbolic solution in MATLAB
(1)
(2)
(3)
(4)
(5)
(6)
syms Ax Ay Dx Dy Fh Fb
Eq(1) = Fh -0.6*Fb + Ax == 0;
Eq(2) = Ay + 0.8*Fb -400 == 0;
Eq(3) = 0.8*Fb - 3*Fh + 1400 == 0;
Eq(4) = Dx - 0.6*Fb == 0;
Eq(5) = Dy + 0.8*Fb - 400 == 0;
Eq(6) = 0.8*Fb +200 == 0;
define symbolic forces and equations
Notes: Here is the setup for the MATLAB symbolic solution. We include the ==0 in these equations but that is not necessary, as we have mentioned before.

## Slide 10
S = solve(Eq)
S =
struct with fields:
Ax: -550
Ay: 600
Dx: -150
Dy: 600
Fb: -250
Fh: 400
double([S.Ax S.Ay S.Dx S.Dy S.Fb S.Fh])
ans =
-550 600 -150 600 -250 400
Solve equations symbolically. Results are in a MATLAB structure
convert symbolic values
to numerical values
same values as before
Notes: And here is the symbolic solution, converted to double precision numerical values.

## Slide 11
550 lb
600 lb
400 lb
250 lb
4
3
400 lb
3 ft
1 ft
7/2 ft
400 lb
250 lb
4
3
150 lb
600 lb
550 lb
600 lb
400 lb
150 lb
600 lb
250 lb
4
3
4
3
250 lb
400 lb
400 lb
free body diagrams of the system and its parts:
Notes: We can take either the numerical or symbolic solution and show the results on the FBDs of the entire system and all its parts . All these parts are in equilibrium.

## Slide 12
Note that if we included the weights (and their locations – not shown) for the two supporting arms we could still solve this problem (need only 3 FBDs out of the 5 shown, with 9 equations in 9 unknowns)
Ax
Ay
FH
Bx
400 lb
3 ft
1 ft
7/2 ft
1 ft
2 ft
By
400 lb
Dx
Dy
Ex
Ey
1 ft
W1
W2
Ex
Ey
Bx
By
W2
Ax
Ay
Dx
Dy
FH
W1
FH
FH
Notes: Even if we had included the weights ( and centers of gravity) of the support arms we could solve for all the unknowns

## Slide 13
550 lb
600 lb
400 lb
150 lb
600 lb
250 lb
4
3
4
3
250 lb
400 lb
400 lb
0.5 ft
D
C
A
E
B
C
F
150 lb
600 lb
D
4
3
250 lb
E
V1
N1
M1
N2
V2
M2
C
400 lb
T
If we had looked at free body diagrams of sections where we cut through the members, not at the pins, we would expose more internal unknowns. For example:
0.5 ft
0.5 ft
Notes: You might have noticed that we cut the structure up only at the connecting pins. We did not take sections where we cut through the members as done in the method of sections for trusses. The reason is that except for a straight two force member, as usually found in trusses, there are two internal forces and an internal moment acting in a member in coplanar problems. Since that represents a total of three unknowns, and we have only three equilibrium equations for such a section, unless we know all the other forces on the FBD we will not be able to solve for these internal forces and moments. For example, if we take a section one half foot below pins D and E in members DCA and EB, as shown, we have an internal shear force, V, normal force, N, and bending moment, M, acting at those sections. For the hydraulic cylinder, of course, we just have an internal tension, T, in the cylinder acting at a sectional cut since CF is a straight two force member. Here we do know all the other forces acting on the FBDs so we can solve for these internal forces. By breaking the system at only the smooth pins we exposed at most two unknown reaction forces at each pin so that was a good choice. When we discuss equilibrium of beams, we will make such cuts to find the internal forces and moments in the beam, but for the frames and machines usually discussed in Statics problems we will stick with FBDs of sections that are cut at the pins.

## Slide 14
200 N
0.3 m
0.3 m
0.3 m
0.6 m
A
B
C
D
E
F
1.2 m
Determine all the forces acting on the frame using MATLAB. Neglect the weights of all the members.
Example 6.2
Notes: Here is a frame problem.

## Slide 15
200 N
Ax
Ay
TCD
12
3
0.3 m
0.3 m
Fx
Fy
TCD
FE
0.3 m
0.6 m
12
3
equations of equilibrium
Notes: Note that for the entire frame we have four reaction forces, so we need to break the system up. We only need two FBDs if we recognize that CD is a two-force member. Then we have a total of six equations and six unknowns.

## Slide 16
syms Ax Ay Tcd Fe Fx Fy
Eq(1) = Ax +200 +(12/sqrt(153))*Tcd == 0;
Eq(2) = Ay + (3/sqrt(153))*Tcd == 0;
Eq(3) = 0.6*(12/sqrt(153))*Tcd + 0.3*200== 0;
Eq(4) = Fx - Fe - (12/sqrt(153))*Tcd == 0;
Eq(5) = Fy -(3/sqrt(153))*Tcd == 0;
Eq(6) = 0.9*(12/sqrt(153))*Tcd + 0.6*Fe == 0;
S = solve(Eq)
S =
struct with fields:
Ax: -100
Ay: 25
Fe: 150
Fx: 50
Fy: -25
Tcd: -25*17^(1/2)
double([ S.Ax S.Ay S.Fe S.Fx S.Fy S.Tcd])
ans =
-100.0000 25.0000 150.0000 50.0000 -25.0000 -103.0776
Notes: Here is the MATLAB symbolic solution. The force in CD is negative so that member is in compression. Fy is just the negative of Ay, which is consistent with what we would see from a FBD of the entire structure.

## Slide 17
200 N
100 N
25 N
103 N
12
3
0.3 m
0.3 m
50 N
25 N
103 N
150 N
0.3 m
0.6 m
12
3
Both sections are in equilibrium:
Notes: Here are all the forces on the frame.

## Slide 18
A bolt cutter operated by hand is shown in the figure. For a force P = 100 N acting on the handle, determine the force F developed by each jaw on the rod to be cut as well as the other forces at the pins using MATLAB. All the dimensions are in mm.
20 mm
60 mm
180 mm
30 mm
P = 100 N
P = 100 N
A
B
C
D
E
Example 6.3
Notes: This is a “machine” type of problem.

## Slide 19
F
TAB
Ex
Ey
100 N
20 mm
90 mm
180 mm
F
TAB
Dx
Dy
20 mm
60 mm
F
F
by inspection Ex = 0, Dx = 0
D
syms F Tab Ey Dy
Eq(1) = F - Tab + Ey -100 == 0;
Eq(2) = 90*Tab -18000 -110*F == 0;
Eq(3) = F - Tab + Dy == 0;
Eq(4) = 60*Tab - 80*F == 0;
S = solve(Eq)
S = struct with fields: Dy: 600
Ey: 700
F: 1800
Tab: 2400
Notes: If we draw a FBD of the upper arm (the lower arm will look the same by symmetry) we see that there are too many unknowns to solve for the forces. Thus, we also draw a FBD of the cutter head. Note that AB is a two-force member. We see there are no forces acting in the x-direction except Ex and Dx so these both must be zero. We use MATLAB to find the other forces.

## Slide 20
21
9
2
17
28
6
6
14
13
13
y
z
x
A
B
C
D
E
A thin 200 lb homogeneous plate is supported by two hinges and a continuous cable, as shown. The cable runs over a smooth eyebolt at point C and is attached to the vertical wall at points D and E. The hinges are in alignment so that they only exert forces at A and B and only the hinge at B can support a force along its axis. Determine the forces at the hinges acting on the plate and the tension in the cable. All dimensions are in inches.
Example 6.4
Notes: Here is a 3-D problem. MATLAB is usually very helpful in solving such problems. Here we will show a solution done by hand and with MATLAB.

## Slide 21
The free body diagram of the plate is shown. The plate is homogeneous so that the center of gravity, G, where the weight of plate acts is at the plate center. There are six unknowns and six equations of equilibrium, so the problem is statically determinate.
First, we need to get vector expressions for the forces in the cable along CD and CE
Notes: First, we get the vector expressions for the cable forces.

## Slide 22
The total force at C is:
For equilibrium equations we are going to sum moments about B for the three moment equations and use them in conjunction with the three force equations. Thus, we need to compute moments about B, using position vectors.
Here are the moment equations
Notes: We take moments about point B. If we set those moments equal to zero we can solve directly for the tension in the cable and the reactions at A.

## Slide 23
and here are the force equations
We chose point B to take moments about since it allowed us to solve directly for the tension, T, and the reactions at A without solving any simultaneous equations. Now, we are going to solve this problem in MATLAB. We do not need to choose a “good” point to take moments about since MATLAB will solve the simultaneous equations. Thus, we will instead calculate moments about the origin O for the moment equation(s).
Notes: Here are the force equilibrium equations which we can use to solve for the reactions at B. Now, consider the MATLAB solution.

## Slide 24
MATLAB solution
syms T Ay Az Bx By Bz
W = [ 0 0 -200];
B = [ Bx By Bz];
A = [ 0 Ay Az];
define the unknowns and the vector forces
CD = [ 4 -28 19];
eCD = CD/norm(CD); % unit vector along CD
Td = T*eCD; % cable force along CD
CE = [ -13 -28 19];
eCE = CE/norm(CE); % unit vector along CE
Te = T*eCE; % cable force along CE
obtain vector cable forces
Notes: We define symbolically the unknown force components and their vectors.

## Slide 25
ra = [ -6 0 0]; % position vectors from O to A, B, C
rb = [ -20 0 0 ];
rc = [ -13 28 2];
rw = [ -13 14 0]; % position vector from O to G for the weight
use position vectors from origin O to compute moments
F = A + B + W + Td + Te;
M = cross(ra, A) + cross(rb, B) + cross(rc, Td) +cross(rc,Te) + cross(rw, W);
Eq = [ F M ]
S = solve(Eq);
double([ S.Ay S.Az S.Bx S.By S.Bz S.T])
ans = 26.3141 51.8796 20.1763 107.0192 57.6442 83.6372
Determine the net force and moment vector, put in equilibrium equations, and solve:
Notes: We define position vectors to use to calculate moments and form up the net force and moment. If we place those vectors together in a set of equilibrium equations, we can solve them directly. As done previously, we convert the results to double precision numerical values.